## Slide 1: RU Adaptation in TB UL MU Transmission
Date: 2020-11-27
Authors:
Name | Affiliation | Address | Phone | Email
Yanyi Ding | Panasonic Corporation |  |  | yanyi.ding@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2
Background
802.11be supports channel bandwidth up to 320MHz and shall allow more than one RUs to be allocated to a single STA. [1]
RUs with equal to or more than 242 tones are defined as large-size RUs. [1]
This contribution proposes a mechanism (RU adaptation procedure) for enhancement of Trigger-based UL MU transmission.

## Slide 3
TB UL MU transmission Problem
In TB UL MU transmission, if CS requirement is indicated in the Trigger frame, ED-based CCA shall be performed on 20MHz subchannels overlapping the allocated RU/MRU.
If any of the 20MHz subchannels is detected as busy, STA does not transmit EHT TB PPDU at the allocated RU/MRU.
Whole allocated large-size RU/MRU is wasted even if only a small number of 20MHz subchannels is detected as busy, which would degrade system throughput.

## Slide 4
RU Adaptation
We propose an RU Adaptation procedure to avoid such waste.
When large-size RU/MRU is allocated to a STA, the AP may indicate whether RU adaptation procedure is enabled in the User Info field to the STA.
  When the allocated RU or RU combination is not larger than 242 tones, the RU adaptation shall be disabled.

## Slide 5
RU Adaptation
When an RU adaptation procedure is indicated, STA may adapt allocated RU/MRU according to ED-based CCA results.
  Example RU adaptation
Note: there may be many other possible options of adapted RU/MRU.
In order to reduce process complexity, some restrictions should be forced to reduce the number of possible options of adapted RU/MRU for each large-size RU/MRU. (example of details in Annex slide 11)

## Slide 6
Signaling options
There are several options for the EHT TB PPDU to indicate adapted RU/MRU.
  Without explicit signaling
    Decoding may be performed based on blind decoding or signal detection of pre-EHT modulated fields in all 20MHz subchannels.
  Explicit signaling
    Adapted RU/MRU is explicitly signaled in U-SIG field of EHT TB PPDU
Only small changes needed.

## Slide 7
Conclusion
Large-size RU/MRU may be wasted in UL MU transmission when CS is required.
In this contribution, we propose the RU adaptation procedure to improve throughput of TB UL MU transmission with large-size RU/MRU.
  STA may adapt allocated RU/MRU according to ED-based CCA results.
  There may be some restrictions on associated RU/MRU to reduce process complexity.
  Only small changes are needed for AP to decode EHT TB PPDU transmitted on adapted RU/MRU.

## Slide 8
SP#1
Do you support that EHT should consider allowing non-AP STAs to adapt allocated RU/MRU for EHT TB PPDU according to ED-based CCA results?
Y/N/A:

## Slide 9
SP#2
Which option do you prefer to indicate the adapted RU/MRU in EHT TB PPDU?
  Option 1: without explicit signaling
  Option 2: with explicit
Y/N/A:

## Slide 10
Annex

## Slide 11
RU Adaptation
Define Associated RU/MRU for each large-size RU/MRU
  Associated RU/MRU is a set of possible options of adapted RU/MRU where the STA shall choose from when a large-size RU/MRU is allocated.
  Some restrictions may be enforced, for example, set a threshold for the size.
Example (the size of associated RU/MRU shall not be smaller than 50% of the size of allocated RU/MRU)
BW (MHz) | RU/MRU Larger Than 242 Tones | Associated RU/MRU
40, 80, 160/80+80, 320/160+160 | RU484 | RU484, RU242 (two options)
80, 160/80+80, 320/160+160 | RU242+RU484 | RU242+RU484, RU484
80, 160/80+80, 320/160+160 | RU996 | RU996, RU242+RU484 (4 options), RU484 (2 options)
160/80+80, 320/160+160 | RU484+RU996 | RU484+RU996, RU996, RU484+RU242 (4 options)
… | … | ...
* When part of the allocated RU/MRU which is detected as idle does not match or cover any of its associated RU/MRU, the allocated RU/MRU is not adapted.