## Slide 1: Clean UL BW Signaling in Enhanced Trigger Frame
Date: 2020-12-4
Authors:
Name | Affiliation | Address | Phone | Email
Lei Huang | OPPO |  |  | huang.lei1@oppo.com
Chaoming Luo |  |  |  | 
Pei Zhou |  |  |  | 
Aiguo Yan | Zeku |  |  | 

## Slide 2: Background
An enhanced Trigger frame can be used to solicit the following TB PPDU transmissions:
  HE TB PPDU transmission from HE STAs
  EHT TB PPDU transmission from EHT STAs
  TB A-PPDU transmission from both HE STAs and EHT STAs
Several contributions [1-3] have addressed the design of enhanced Trigger frame, including UL BW signaling.
This contribution further discusses UL BW signaling in enhanced Trigger frame.

## Slide 3: Overview of Existing UL BW Signaling Options
Besides 2-bit UL BW subfield, an additional subfield is required for UL BW signalling in enhanced Trigger frame.
  Option 1: 1-bit UL BW Extension subfield [1] or Wide UL BW Indication subfield [2]
    Pros: only a single signaling bit is required.
    Cons: not able to signal the exact BW of EHT TB PPDU in TB A-PPDU when EHT TB PPDU have different BW from HE TB PPDU.
  Option 2: 3-bit EHT UL BW subfield [2][3]
    Pros: able to signal the exact BW of EHT TB PPDU in TB A-PPDU even when EHT TB PPDU have different BW from HE TB PPDU.
    Cons: two more signaling bits are required compared to Option 1.
  Option 3: 2-bit BW Extension subfield [3]
    Pros: able to signal the exact BW of EHT TB PPDU in TB A-PPDU even when EHT TB PPDU have different BW from HE TB PPDU.
    Cons: a bit complicated and not easy to be parsed.

## Slide 4: Proposed UL BW Signaling
We propose an alternative to Option 3 using the 2-bit Delta UL BW subfield
  Given UL BW subfield value = n and the Delta UL BW subfield value = m.
  For valid combinations of n and m,
    when m =0, 1 or 2, BW index for EHT TB PPDU = n+m
    when m =3, BW index for EHT TB PPDU = n-1
UL BW subfield value (n) | Delta UL BW subfield value (m) | BW Index for EHT TB PPDU | BW of HE TB PPDU (MHz) | BW of EHT TB PPDU (MHz) | Use Case
0-3 | 0 | 0-3 | 20/40/80/160 | 20/40/80/160 | 20/40/80/160 MHz HE TB PPDU transmission, 20/40/80/160 MHz EHT TB PPDU transmission, 320 MHz TB A-PPDU transmission
2 | 1 | 3 | 80 | 160 | 320 MHz TB A-PPDU transmission with one 80 MHz channel punctured
3 | 1 | 4 | 160 | 320-1 | 320 MHz EHT TB PPDU transmission
3 | 2 | 5 | 160 | 320-2 | 320 MHz EHT TB PPDU transmission
3 | 3 | 2 | 160 | 80 | 320 MHz TB A-PPDU transmission with one 80 MHz channel punctured
Note: Other value combinations of UL BW subfield and Delta UL BW subfield are reserved due to lack of use cases.
Valid value combinations of UL BW subfield and Delta UL BW subfield and corresponding use cases

## Slide 5: Delta UL BW Subfield Encoding
UL BW subfield value (n) | Delta UL BW subfield value (m) | Description
0-3 | 0 | BW for EHT TB PPDU as indicated in the UL BW subfield
0-1 | 1 | Reserved
2 | 1 | Reserved and maybe used in future releases of amendments.
3 | 1 | 320 MHz-1 BW for EHT TB PPDU
0-2 | 2 | Reserved
3 | 2 | 320 MHz-2 BW for EHT TB PPDU
0-2 | 3 | Reserved
3 | 3 | Reserved and maybe used in future releases of amendments.
The value combinations of UL BW subfield and Delta UL BW subfield marked by red, i.e. {n = 2, m = 1} and {n = 3, m =3}, are only used for TB A-PPDU transmission.
  such value combinations shall be reserved in R1.

## Slide 6: R2 Update
According to the passed #SP368 [5], the Special User Info field of the Trigger frame includes a 2-bit PPDU Bandwidth Extension subfield, which together with UL BW subfield in common info field, indicates BW for EHT TB PPDU. However, the definition of 2-bit PPDU Bandwidth Extension subfield is TBD.
We propose the 2-bit PPDU Bandwidth Extension subfield can be defined in 11be R1 as follows:
  Note 1: BW index for EHT TB PPDU = n+m
  Note 2: the proposed definition can be easily extended for 11be R2 with A-PPDU supported
  Pros: BW for EHT TB PPDU can be determined via simple calculation, which is much easier than [4]
PPDU Bandwidth Extension subfield value (m) | UL BW subfield value (n) | BW index for EHT TB PPDU | Description
0 | 0-3 | 0-3 | BW for EHT TB PPDU as indicated in the UL BW subfield of Common Info field
1 | 0-2 | Reserved | Reserved
 | 3 | 4 | 320 MHz-1 BW for EHT TB PPDU
2 | 0-2 | Reserved | Reserved
 | 3 | 5 | 320 MHz-2 BW for EHT TB PPDU
3 | 0-3 | Reserved | Reserved

## Slide 7: Summary
We propose an alternative UL BW signalling scheme for enhanced Trigger frame
  It is able to signal the exact BW of EHT TB PPDU in TB A-PPDU even when EHT TB PPDU have different BW from HE TB PPDU.
  It is a clean design and easy to be parsed.

## Slide 8: SP 1
Do you agree to define the following 2-bit PPDU Bandwidth Extension subfield in the Special User Info field of the Trigger frame in R1?
  Note: BW index for EHT TB PPDU = n+m
PPDU Bandwidth Extension subfield value (m) | UL BW subfield value (n) | BW index for EHT TB PPDU | Description
0 | 0-3 | 0-3 | BW for EHT TB PPDU as indicated in the UL BW subfield of Common Info field
1 | 0-2 | Reserved | Reserved
 | 3 | 4 | 320 MHz-1 BW for EHT TB PPDU
2 | 0-2 | Reserved | Reserved
 | 3 | 5 | 320 MHz-2 BW for EHT TB PPDU
3 | 0-3 | Reserved | Reserved

## Slide 9: Reference
11-20-1429-02-00be-enhanced-trigger-frame-for-eht-support
11-20-1911-00-00be-ul-bw-subfield-design-in-trigger-frame.
11-20-1808-01-00be-backward-compatible-eht-trigger-frame-follow-up
11-20-1808-04-00be-backward-compatible-eht-trigger-frame-follow-up
11-20-1935-06-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2