## Slide 1: 11be Spectral Flatness Requirements
Date: 2020-12-10
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Youhan Kim |  |  |  | 
Bin Tian |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
In this presentation we will talk about the spectral flatness requirements for 11be transmissions, which is much complicated than legacy due to different tone plans in DUP mode and puncturing transmissions
We first look at the requirements for full BW non-OFDMA transmissions, then extend to DUP and puncturing cases

## Slide 3: High Level Thoughts on EHT Spectral Flatness Requirements
For full BW non-OFDMA transmission, propose to have same maximum deviation requirement as 11ax
  +/-4dB for inner subcarriers (i.e. averaging subcarriers in spec)
  +4/-6dB for edge subcarriers
Propose to have same spectral flatness requirements as 11ax for the full BW non-OFDMA 20/40/80MHz
Since 11be removes 80+80MHz mode, we need to update the requirement for 160MHz mode
  The 11ac/11ax spectral flatness assumed 80+80 thus the relaxed flatness at the middle of 160

## Slide 4: Discussion on Flatness Requirements for EHT DUP, Puncturing, and OFDMA Cases
11be supports many puncturing cases, each with different populated tones and punctured edges
To simplify the spec writing on the definition of averaging subcarrier indices and tested subcarrier indices while covering so many cases, we can relax the maximum deviation requirement to be +4/-6dB for all populated subcarriers for puncturing case
  Flatness requirement is specified to limit some weird transmission and is not very helpful to performance
  Good for EHT80 and above with puncturing
For EHT DUP, Puncturing, and OFDMA Cases, power averaging and testing are only on the populated subcarriers
  Same as 11ax

## Slide 5: Spectral Flatness Requirements for EHT modes (1)
Full BW Non-OFDMA case
  For 160MHz, change the used tones around DC to be inner subcarrier
  For 320MHz, calculate the tone indices for averaging based on 320MHz tone plan and the existing table
    The populated 4x tone indices belong to [-2036:-1539, -1533:-1036, -1012:-515, -509:-12, 12:509, 515:1012, 1036:1533, 1539:2036]
      Outer most INNER subcarrier = floor(696*2036/1012)=1400
      Inner most INNER subcarrier = 1st used tone by DC
    Remove sub-DCs and guard tones
For puncturing cases
  Use the same table with relaxed allowed max deviation specified separately and consider only the populated subcarriers in the averaging subcarrier indices and tested subcarrier indices
EHT DUP and OFDMA Cases
  Power averaging and testing only on the populated subcarriers
  Used RUs only to be considered

## Slide 6: Spectral Flatness Requirements for EHT modes (2)
Maximum transmit spectral flatness deviations |  |  |  | 
Bandwidth of EHT transmission (MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum deviation (dB) (Full BW Non-OFDMA) | Maximum deviation (dB) (punctured cases)
20 | –84 to –2 and +2 to +84 | –84 to –2 and +2 to +84 | ±4 | N/A
 |  | –122 to –85 and +85 to +122 | +4/–6 | 
40 | –168 to –3 and +3 to +168 | –168 to –3 and +3 to +168 | ±4 | 
 |  | –244 to –169 and +169 to +244 | +4/–6 | 
80 | –344 to –3 and +3 to +344 | –344 to –3 and +3 to +344 | ±4 | +4/–6
 |  | –500 to –345 and +345 to +500 | +4/–6 | +4/–6
160 | –696 to –515, –509 to -12, –166, +166 +12 to +509, and +515 to +696 | –696 to –515, –509 -12, –166, +166 +12 to +509, and +515 to +696 | ±4 | +4/–6
 |  | –1012 to –697 , –165 to –12, +12 to +165, and +697 to +1012 | +4/–6 | +4/–6
320 | -1400 to -1036, -1012 to -515, -509 to -12, +12 to +509, +515 to +1012, and +1036 to +1400 | -1400 to -1036, -1012 to -515, -509 to -12, +12 to +509, +515 to +1012, and +1036 to +1400 | ±4 | +4/–6
 |  | -2036 to -1539, -1533 to -1401, +1401 to +1533, and +1539 to +2036 | +4/–6 | +4/–6

## Slide 7: Flatness Requirements for Non-HT DUP over Up to 320MHz
For the full BW case, the populated 1x tone indices belong to [-506, +506] - 20MHz sub-DCs and guard tones
  Outer most INNER subcarrier = floor(172*506/250)=348
  Inner most INNER subcarrier = shift the outer most INNER subcarrier for 160MHz by 256 tones = 256-172 = 84
  Remove 20MHz sub-DCs and guard tones
For punctured case, use the same table with relaxed allowed max deviation specified separately and consider only the populated subcarriers in the averaging subcarrier indices and tested subcarrier indices
Maximum transmit spectral flatness deviations |  |  |  |  | 
Non-HT duplicate | Bandwidth of transmission (MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum deviation (dB) (Full BW) | Maximum deviation (dB) (Punctured)
 | 40 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | ±4 | N/A
 |  |  | -58 to -43 and +43 to +58 | +4/-6 | 
 | 80 | -84 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | -84 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | ±4 | +4/-6
 |  |  | -122 to -97, -95 to -85 and +85 to 95, +97 to +122 | +4/-6 | +4/-6
 | 160 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | ±4 | +4/-6
 |  |  | -250 to -225, -223 to -198, -186 to -173, -43 to -33, -31 to -6, +6 to +31, +33 to +43, +173 to +186, +198 to +223, +225 to +250 | +4/-6 | +4/-6
 | 320 | -348 to -326, -314 to -300, -212 to -198, -186 to -161, -159 to -134, -122 to -97, -95 to -84, +84 to +95, +97 to +122, +134 to +159, +161 to +186, +198 to +212, +300 to +314, +326 to +348 | -348 to -326, -314 to -300, -212 to -198, -186 to -161, -159 to -134, -122 to -97, -95 to -84, +84 to +95, +97 to +122, +134 to +159, +161 to +186, +198 to +212, +300 to +314, +326 to +348 | ±4 | +4/-6
 |  |  | -506 to -481, -479 to -454, -442 to -417, -415 to -390, -378 to -353, -351 to -349, -299 to -289, -287 to -262, -250 to -225, -223 to -213, -83 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to+58, +70 to +83, +213 to +223, +225 to +250, +262 to +287, +289 to +299, +349 to +351, +353 to +378, +390 to +415, +417 to +442, +454 to +479, +481 to +506 | +4/-6 | +4/-6

## Slide 8: SP #1
Do you support the following for 11be spectral flatness maximum deviation requirement
For non-puncturing case, same as 11ax
  +4/-4dB for inner tones, +4/-6dB for edge tones
For puncturing case, +4/-6dB for all populated tones
Y
N
A

## Slide 9: SP #2
Maximum transmit spectral flatness deviations |  |  |  | 
Bandwidth of EHT transmission (MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum deviation (dB) (Full BW Non-OFDMA) | Maximum deviation (dB) (punctured cases)
20 | –84 to –2 and +2 to +84 | –84 to –2 and +2 to +84 | ±4 | N/A
 |  | –122 to –85 and +85 to +122 | +4/–6 | 
40 | –168 to –3 and +3 to +168 | –168 to –3 and +3 to +168 | ±4 | 
 |  | –244 to –169 and +169 to +244 | +4/–6 | 
80 | –344 to –3 and +3 to +344 | –344 to –3 and +3 to +344 | ±4 | +4/–6
 |  | –500 to –345 and +345 to +500 | +4/–6 | +4/–6
160 | –696 to –515, –509 to -12, –166, +166 +12 to +509, and +515 to +696 | –696 to –515, –509 -12, –166, +166 +12 to +509, and +515 to +696 | ±4 | +4/–6
 |  | –1012 to –697 , –165 to –12, +12 to +165, and +697 to +1012 | +4/–6 | +4/–6
320 | -1400 to -1036, -1012 to -515, -509 to -12, +12 to +509, +515 to +1012, and +1036 to +1400 | -1400 to -1036, -1012 to -515, -509 to -12, +12 to +509, +515 to +1012, and +1036 to +1400 | ±4 | +4/–6
 |  | -2036 to -1539, -1533 to -1401, +1401 to +1533, and +1539 to +2036 | +4/–6 | +4/–6
Do you support the 11be spectral flatness requirements for EHT modes as defined in the following table?
Y
N
A

## Slide 10: SP #3
Do you support the non-HT DUP spectral flatness requirements as defined in the following table?
Y
N
A
Maximum transmit spectral flatness deviations |  |  |  |  | 
Non-HT duplicate | Bandwidth of transmission (MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum deviation (dB) (Full BW) | Maximum deviation (dB) (Punctured)
 | 40 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | -42 to -33, -31 to -6, +6 to +31, and +33 to +42 | ±4 | N/A
 |  |  | -58 to -43 and +43 to +58 | +4/-6 | 
 | 80 | -84 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | -84 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to +58, +70 to +84 | ±4 | +4/-6
 |  |  | -122 to -97, -95 to -85 and +85 to 95, +97 to +122 | +4/-6 | +4/-6
 | 160 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | -172 to -161, -159 to -134, -122 to -97, -95 to -70, -58 to -44, +44 to +58, +70 to +95, +97 to +122, +134 to +159, +161 to +172 | ±4 | +4/-6
 |  |  | -250 to -225, -223 to -198, -186 to -173, -43 to -33, -31 to -6, +6 to +31, +33 to +43, +173 to +186, +198 to +223, +225 to +250 | +4/-6 | +4/-6
 | 320 | -348 to -326, -314 to -300, -212 to -198, -186 to -161, -159 to -134, -122 to -97, -95 to -84, +84 to +95, +97 to +122, +134 to +159, +161 to +186, +198 to +212, +300 to +314, +326 to +348 | -348 to -326, -314 to -300, -212 to -198, -186 to -161, -159 to -134, -122 to -97, -95 to -84, +84 to +95, +97 to +122, +134 to +159, +161 to +186, +198 to +212, +300 to +314, +326 to +348 | ±4 | +4/-6
 |  |  | -506 to -481, -479 to -454, -442 to -417, -415 to -390, -378 to -353, -351 to -349, -299 to -289, -287 to -262, -250 to -225, -223 to -213, -83 to -70, -58 to -33, -31 to -6, +6 to +31, +33 to+58, +70 to +83, +213 to +223, +225 to +250, +262 to +287, +289 to +299, +349 to +351, +353 to +378, +390 to +415, +417 to +442, +454 to +479, +481 to +506 | +4/-6 | +4/-6