## Slide 1: Ranging PHY Security
Date: Dec 16, 2020
Authors:

## Slide 2
Feedback Protected PHY Security

## Slide 3: Detection of PHY attacks
We have repetition of LTFs to enable attack on encrypted LTFs.
  Relies on the peer modem to detect the attack
Consider channel metric feedback to detect PHY attacks
  Utilize reciprocity of channel
  Feed back a metric of the channel estimate
    Whole channel estimate, or e.g.
    Average delay in the channel, i.e. the PS-TOA
  Enables the originating modem to detect the attack

## Slide 4: Attack Scenario
Unlikely that the channels are the same

## Slide 5: PS-TOA Feedback PHY Attack Detection
RSTA
ISTA
Measure t2 and tp2
Measure t4 and tp4
Feedback t2 and tp2
Feedback t4 and tp4
Compare tp2-t2 with tp4-t4!
I2R NDP
R2I NDP
Compare tp2-t2 with tp4-t4!
Forces attacker to attack both links or shift the entire channel estimate.
Probably hard to do without triggering detection of the attack!
Can be combined with LTF encryption!

## Slide 6
Combination with LTF encryption

## Slide 7: PHY attacks when the LTFs are encrypted
When the LTFs are encrypted, attacks may not be possible with perfect LTF replica
  Possibly only some of the tones are estimated correctly
  The attack may only be partial in the time domain
Causes unintended distortions of the channel raising the probability of detection

## Slide 8
Proposed draft changes

## Slide 9: Proposed Draft Changes
Category
CFO Parameter
Octets
Public Action
Octets
Dialog Token
TOD
TOA
TOD Error
TOA Error
R2I NDP Tx Power
I2R NDP Target RSSI
AOA Feedback
(Optional)
Secure LTF Parameters
(Optional)
PSTOA
(Optional)
PSTOA Error
(Optional)
1
1
6
6
6
1
1
2
1
1
13
9
6
1
Add PS-TOA feedback in PHY secure mode as additional protection against attacks!
LMR frame:

## Slide 10
Combination with Ranging Authentication Payload

## Slide 11: Ranging Authentication Message
RSTA
ISTA
Authenticate M1
Feed back M1
Feed back M2
M1
M2
Ranging authentication messages in ranging frames
Keeping TOA minus PS-TOA consistent makes it harder to attack the LTF and allow correct demodulation of the ranging authentication messages!
Authenticate that M2
Authenticate that M1
Authenticate M2

## Slide 12: Vehicle and Modulation for Ranging Authentication Message
Vehicle
  NDP PE
  Replace NDP with regular PPDU
Modulation
  Need LTF sounding all Tx antennas
  Need to use STBC or MIMO
Feasible?

## Slide 13: Straw Poll
Do you support adding PS-TOA feedback, along with the TOA feedback, in the PHY secure mode?
Y/N/A:

## Slide 14
Thank You!