## Slide 1: Considerations on Open Issues PHY requirements
Date: 2021-01-04
Authors:

## Slide 2: Introduction
In this contribution, we discussed open issues in PHY requirements such as
  LO requirement for 320 MHz transmission
  EVM requirement for 1024 QAM and BPSK-DCM-DUP requirement
  Minimum sensitivity for 4K QAM and BPSK-DCM-DUP
  Channel rejection level for 4K QAM and BPSK-DCM-DUP

## Slide 3: LO requirement for 320 MHz transmission
For 20/40/80/160 MHz transmission, the power measured at the location of the RF LO using resolution BW 78.125 kHz shall not exceed the maximum of –32 dB relative to the total transmit power and –20 dBm, or equivalently max(P-32,-20), where P is the transmit power per antenna in dBm.
In case of 320 MHz, NST = 3984, and thus each subcarrier may have PSD of (P-36).
Proposal: For 320 MHz transmission, the power measured at the location of the RF LO using resolution BW 78.125 kHz shall not exceed the maximum of -36 dB relative to the total transmit power and -20 dBm, or equivalently max(P-36,-20).

## Slide 4: EVM requirement (1/2)
In 11ax, there are two EVM requirements for 1024 QAM.
Device may meet either
  -35 dB with amplitude drift compensation disabled
  -35 dB with amplitude drift compensation enabled and -32 dB with amplitude drift compensation disabled
In 11be, there is a single EVM requirement for other than 1024 QAM. EVM requirement for 1024 QAM is TBD.
For simplicity, we propose to have a single EVM requirement for 1024 QAM as well.
We may not need to mention whether amplitude drift compensation is enabled or not.
Proposal: Set -35 dB as an EVM requirement for 1024 QAM

## Slide 5: EVM requirement (2/2)
In 11be (and 11ax), EVM requirements for BPSK and BPSK-DCM are same.
Currently EVM requirement for BPSK-DCM-DUP is missing.
Note that BPSK-DCM-DUP is only applicable for SU transmission, i.e. EHT MU PPDU.
Proposal: Set -5 dB as an EVM requirement for BPSK-DCM-DUP in an EHT MU PPDU. N/A in EHT TB PPDU.

## Slide 6: Minimum sensitivity
In 11be D0.2, minimum sensitivities for 4K QAM and BPSK-DCM-DUP are not defined.
10% required SNR for 4K QAM ¾ is about 2.8 dB from 1024 QAM 5/6
10% required SNR for 4K QAM 5/6 is about 5.3 dB from 1024 QAM 5/6
BPSK-DCM-DUP minimum sensitivity can be set to that of half bandwidth of BPSK-DCM
Proposal:
Modulation | Rate | 20 MHz | 40 MHz | 80 MHz | 160 MHz | 320 MHz
4096-QAM | 3/4 | –49 | –46 | –43 | –40 | –37
4096-QAM | 5/6 | –46 | –43 | –40 | –37 | –34
BPSK-DCM | 1/2 | –82 | –79 | –76 | –73 | –70
BPSK-DCM-DUP | 1/2 | N/A | N/A | –78 | –75 | –72

## Slide 7: Channel Rejection Level
Similarly, we propose 3 dB and 6 dB lower requirement for 4K QAM ¾ and 5/6 from 1K QAM 5/6 requirement for channel rejection level.
Also, we propose to use same nonadjacent channel rejection level for BPSK-DCM-DUP and BPSK-DCM as BPSK-DCM uses that of BPSK.
Proposal:
Modulation | Rate | Adjacent channel rejection (dB) | Nonadjacent channel rejection (dB)
4096-QAM | 3/4 | –17 | –1
4096-QAM | 5/6 | –20 | –4
BPSK-DCM | 1/2 | 16 | 32
BPSK-DCM-DUP | 1/2 | 16 | 32

## Slide 8: SP #1
Do you support
  For 320 MHz transmission, the power measured at the location of the RF LO using resolution BW 78.125 kHz shall not exceed the maximum of -32 dB relative to the total transmit power and -20 dBm, or equivalently max(P-32,-20).
  Y
  N
  A

## Slide 9: SP #2
Do you support a single EVM requirement for 1024 QAM?
  An EVM requirement for 1024 QAM: -35 dB
  Y
  N
  A

## Slide 10: SP #3
Do you support the same EVM requirement for BPSK, BPSK-DCM and BPSK-DCM-DUP in EHT MU PPDU?
  An EVM requirement for BPSK-DCM-DUP in EHT MU PPDU: -5 dB
  An EVM requirement for BPSK-DCM-DUP in EHT TB PPDU: N/A
  Y
  N
  A

## Slide 11: SP #4
Do you support following minimum sensitivity levels for 4K QAM and BPSK-DCM-DUP?
  Y
  N
  A
Modulation | Rate | 20 MHz | 40 MHz | 80 MHz | 160 MHz | 320 MHz
4096-QAM | 3/4 | –49 | –46 | –43 | –40 | –37
4096-QAM | 5/6 | –46 | –43 | –40 | –37 | –34
BPSK-DCM | 1/2 | –82 | –79 | –76 | –73 | –70
BPSK-DCM-DUP | 1/2 | N/A | N/A | –78 | –75 | –72

## Slide 12: SP #5
Do you support following channel rejection levels for 4K QAM and BPSK-DCM-DUP?
  Y
  N
  A
Modulation | Rate | Adjacent channel rejection (dB) | Nonadjacent channel rejection (dB)
4096-QAM | 3/4 | –17 | –1
4096-QAM | 5/6 | –20 | –4
BPSK-DCM | 1/2 | 16 | 32
BPSK-DCM-DUP | 1/2 | 16 | 32