## Slide 1: Group Addressed Data Frame Delivery Methods for MLO
Date: 2021-1-19
Authors:
Name | Affiliations | Address | Phone | Email
Qi Wang Yong Liu Jarkko Kneckt Jinjing Jiang Tianyu Wu SK Yong | Apple Inc. |  |  | qi_wang2@apple.com
Matthew Fischer | Broadcom |  |  | matthew.fischer@broadcom.com
Srinivas Kandala Sharan Naribole | Samsung |  |  | srini.k1@samsung.com n.sharan@samsung.com

## Slide 2: Overview
Per 11be SFD [1], group addressed data frames (GADFs) are transmitted independently over multiple links of MLD, and a non-AP MLD needs to select one link to receive GADFs.
As a result, a non-AP MLD can receive undetectable duplicated GADFs when switching link for GADF reception.
We propose group addressed data frame delivery methods to enable duplicate detection .
We also propose to use a single GTK, PN space per security domain for group addressed data frame delivery for MLO.

## Slide 3: SNS 1 defined in 802.11 (Pre-11be)
SNS1 is used by:
-- Groupcast data (QoS, non-QoS);
-- Groupcast management frames.
-- Unicast data (Non-QoS);
-- Unicast management frames.

## Slide 4: Problem of Undetected Duplicates
A GADF is transmitted independently on all links, with its SN assigned by the per link SNS1 independently.
When a STA switches link for GADF reception, it might receive undetectable duplicated GADFs.
STAs may need to switch link at any time. Selective timing for link switch to avoid undetected duplicates, as proposed in [2], is not workable (See slide 5, 6).
AP1
SNS1_1
AP2
SNS1_2
AP3
SNS1_3
GC-Data frame
STA1
STA2
STA3
Link 1
Link 2
Link 3
GC-Data frame (SN = n1)
GC-Data frame (SN = n2)
Undetected duplicate with link switch
(false negative)

## Slide 5: Significant Limitation On Link Switch (1)
Link 1
Intended link switch time
Actual link switch time
Link 2
DTIM Indication
G-BU_link 1 = 0
G-BU_link 2 = 0
DTIM Indication
G-BU_link 1
G-BU_link 2 = 0
DTIM Indication
G-BU_link 1 = 0
G-BU_link 2 = 1
Wait time for link switch
Case 1: With NO incoming GADFs between DTIM Beacon 1 and DTIM Beacon 2
DTIM Indication
G-BU_link 1= 1
G-BU_link 2 =1
DTIM
Beacon 1
DTIM
Beacon 2
Condition for link switch to avoid duplicates
Wait time for link switch can be one DTIM Beacon Interval

## Slide 6: Significant Limitation On Link Switch (2)
Link 1
Intended link switch time
Link 2
DTIM Indication
G-BU_link 1 = 1
G-BU_link 2 = 1
DTIM Indication
G-BU_link 1 = 1
G-BU_link 2 = 1
DTIM Indication
G-BU_link 1 = 1
G-BU_link 2 = 1
Wait time for link switch
Wait time for link switch can be indefinite!
Case 2: With incoming GADFs
DTIM Indication
G-BU_link 1= 1
G-BU_link 2 =1
DTIM
Beacon 1
DTIM
Beacon 2
DTIM Indication
G-BU_link 1 = 1
G-BU_link 2 = 1
DTIM
Beacon 3
GADFs
GADFs
GADFs
GADFs
GADFs
GADFs
DTIM Indication
G-BU_link 1 = 1
G-BU_link 2 = 1
GADFs
GADFs

## Slide 7: Proposal: New SNS Design
Create a new SNS that is shared across all links, SNS_new_shared, used by:
  Groupcast data frames
  Groupcast management frames (ML) (i.e., generated at the ML level)
  Unicast management frames (ML)
Note: SNS_new_shared may have multiplicity distinguished by Address 1, TID, frame type, etc.
AP1
SNS1_1:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt (Local)
AP MLD
SNS_new_shared:
GC-data, GC-Mgmt (ML), UC-Mgmt (ML)
STA1
STA2
STA3
Link 1
Link 2
Link 3
AP2
SNS1_2:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt
(Local)
AP3
SNS1_3:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt
(Local)
The existing per link SNS1 remains to be used by:
  Unicast data (non-QoS)
  Unicast management frames (local) (i.e., generated at the local AP level)
  Groupcast management frames (local) (i.e., generated at the local AP level)

## Slide 8: Proposal: New SNS Design – Receiver Behavior
A non-AP MLDs uses <address 1= group address, sequence number (SN) > for duplicate GADF detection.
  At least the most recent cache entry needs to be maintained at the MLD level.
STA1
STA2
STA3
Link 1
Link 2
Non-AP MLD
Link 3
Rx cache with one entry
GADFs
GADFs
GADFs
Rx discards any GADFs with SN <= the cache entry to avoid duplicates.
STA1
STA2
STA3
Link 1
Link 2
Non-AP MLD
Link 3
Rx cache with N entries
GADFs
GADFs
GADFs
Rx (a) discards any GADFs with SN <= cache entries to avoid duplicates, (b) fill in the hole(s), if any, by reception on other link to improve reliability, where N is implementation specific.
Mandatory/minimal requirement
(Sufficient for duplicate detection)
Optional implementation-specific behavior
(Improvement on GADF reliability)

## Slide 9: Proposal: Single GTK and PN Space for GADF Delivery for MLO
11be SFD:
Proposal (unified unicast and groupcast approach):

## Slide 10: A Single GTK Per Security Domain Introduces No New Security Risks
AP1
AP2
AP3
AP MLD
STA1
STA2
STA3
Link 1
Link 2
Link 3
Guest # 2: Non-AP MLD
SSID1 = Home
SSID2 = Guest
GTK_SSID2
_link1
GTK_SSID2_link2 = GTK_SSID2_link1?
GTK_SSID2_link3 = GTK_SSID2_link1?
Guest # 1: Single-link legacy
GTK_SSID2
_link1
Guest #1 and Guest #2 are equally trusted by the host of SSID2.
Guest #2 obtains GTK_SSID2_link2 and GTK_SSID2_link3 from AP1, and can attack on link 2 and link 3.
Making GTK_SSID2_link1 = GTK_SSID2_link2 = GTK_SSID2_link3 introduces no new security risks.

## Slide 11: GTK Update and Group Cipher Considerations
GTK update:
  The handling of the GTK update frame (unicast) needs to occur at the MLD level because a non-AP MLD can be in power save doze state on some links.
    That is: GTK_link1 can be updated on link 2
  As a result, it’s natural to generate GTK at the MLD level.
Group cipher:
  The single/common GTK approach leads to the use of the same group cipher on all links.
  GADFs are duplicated on all links, using link-specific group cipher does not keep the data secret on each link.
  As a result, link-specific group cipher is not needed.

## Slide 12: Benefits of Single GTK and PN Space for GADF Delivery for MLO (1)
Duplicate detection
Decryption
Replay detection
(PN check)
Unicast frames
Duplicate detection
Decryption
Replay detection
(PN check)
Groupcast data frames
Reception over a single link:
  Duplicate detection for unicast frames occurs before decryption/replay detection (note: no duplicate issue for groupcast frames).
Reception over multiple links:
  It is desirable to maintain the same processing order (i.e., duplicate detection occurs before decryption/replay detection) for groupcast frames.
MLD level across all links,
enabled by new_shared_SNS
Desirable to have at the MLD level after duplicate detection

## Slide 13: Benefits of Single GTK and PN Space for GADF Delivery for MLO (2)
Currently adopted methods for unicast frame delivery for MLO:
  A single PTK and PN check at the MLD level for all links.
  Duplicate detection occurs before decryption/replay detection.
  Replacement of relevant and required link level address with relevant MLD MAC address during AAD construction. Use of relevant MLD MAC address as A2 for Nonce construction. (See [3])
  Block Ack agreement is established at the MLD level.
    MLD level Block Ack agreement should be applied to GCR-BA for MLO as well.
Using a single GTK and PN check on all links unifies the design for unicast and groupcast data frame delivery for MLO!

## Slide 14: Summary
The group addressed data frame delivery method described in 11be SFD can cause undetected duplicates at non-AP MLDs.
We have proposed to use a new shared SNS to enable duplicate detection of group addressed data frames by non-AP STAs while ensuring non-AP MLD’s flexibility to switch link.
We have also proposed to use a single and common GTK, PN space per security domain for group addressed data frame delivery on all links.

## Slide 15: Reference
[1] IEEE 802.11-19/1262r22, “Specification framework for 11be”, Edward Au, Huawei
[2] IEEE 802.11-20/0903r10, “Multi-link group addressed data frame delivery follow up”, Po-Kai Huang, et al., Intel
[3] IEEE 802.11-20/1545r1, “MLD security considerations”, G. Patwardhan, et al.

## Slide 16: SP1
Do you support to use a common SNS shared across all links of MLD for the transmission of group addressed data frames?

## Slide 17: SP2
Do you support to use a common SNS shared across all links of MLD for the transmission of:
  Unicast management frames (ML) (i.e., generated at the ML level)
  Group addressed management frames generated at the MLD level
  Optionally, unicast management frames (Local) (i.e., generated at the local AP level) whose recipients are a STA affiliated with a non-AP MLD

## Slide 18: SP3
Do you support to use a single and common GTK and PN space per security domain for group addressed data frame delivery on all links of a MLD?

## Slide 19: Appendix

## Slide 20: Problem with Using SNS_new_shared
SNS_new_shared can create false positive duplicate declaration by legacy STAs.
A corner case? Should this be addressed by the spec?
  Note: missing frames already occurs in single-link baseline.
Alternatively, we propose the method shown on next slide as a solution.
  See slide 19.
AP1
SNS1_1:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt (Local)
AP MLD
SNS_new_shared:
GC-data, GC-Mgmt (ML), UC-Mgmt (ML)
Legacy STA
STA2
STA3
Link 1
Link 2
Link 3
AP2
SNS1_2:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt (Local)
AP3
SNS1_3:
UC-data (non-QoS)
UC-Mgmt (Local)
GC-Mgmt (Local)
GC-Data frame (SN = n1)
Failed
UC-Mgmt frame (SN = n1)
Retransmitted
UC-Mgmt frame (SN = n1)
Incorrectly declared duplicate
(false positive)

## Slide 21: Solution to False Positive Problem at Legacy STAs
Transmit an additional copy of GADFs with MLD Address as TA and BSSID.
 | Link(s) transmitted | Encryption Key | SNS_new_shared
GADF with TA = BSSID= MLD_address | All links | GTK-ML | A single SNS shared across all links for the GCF
GADF with TA = BSSID= AP_i_address | Link_i | GTK_i or GTK-ML | Transmission on link_i uses its own SNS1_link_i, as defined in the 802.11 base spec.
 | Legacy_STA | MLD_STA
GADF with TA = BSSID = MLD_address | Discard | Receive and perform duplicate detection using SN
GADF with TA = BSSID = AP_i_address | Receive | Discard
Transmission:
Reception: