## Slide 1: EHT-LTF Related Signaling in Enhanced Trigger Frame
Date: 2021-01-08
Authors:
Name | Affiliation | Address | Phone | Email
Lei Huang | OPPO |  |  | huang.lei1@oppo.com
Chaoming Luo |  |  |  | 
Pei Zhou |  |  |  | 
Aiguo Yan | Zeku |  |  | 

## Slide 2: Background
An enhanced Trigger frame can be used to solicit HE TB PPDU transmission, EHT TB PPDU transmission or TB A-PPDU transmission.
Several contributions [1-3] have addressed the design of enhanced Trigger frame.
According to the existing designs, when the enhanced Trigger frame is used to solicit TB A-PPDU transmission, number of EHT-LTF symbols in EHT TB PPDU is assumed to be the same as number of HE-LTF symbols in HE TB PPDU, which may pose unnecessary limitation on scheduling flexibility of TB A-PPDU.

## Slide 3: Discussion
Number of HE-LTF symbols and number of EHT-LTF symbols in a TB A-PPDU can be different if 4x HE-LTF and 4x EHT-LTF are used.
  Frequency domain orthogonality can be kept symbol-by-symbol.
Therefore, it may be unnecessary to make number of EHT-LTF symbols equal to number of HE-LTF symbols in a TB-A-PPDU.
In addition, it is desirable for an EHT STA to process a received enhanced Trigger frame used to solicit EHT TB PPDU or TB A-PPDU transmission in a similar manner.

## Slide 4: Signaling Support
In order to support different number of HE-LTF and EHT-LTF symbols in a TB A-PPDU, we propose to add a 3-bit new subfield (e.g. Number Of EHT-LTF Symbols subfield) into the common info field to indicate number of EHT-LTF symbols in EHT TB PPDU.
    The new subfield may use 3 reserved bits of UL HE-SIG-A2 Reserved subfield.

## Slide 5: Signaling Support (cont.)
Number of EHT-LTF Symbols subfield can be defined below in R1
Number of EHT-LTF Symbols subfield value | Number of EHT-LTF Symbols
0 | 1
1 | 2
2 | 4
3 | 6
4 | 8
5 | 12
6 | 16
7 | Reserved

## Slide 6: Summary
We propose to add a 3-bit new subfield into common info field of enhanced Trigger frame to indicate the number of EHT-LTF symbols in EHT TB PPDU in R1.

## Slide 7: SP 1
Do you agree number of EHT-LTF symbols and number of HE-LTF symbols in a TB A-PPDU may be different?

## Slide 8: SP 2
Do you agree to add a 3-bit Number Of EHT-LTF Symbols subfield into common info field of enhanced Trigger frame to indicate the number of EHT-LTF symbols in EHT TB PPDU in R1?

## Slide 9: SP 3
Do you agree to define the 3-bit Number Of EHT-LTF Symbols subfield as below in R1?
Number of EHT-LTF Symbols subfield value | Number of EHT-LTF Symbols
0 | 1
1 | 2
2 | 4
3 | 6
4 | 8
5 | 12
6 | 16
7 | Reserved

## Slide 10: Reference
11-20-1429-04-00be-enhanced-trigger-frame-for-eht-support
11-20-1808-04-00be-backward-compatible-eht-trigger-frame-follow-up
11-20-1927-01-00be-clean UL BW signaling in enhanced trigger frame