## Slide 1: Spatial Reuse Fields in EHT Preamble
Date: 2021-01-08
Authors:
Name | Affiliations | Address | Phone | Email
Alice Chen | Qualcomm |  |  | alicel@qti.qualcomm.com
Sameer Vermani |  |  |  | svermani@qti.qualcomm.com
Bin Tian |  |  |  | btian@qti.qualcomm.com
Youhan Kim |  |  |  | youhank@qti.qualcomm.com
Notes: September 2012

## Slide 2: Introduction
In this presentation, we discuss the spatial reuse fields in EHT preamble
  These are for R1

## Slide 3: Spatial Reuse Field in EHT MU PPDU
Based on one passed motion in 20/1238r7, there is 1 spatial reuse (SR) field (of 4 bits) in the EHT-SIG of EHT MU PPDU
Propose to reuse the 11ax encoding table for the SR field in HE SU/MU PPDU for the SR field in the EHT-SIG of EHT MU PPDU

## Slide 4: Spatial Reuse Fields in EHT TB PPDU
Based on one passed SP in 20/1429r4, 2 spatial reuse (SR) fields (4 bits each) are carried in the Special User Info Field of the enhanced Trigger Frame
  These 2 SR fields have spatial reuse information for bystanders to be carried in the TB PPDU
We propose to use two SR fields (4 bits each, total 8 bits), with granularity of half PPDU BW, but no smaller than 20MHz
  This was our proposal in 20/1546r0
Propose to reuse the 11ax encoding table for the SR fields in HE TB PPDU for the SR field in the U-SIG of EHT TB PPDU

## Slide 5: SR Field Encoding Table in HE TB PPDU

## Slide 6: SP 1
Do you support to reuse the 11ax encoding table for the SR field in HE SU/MU PPDU for the SR field in the EHT-SIG of EHT MU PPDU?
Y/N/A

## Slide 7: SP 2
Do you support to have two SR fields (4 bits each, total 8 bits), with granularity of half PPDU BW, but no smaller than 20MHz, in the U-SIG of TB PPDU?
Y/N/A

## Slide 8: SP 3
Do you support to reuse the 11ax encoding table for the SR fields in HE TB PPDU for the SR field in the U-SIG of EHT TB PPDU?
Y/N/A