## Slide 1: PHY-related agreements for SST
Date: 01/21/2021
Authors:

## Slide 2: Introduction
802.11ax defines SST, which allows 80 MHz operating STAs to participate in 160 MHz OFDMA, even in non-primary 80 MHz
It’s expected that SST will be defined for 802.11be, with possible enhancements (320 MHz, …)
SST mode of operation requires both PHY and MAC elements to be specified
Purpose of this submission is to highlight some PHY-related agreements that will impact the definition of SST

## Slide 3: Relevant agreements reached in PHY ad-hoc
80 MHz operating STAs are required to support participation in 160 MHz and 320 MHz OFDMA
  80 MHz could be primary or non-primary 80 MHz
Support for operation in non-primary 80 MHz is expected
  Full extent TBD
  RU allocation to 80 MHz operating STAs could be outside the primary 80 MHz
STA is not required to process more than one 80 MHz segment for preamble decoding
  Specifically, no 80 MHz segment change is needed while processing L-SIG, U-SIG and EHT-SIG

## Slide 4: Issue: preamble processing in non-primary 80 MHz (with possible puncturing)
For an 80 MHz operating STA in a secondary 80 MHz, there is no guaranteed 20 MHz channel to decode U-SIG and learn about possible puncturing in the 80 MHz channel
  By contrast, in primary 80 MHz, the primary 20 MHz is always present
  Could mean different processing in primary 80 MHz vs. secondary 80 MHz
    Especially with puncturing, this adds processing complexity
  Reminder: STA is not expected to process more than its 80 MHz channel

## Slide 5: Possible scenarios for non-primary 80 preamble processing
How does the 80 MHz operating STA deal with puncturing in its (non-primary) 80 MHz channel?
  Option 1: STA autonomously finds a 20 MHz channel that is not punctured, without explicit information
  Option 2: Disallow puncturing in non-primary 80 MHz of wider band OFDMA transmission that includes 80 MHz-operating STAs in the non-primary 80 MHz
  Option 3: Provide a “guaranteed non-punctured” 20 MHz channel for 80 MHz-operating STAs in the non-primary 80 MHz
PHY ad-hoc discussed the issue [3] and found strong support for Option 3 (SP results: 7/3/42)
  It was suggested that SFD SP should be run in the joint session

## Slide 6: Required MAC support for Option 3
The details of the SST protocol and signaling will mostly be developed in the MAC ad-hoc
As part of SST signaling, the STA should receive an indication of a “guaranteed non-punctured 20 MHz” within its non-primary 80 MHz
It is requested that this requirement is taken into account during the definition of SST

## Slide 7: 160 MHz operating STAs
Similar discussion and questions need to be resolved for 160 MHz operating STAs

## Slide 8: Summary
We’ve highlighted some of the PHY-related agreements that may impact definition of SST in 802.11be
Full definition of SST protocol needs to be consistent with these agreements

## Slide 9: SP1
Do you agree that:
  for an 80 MHz operating STA supporting SST that is assigned (by the AP) a non-primary 80 MHz channel in a 160 MHz or 320 MHz EHT MU PPDU using SST, the STA shall have prior knowledge of at least one "guaranteed non-punctured 20 MHz channel" from the AP within the non-primary 80 MHz.
  Notes:
    This agreement might apply to R1 insofar as operation in non-primary 80 MHz is defined in R1
    SST in non-primary 160 MHz is an agreed R2 feature
    ways of informing the STA (signaling, static information, …) are TBD

## Slide 10: SP2
Do you agree that:
  for a 160 MHz operating STA supporting SST that is assigned (by the AP) a non-primary 160 MHz channel in a 320 MHz EHT MU PPDU using SST, the STA shall have prior knowledge of at least one "guaranteed non-punctured 20 MHz channel" from the AP within the non-primary 160 MHz.
  Notes:
    SST in non-primary 160 MHz is an agreed R2 feature
    ways of informing the STA (signaling, static information, …) are TBD

## Slide 11: References
[1] “Mandatory larger BW support,” 20/0796r1, June 2020.
[2] “U-SIG structure and preamble processing,” 20/0380r0, March 2020.
[3] “Clarification of 80 MHz operation in wider-BW OFDMA”, 21/0015r1, January 2021