## Slide 1: Considerations on Capabilities and Operation Mode: MU-MIMO
Date: 2021-01-18
Authors:
Name | Affiliations | Address | Phone | email
Wook Bong Lee | Samsung |  |  | wookbong.lee@Samsung.com
Pavan Veerashetty | Samsung |  |  | 
Junghoon Suh | Huawei |  |  | Junghoon.Suh@huawei.com
Jinsoo Choi | LG |  |  | js.choi@lge.com

## Slide 2: Introduction
In this contribution, we provided 11ax MU-MIMO field test results and we discussed issues and proposed solutions for 11be
Revision 1-3:
  Updated discussions
  Updated proposed OM field, A-Control, SPs are modified accordingly

## Slide 3: Test Setup
AP: 4 transmit antennas
This AP scheduled Nss = [2, 2] using MU-MIMO when there are two non-AP STAs with Nss 2 reception capabilities
Non-AP STA: 2 receive antennas and capable of MCS 11 for Nss = 2
Run downlink throughput test
  MU mode: two non-AP STAs connected to the AP
  SU mode: single non-AP STA connected to the AP
Note that we also tested different non-AP STA. As we can’t control its capabilities, we checked 2x2+2x2 and Nss2 with MCS11, and results were pretty much same for that of DUT

## Slide 4: Test Results
Test scenarios
  Three test cases: different Supported HE-MCS And NSS Set
    Case1: HE-MCS 0-7 Nss = 2
    Case2: HE-MCS 0-9 Nss = 2
    Case3: HE-MCS 0-11 Nss = 2
Observation:
  Nss = [2, 2] with higher MCS level suffers from inter-stream interference. In this case, it is better to support only Nss = 2 HE-MCS 0-9 (only for MU)
Note that for Case 1 and Case 2, actual throughput will be better if we can support different MCS level for SU and MU. As there were quite many SU packet during the test.
With the same test setup, device could support Nss 2 with MCS 11 with almost no error in SU case
 | Sum Throughput / Case 3 Sum Throughput | Number of MPDU Errors
Case 1 | 96.2 % | 41
Case 2 | 99.9 % | 7959
Case 3 | 100 % | 138043

## Slide 5: Test Results 2
Test scenarios
  Two test cases: Supported HE-MCS And NSS Set
    Case1: HE-MCS 0-11 Nss = 2
    Case2:
      One device: HE-MCS 0-11 Nss = 2,
      Other device: HE-MCS 0-11 Nss = 1 (still two receive antennas)
Observation:
  Reducing total number of stream helps to improve throughput in many cases
Similar to test 1, actual throughput of case 2 will be better if we can support different Nss level for SU and MU. As there were quite many SU packet during the test.
 | Case 2 / Case 1
Test 1 | 100%
Test 2 | 107.4%
Test 3 | 114.2%

## Slide 6: Supported NSS and MCS level
11ax does not distinguish between SU and MU supported NSS and MCS level.
When there is no inter-stream interference, indeed, a non-AP STA can support same NSS and MCS level for SU and MU operation.
However, when there is inter-stream interference, (depending on interference level) supported NSS and MCS level for MU can be smaller than SU case.
Note that inter-stream interference level can be increased as time between sounding and data transmission increased.
We propose to have two different set of Supported NSS and MCS level and separate Rx NSS can be updated by e.g. OMI (OM Control)

## Slide 7: Discussions (1/4)
AP needs to have two sets of non-AP STA capabilities for (Rx Nss, MCS).
  High MCS level is sensitive to additional interference. For example, 1024 QAM and 4K QAM may be not suitable for MU-MIMO when using all of antennas to receive its spatial streams, e.g. MU-MIMO with Nss = 2, MCS 10 to 13 when non-AP STA has two receive antennas
Different Rx Nss, MCS assumptions in SU and MU link adaptation
  SU and MU show quite different performance, so it is natural to have two different link adaptation results (Rx Nss, MCS)
Dynamic link adaptation solution, e.g. feedback in BA, will be better than static/semi-static (Capability/OM) solution
  We can develop dynamic link adaptation solution in release 2
  In the meantime, we want some solution in release 1 as well

## Slide 8: Discussions (2/4)
Updating Rx Nss may result in re-grouping and re-sounding
  AP can apply update Rx Nss (or MU Nc) from next sounding
A non-AP STA may be participated in multiple Groups. In this case, if a non-AP STA determine lowering MU Rx Nss based on a certain MU group, it may be not best
  This is actually a good case where the signaling is helping AP not to use the group.
  Furthermore if there are more than 3 non-AP STAs, it will be better if AP assigns 1 steam each so that non-AP STA can reject/suppress inter-stream interference using extra receive antenna. In this way, the chance of using more number of streams will be higher.

## Slide 9: Discussions (3/4)
Three streams may not be optimal as there are cases where two or four stream transmission is better. Since AP has all the information it needs to select best Nss, it should be AP’s role to determine right Nss
  As seen in the test results, even though AP has all the information, some AP couldn’t select the right Nss value for certain cases.
  Proposed method will help AP to determine the right Nss for these cases
Note that in many case, two user with single stream each will provide much higher throughput than SU two stream case as
  the transmitter can suppress inter stream interference more using its extra degree of freedom (e.g. 4 Tx to 2 streams or 3 streams) and
  the receiver can suppress inter stream interference using its extra degree of freedom (e.g. 2 antennas to receive one spatial steam and suppress other steam interference)
However, currently we observed worse MU-MIMO throughput than SU in some cases

## Slide 10: Discussions (4/4)
There is no difference for 1x1 non-AP STA
Non-AP STA with more than two receive antennas (high throughput demanding STAs) will try its best to have better throughput in MU-MIMO
So, it won’t reduce MU-MIMO Rx Nss unless it is beneficial for the STA
If changing MU-MIMO Rx Nss is beneficial for the STA, then it is beneficial for network throughput as well

## Slide 11: SU and MU Rx EHT MCS Map
Two sets of Rx EHT-MCS Map
  Rx EHT-MCS Map indicates the maximum value of the maximum MCS that can be received by the STA for each number of spatial stream using SU-MIMO
  MU-MIMO Rx EHT-MCS Map indicates the maximum value of the maximum MCS that can be received by the STA for each number of spatial stream using MU-MIMO
Tx EHT-MCS Map indicates the maximum value of the maximum MCS that can be transmitted by the STA for each number of spatial stream using either SU or MU-MIMO
 | Rx EHT-MCS Map ≤ 80 MHz | MU-MIMO Rx EHT-MCS Map ≤ 80 MHz | Tx EHT-MCS Map ≤ 80 MHz | Rx EHT-MCS Map 160 MHz | MU-MIMO Rx EHT-MCS Map 160 MHz | Tx EHT-MCS Map 160 MHz | Rx EHT-MCS Map 320 MHz | MU-MIMO Rx EHT-MCS Map 320 MHz | Tx EHT-MCS Map 320 MHz
Octets: | 4 | 1 | 4 | 0 or 4 | 0 or 1 | 0 or 4 | 0 or 4 | 0 or 1 | 0 or 4

## Slide 12: Rx/Tx EHT MCS Map
Need to support 16 spatial stream (in R2), and MCS level is now increased to 15
So, each subfield can be 4 Byte with following format
  For 20 MHz only STA,
    0 indicates support for EHT-MCS 0-7 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    1 indicates support for EHT-MCS 0-9 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    2 indicates support for EHT-MCS 0-11 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    3 indicates that n spatial streams is not supported for EHT PPDUs
  For other STA
    0 indicates support for EHT-MCS 0-9 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    1 indicates support for EHT-MCS 0-11 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    2 indicates support for EHT-MCS 0-13 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    3 indicates that n spatial streams is not supported for EHT PPDUs
Note: EHT-MCS 14 can be indicated separately
 | B0 B1 | B2 B3 | B4 B5 | B6 B7 | B8 B9 | B10 B11 | B12 B13 | B14 B15
 | Max EHT-MCS For 1 SS | Max EHT-MCS For 2 SS | Max EHT-MCS For 3 SS | Max EHT-MCS For 4 SS | Max EHT-MCS For 5 SS | Max EHT-MCS For 6 SS | Max EHT-MCS For 7 SS | Max EHT-MCS For 8 SS
Bits: | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | B16 B17 | B18 B19 | B20 B21 | B22 B23 | B24 B25 | B26 B27 | B28 B29 | B30 B31
 | Max EHT-MCS For 9 SS | Max EHT-MCS For 10 SS | Max EHT-MCS For 11 SS | Max EHT-MCS For 12 SS | Max EHT-MCS For 13 SS | Max EHT-MCS For 14 SS | Max EHT-MCS For 15 SS | Max EHT-MCS For 16 SS
Bits: | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2

## Slide 13: MU-MIMO Rx EHT MCS Map
MU-MIMO supports up to 4 SS
So, each subfield can be 1 Byte with following format
  For 20 MHz only STA,
    0 indicates support for EHT-MCS 0-7 for n spatial streams
    1 indicates support for EHT-MCS 0-9 for n spatial streams
    2 indicates support for EHT-MCS 0-11 for n spatial streams
    3 indicates that n spatial streams is not supported for EHT PPDUs
  For other STA
    0 indicates support for EHT-MCS 0-9 for n spatial streams
    1 indicates support for EHT-MCS 0-11 for n spatial streams
    2 indicates support for EHT-MCS 0-13 for n spatial streams
    3 indicates that n spatial streams is not supported for EHT PPDUs
 | B0 B1 | B2 B3 | B4 B5 | B6 B7
 | Max EHT-MCS For 1 SS | Max EHT-MCS For 2 SS | Max EHT-MCS For 3 SS | Max EHT-MCS For 4 SS
Bits: | 2 | 2 | 2 | 2

## Slide 14: Extended Operating Mode Notification Frame Format
Proposal is to add an extended operating mode notification frame action field format as follows
Extended Operating Mode can also be defined as standalone IE to be included in beacon and Probe response frame
Order | Information
1 | Category
2 | EHT
3 | Extended Operating

## Slide 15: Extended Operating Mode
The Rx NSS indicates the maximum number of spatial streams that the STA supports in reception using SU-MIMO
The MU-MIMO Rx NSS indicates the maximum number of spatial streams that the STA supports in reception using MU-MIMO
 | B0 B2 | B3 | B4 B7 | B8 B9 | B10 | 
 | Channel Width | No LDPC | Rx NSS | MU-MIMO Rx NSS | Rx NSS Type | 
Bits: | 3 | 1 | 4 | 2 | 1 | 
Example of Operating Mode field format

## Slide 16: Extended Operating Mode Control As part of A-Control
A new A-Control field which has the functionality of existing OM Control Can be defined to accommodate this new field which looks as follows
 | B0 B3 | B4 B5 | B6 B8 | B9
 | Rx NSS | MU-MIMO Rx NSS | Channel Width | UL MU Disable
Bits: | 4 | 2 | 3 | 1
 | B10 B13 | B14 | B15 | B16
 | TX NSS | ER SU Disable | DL MU-MIMO Resound Recommendation | UL MU Data Disable
Bits: | 4 | 1 | 1 | 1
Example of Extended OM Control format

## Slide 17: SP #1
Do you support different (MCS, NSS) capabilities for SU and MU-MIMO?
  Y/N/A

## Slide 18: SP #1a
Do you support link adaptation feedback, from a non-AP STA to its associated AP, in EHT R2?
  The format of the feedback is TBD (e.g., MCS)
  The feedback might reflect differences between SU MIMO and MU MIMO
  Y/N/A

## Slide 19: SP #2
Which option do you prefer?
  Option 1: OM to change MU-MIMO Rx Nss or maximum Nc for MU in release 1
  Option 2: Improve link adaptation, especially MU-MIMO in release 2
  Option 3: Both option 1 and 2
  Option 4: None of option 1 or 2
  This SP is for information gathering
  Result was
    Opt1: 25
    Opt2: 31
    Opt3: 19
    Opt4: 28

## Slide 20: SP #3
Do you support to define the following as a Supported EHT-MCS And NSS field?
  SU Rx EHT-MCS Map indicates the maximum value of the maximum MCS that can be received by the STA for each number of spatial stream using SU-MIMO
  MU Rx EHT-MCS Map indicates the maximum value of the maximum MCS that can be received by the STA for each number of spatial stream using MU-MIMO
  Tx EHT-MCS Map indicates the maximum value of the maximum MCS that can be transmitted by the STA for each number of spatial stream using either SU or MU-MIMO
  Y/N/A
 | Rx EHT-MCS Map ≤ 80 MHz | MU-MIMO Rx EHT-MCS Map ≤ 80 MHz | Tx EHT-MCS Map ≤ 80 MHz | Rx EHT-MCS Map 160 MHz | MU-MIMO Rx EHT-MCS Map 160 MHz | Tx EHT-MCS Map 160 MHz | Rx EHT-MCS Map 320 MHz | MU-MIMO Rx EHT-MCS Map 320 MHz | Tx EHT-MCS Map 320 MHz
Octets: | 4 | 1 | 4 | 0 or 4 | 0 or 1 | 0 or 4 | 0 or 4 | 0 or 1 | 0 or 4

## Slide 21: SP #4
Do you support to define the following as an Rx/Tx EHT MCS Map subfields?
  For 20 MHz only STA,
    0 indicates support for EHT-MCS 0-7 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    1 indicates support for EHT-MCS 0-9 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    2 indicates support for EHT-MCS 0-11 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    3 indicates that n spatial streams is not supported for EHT PPDUs
  For other STA
    0 indicates support for EHT-MCS 0-9 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    1 indicates support for EHT-MCS 0-11 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    2 indicates support for EHT-MCS 0-13 for n spatial streams, for 1 spatial stream it includes EHT-MCS 15
    3 indicates that n spatial streams is not supported for EHT PPDUs
  Note: EHT-MCS 14 can be indicated separately
  Y/N/A
 | B0 B1 | B2 B3 | B4 B5 | B6 B7 | B8 B9 | B10 B11 | B12 B13 | B14 B15
 | Max EHT-MCS For 1 SS | Max EHT-MCS For 2 SS | Max EHT-MCS For 3 SS | Max EHT-MCS For 4 SS | Max EHT-MCS For 5 SS | Max EHT-MCS For 6 SS | Max EHT-MCS For 7 SS | Max EHT-MCS For 8 SS
Bits: | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
 | B16 B17 | B18 B19 | B20 B21 | B22 B23 | B24 B25 | B26 B27 | B28 B29 | B30 B31
 | Max EHT-MCS For 9 SS | Max EHT-MCS For 10 SS | Max EHT-MCS For 11 SS | Max EHT-MCS For 12 SS | Max EHT-MCS For 13 SS | Max EHT-MCS For 14 SS | Max EHT-MCS For 15 SS | Max EHT-MCS For 16 SS
Bits: | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2

## Slide 22: SP #5
Do you support to define the following as an MU-MIMO Rx EHT MCS Map subfields?
  For 20 MHz only STA,
    0 indicates support for EHT-MCS 0-7 for n spatial streams
    1 indicates support for EHT-MCS 0-9 for n spatial streams
    2 indicates support for EHT-MCS 0-11 for n spatial streams
    3 indicates that n spatial streams is not supported for EHT PPDUs
  For other STA
    0 indicates support for EHT-MCS 0-9 for n spatial streams
    1 indicates support for EHT-MCS 0-11 for n spatial streams
    2 indicates support for EHT-MCS 0-13 for n spatial streams
    3 indicates that n spatial streams is not supported for EHT PPDUs
  Y/N/A
 | B0 B1 | B2 B3 | B4 B5 | B6 B7
 | Max EHT-MCS For 1 SS | Max EHT-MCS For 2 SS | Max EHT-MCS For 3 SS | Max EHT-MCS For 4 SS
Bits: | 2 | 2 | 2 | 2

## Slide 23: SP #6-a
Do you support to add 2 bit MU Nc subfield in (Extended/EHT) Operating Mode field and in A-Control field for (Extended/EHT) Operating Mode Control?
  The MU Nc subfield indicates the maximum number of the Nc subfield when “Feedback Type And Ng subfield and Codebook Size subfield” indicates MU feedback
  Y/N/A

## Slide 24: SP #6-b
Do you support to add 2 bit MU-MIMO Rx Nss subfield in (Extended/EHT) Operating Mode field and in A-Control field for (Extended/EHT) Operating Mode Control?
  The MU-MIMO Rx Nss subfield indicates the maximum number of Nss,u/Nss,r,u value for the STA to receive in MU-MIMO packet
  Y/N/A

## Slide 26: SP #5
Do you support to add 2 bit MU Nc subfield in (Extended/EHT) Operating Mode field and in A-Control field for (Extended/EHT) Operating Mode Control?
  The MU Nc subfield indicates the maximum number of the Nc subfield when “Feedback Type And Ng subfield and Codebook Size subfield” indicates MU feedback
  Y/N/A

## Slide 27: Appendix

## Slide 28: OM Control
The Control Information subfield in an OM Control subfield contains information related to the operating mode (OM) change of the STA transmitting the frame containing this information (see 26.9 (Operating mode indication)).
If the operating channel width of the STA is greater than 80 MHz, then the Rx NSS subfield indicates the maximum number of spatial streams, NSS, that the STA supports in reception for PPDU bandwidths less than or equal to 80 MHz and is set to NSS – 1. If the operating channel width of the STA is less than or equal to 80 MHz, then the Rx NSS subfield indicates the maximum number of spatial streams, NSS, that the STA supports in reception and is set to NSS – 1.

## Slide 29: Supported HE-MCS And NSS Set field
The Supported HE-MCS And NSS Set field indicates the combinations of HE-MCSs and spatial streams that a STA supports for reception and the combinations that it supports for transmission. The format of the field is shown in Figure 9-788d (Supported HE-MCS And NSS Set field format). The Rx HE-MCS Map and Tx HE-MCS Map subfields have the format shown in Figure 9-788e (Rx HE-MCS Map subfield, Tx HE-MCS Map subfield and Basic HE-MCS And NSS Set field format).