## Slide 1: PAPR Comparison for Two 320MHz Phase Rotation Sequences
Date: 2021-01-20
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], a new 320MHz phase rotation sequence was proposed for 320MHz non-HT Dup PPDU and pre-EHT modulated fields as well
In this contribution, we provide several reasons why we need to keep the agreed 320MHz phase rotation for pre-EHT modulated fields as follows
  160MHz RF and Worst U-SIG PAPR
  Overall U-SIG PAPR
  EHT-SIG PAPR
We also propose that the agreed 320MHz phase rotation sequence is applied to 320MHz non-HT Dup PPDU to reduce its PAPR

## Slide 3: Assumption (1/2)
We use the following notation for each phase rotation sequence
  PR1: 320MHz phase rotation agreed in TGbe
    [1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
  PR2: 320MHz phase rotation proposed in [1]
    [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1]
We investigate PAPR by focusing on U-SIG and EHT-SIG
  As shown in [2], U-SIG, L-SIG or EHT-SIG have higher PAPR than the other pre-EHT modulated fields
    Note that U-SIG and L-SIG have similar PAPR
  We assume the following structures
    U-SIG is duplicated in all 20MHz subchannels
    EHT-SIG consists of two content channels, i.e., [1212 1212 1212 1212]
For PAPR investigation, we consider 23 mandatory preamble puncturing cases defined in 320MHz as shown in the next slide

## Slide 4: Assumption (2/2)
23 mandatory preamble puncturing cases
  [OOOO OOOO OOOO OOOO]
  [XXOO OOOO OOOO OOOO], [OOXX OOOO OOOO OOOO], [OOOO XXOO OOOO OOOO], [OOOO OOXX OOOO OOOO], [OOOO OOOO XXOO OOOO], [OOOO OOOO OOXX OOOO], [OOOO OOOO OOOO XXOO], [OOOO OOOO OOOO OOXX]
  [XXXX OOOO OOOO OOOO], [OOOO OOOO OOOO XXXX]
  [XXXX XXOO OOOO OOOO], [XXOO OOOO OOOO XXXX], [XXXX OOXX OOOO OOOO], [OOXX OOOO OOOO XXXX], [XXXX OOOO XXOO OOOO], [OOOO XXOO OOOO XXXX], [XXXX OOOO OOXX OOOO], [OOOO OOXX OOOO XXXX], [XXXX OOOO OOOO XXOO], [OOOO OOOO XXOO XXXX], [XXXX OOOO OOOO OOXX], [OOOO OOOO OOXX XXXX]
O: non-punctured 20MHz
X: punctured 20MHz

## Slide 5: 160MHz RF and Worst U-SIG PAPR (1/2)
When transmitting 320MHz PPDU, it can be generated by using two 160MHz capable RFs
  These devices may be commonly used and relatively low-end compared to those with 320MHz capable RF
160MHz operating STAs can participate in 320MHz transmission
  They can transmit 320MHz TB PPDU by being assigned within 160MHz which is either lower or upper 160MHz
  They may use 160MHz RF to generate the TB PPDU
Thus, we need to take much more care of 160MHz PAPR in 320MHz PPDU transmission

## Slide 6: 160MHz RF and Worst U-SIG PAPR(2/2)
Following figure shows the *worst 320MHz U-SIG PAPR among agreed mandatory puncturing cases when using 160MHz RF
  PR2 has higher PAPR and its median PAPR is about 12dB
  Note that median Data PAPR for 160MHz PPDU is about 9dB as shown in [2]
In Appendix, the worst 320MHz U-SIG PAPR is shown when using 320MHz RF
PR1 has higher PAPR but it is similar to the worst EHT-SIG PAPR of PR2 shown in slide 8
This issue is further discussed in slide 8
* To obtain the worst PAPR, in each generation, 23 puncturing cases are applied and maximum PAPR is chosen (we generate 500 random U-SIG)

## Slide 7: Overall U-SIG PAPR
Following figures show the *overall 320MHz U-SIG PAPR by considering all of the agreed mandatory puncturing cases when using 320MHz RF and 160MHz RF, respectively
<320MHz>
<160MHz>
* To obtain the overall PAPR, in each generation all of the PAPR values for 23 puncturing cases are used (we generate 500 random U-SIG)

## Slide 8: EHT-SIG PAPR (1/2)
We also check on the worst and overall 320MHz EHT-SIG PAPR
Following figures show the worst 320MHz EHT-SIG PAPR among agreed mandatory puncturing cases when using 320MHz RF
<BPSK>
<QPSK>
PR2 has higher PAPR and it is similar to the worst U-SIG PAPR of PR1 as shown in Appendix
EHT-SIG may be more vulnerable to the distortion caused by high PAPR
U-SIG may obtain better combining gain than EHT-SIG at the receiver
It is better to have low EHT-SIG PAPR
In Appendix, we show the worst 320MHz EHT-SIG PAPR among agreed mandatory puncturing cases when using 160MHz RF

## Slide 9: EHT-SIG PAPR (2/2)
Following figures show the overall 320MHz EHT-SIG PAPR by considering all of the puncturing cases when using 320MHz RF
<BPSK>
<QPSK>
In Appendix, we show the overall 320MHz EHT-SIG PAPR by considering all of the puncturing cases when using 160MHz RF

## Slide 10: Summary for PAPR Investigation
PAPR Comparison between PR1 and PR2 for pre-EHT modulated fields of 320MHz PPDU
 | 320MHz RF | 160MHz RF
Worst PAPR | PR1 and PR2 are similar Maximum for PR1 comes from U-SIG Maximum for PR2 comes from EHT-SIG | PR1 is better Maximum for Both comes form U-SIG
Overall PAPR | PR1 and PR2 are similar Maximum for Both comes form U-SIG | PR1 and PR2 are similar Maximum for Both comes form U-SIG

## Slide 11: 320MHz Non-HT Dup PPDU
320MHz non-HT Dup PPDU consists of legacy preamble and Data fields
  All of the fields are duplicated in all 20MHz subchannels
The agreed 320MHz phase rotation sequence can be applied to the legacy preamble field to reduce PAPR
In this case, the same phase rotation needs to be applied to the Data field to enable unassociated / OBSS STAs to correctly decode it
  This phase rotation can also reduce Data field PAPR
  As a result, Data field PAPR is similar to U-SIG and slightly higher than U-SIG when BPSK and QPSK is used for modulation of the Data field, respectively
We propose that the agreed 320MHz phase rotation sequence is applied to all of the fields of 320MHz non-HT Dup PPDU

## Slide 12: Conclusion
We have confirmed that the agreed 320MHz phase rotation sequence is a better choice for pre-EHT modulated fields based on various PAPR results
We have also proposed that the agreed phase rotation sequence is applied to all of the fields of 320MHz non-HT Dup PPDU

## Slide 13: Straw poll #1
Do you agree to add the following text to the TGbe SFD?
  The following 320MHz phase rotation sequence agreed in the TGbe spec is applied to all of the fields of 320MHz non-HT Dup PPDU
    [1 -1 -1 -1 1 -1 -1 -1 -1 1 1 1 -1 1 1 1]
  Note: This is for release 1
Y/N/A: //

## Slide 14: References
[1] 802.11-21/0129r0 Phase Rotation for 320 MHz Non-HT Duplicate Transmission and Pre-EHT modulated Fields
[2] 802.11-20/0699r1 Phase Rotation Proposal Follow-Up

## Slide 15: Appendix
Following figure shows the worst 320MHz U-SIG PAPR among agreed mandatory puncturing cases when using 320MHz RF

## Slide 16: Appendix
Following figures show the worst 320MHz EHT-SIG PAPR among agreed mandatory puncturing cases when using 160MHz RF
<BPSK>
<QPSK>

## Slide 17: Appendix
Following figures show the overall 320MHz EHT-SIG PAPR by considering all of the puncturing cases when using 320MHz RF
<BPSK>
<QPSK>