## Slide 1: Operation after Multi-link Setup
Date: 2021-01-xx
Authors:
Name | Affiliation | Address | Phone | Email
Insun Jang | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | insun.jang@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Namyeong Kim |  |  |  | namyeong.kim@lge.com
Sunhee Baek |  |  |  | sunhee.baek@lge.com

## Slide 2: Introduction
We have determined many points of multi-link (ML) setup [1], [2]
  Exchange of Association frames on a link only
  Basic-variant ML element (including the common info and link info with complete information)
  Including MLD-level information (e.g., AID, Listen Interval)
However, we need to clarify “How can AP(s) on link(s) to be setup, where association frames are not exchanged, operate with non-AP(s)”, which will be discussed in this contribution
  We call the link(s) non-transmitting link while calling the link where association frames are exchanged transmitting link

## Slide 3: Motivation and Problem Statement
Non-AP MLD intends to setup Link 1 (transmitting link) and Link 2 (non-transmitting link) with AP MLD

## Slide 4: Initial Transmission of Non-AP MLD
Non-AP STA (STA B) operating on non-transmitting link (link 2) can first transmit any frame (e.g., Class 1/2/3) to the AP (AP 2) corresponding to that link
  It will include its MAC address in TA field, which lets AP 2 know STA B’s MAC address
However, AP 2 doesn’t know which MLD STA B is affiliated with
  AP 2 cannot update the state/information regarding the non-AP MLD with which STA B is affiliated

## Slide 5: Discussion and Possible Options
Consequently, an AP MLD needs the information to distinguish STAs affiliated with a non-AP MLD on non-transmitting links and bind STAs and their MLD
We can have several options
  Option 1 (Preferred): Signaling MAC addresses of STAs during ML setup
    It can be a good candidate and simply apply to current ML IE format based on D0.3
  Option 2: Carries STA ID (derived from AID) on non-transmitting link right after ML setup
    It can be carried in a control field with a new A-Control ID; however, it may be the waste of control ID only for resolving the issue
  Option 3: Setting MAC address field as MLD MAC address on non-transmitting link right after ML setup
    For example, when a non-AP STA transmits a certain frame initially right after ML setup, its TA field is set to the non-AP MLD’s MAC address; however, a new addressing rule is needed only for resolving the issue

## Slide 6: Main Proposal
We propose to indicate MAC addresses of STAs affiliated with a non-AP MLD during ML Setup
  Beacon or Probe Response frame doesn’t need to include that information because it is unnecessary before ML setup (except for request of the complete information)
Therefore, MAC address field/element is included as a portion of the complete information (one fixed order…) indicated in the Link Info field of Per-STA Profile of Basic-variant ML element

## Slide 7: Applying to Current ML IE format
Currently, we have TBD fields in fixed order and TBD elements in fixed order in the complete information
Therefore, we can have a MAC address field or element in fixed order (e.g., in Element 2)

## Slide 8: Conclusion
We observed an AP MLD needs the information to distinguish STAs affiliated with a non-AP MLD and bind STAs and their MLD in order to operate with non-AP STA(s) on non-transmitting link(s) after ML setup
Therefore, to enable that, we proposed indicate MAC addresses of STAs affiliated with a non-AP MLD during ML Setup
  Specifically, MAC address field/element is included as a portion of the complete information indicated in the Link Info field of Per-STA Profile of Basic-variant ML element

## Slide 9: SP #1
Do you agree to include the information of MAC addresses of STAs as a portion of the complete information indicated in the Link Info field of Per-STA Profile of Basic-variant ML element?
  Signaling is TBD

## Slide 10: References
[1] 802.11-19/1262r23 Specification Framework for TGbe
[2] IEEE P802.11be/D0.3, January 2021