## Slide 1: Flexible TID to AC Mapping for R1
Date: 2020-10-6
Authors:
Name | Affiliation | Address | Phone | Email
Duncan Ho | Qualcomm Inc. | 5665 Morehouse Dr. San Diego, CA 92121 |  | dho@qti.qualcomm.com
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Abhishek Patil | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 

## Slide 2: Intro
For a STA of a non-AP MLD to request low latency traffic flow support, the STA need to describe its expected traffic pattern and QoS requirements of this traffic flow to the AP
  E.g., mean data rate, latency bound, etc.
The MLD can then use the TID to identify this low-latency traffic flow
  TID can then be used to prioritize between the traffic flows (e.g., by EDCA, scheduling and TWT)

## Slide 3: Flexible TID to AC Mapping
Currently 4-bit TID: 0 – 7 mapped to 4 different ACs (fixed mapping)
  Each AC can only support 2 TIDs
To support multiple low-lat traffic flows for the same non-AP MLD, we may need more than 2 TIDs for the same AC
Proposal:
  Decouple the 4-bit TID completely from AC for QoS traffic streams
  TID to AC mapping can be specified separately (signaling TBD)
    TID 0-7 mapped freely to 4 ACs
    Capability on BOTH sides that says I allow flex TID to AC mapping (optional for both sides)

## Slide 4: SP1
Do you agree to add to 11be R1:
  Have a flexible mapping between the TID value and an AC (signaling TBD)