## Slide 1: Discussion on NSTR Blindness Recovery
Date: 2021-01-15
Authors:

## Slide 2
Abstract
In this contribution, we provide some discussion on blindness recovery for NSTR non-AP MLDs.

## Slide 3: Introduction
TGbe has agreed on the following for blindness recovery for NSTR MLDs [Motion 150, #SP373]:
  In R1, if during a transmission of a STA (STA-1) of a non-STR non-AP MLD, another STA (STA-2) of the same MLD cannot detect its medium state when required (due to STA-1’s UL transmission interference), STA-2 shall start a MediumSyncDelay timer at the end of STA-1’s transmission, unless the STA-2 ended a transmission at the same time.
    The MediumSyncDelay timer expires after a duration value that is either assigned by AP or a default value in the specification or if at least either of the following events happens:
    any received PPDU with a valid MPDU,
    a received PPDU whose corresponding RXVECTOR parameter TXOP_DURATION is not UNSPECIFIED,
  whichever happens first.
STA-2 shall perform CCA until the MediumSyncDelay timer expires. Additional TBD exceptions may be considered.
NOTE – It is TBD whether STA-2 is required to start the MediumSyncDelay timer if the transmission of STA-1 is shorter than TBD duration.
Frequent self-interference within a NSTR MLD causes the MLD to suffer from decreased medium access
We discuss a few options to ensure that such loss of efficiency due to NSTR blindness may be reduced

## Slide 4: NSTR Blindness
NSTR blindness is caused by transmission of a NSTR MLD on one of the NSTR link and causes self-interference on other NSTR links because the other NSTR links cannot receive packets correctly
Frequent self-interference can lead to loss of medium access opportunities, and hence decreased throughput
A number of mechanisms have been proposed to try to mitigate this issue

## Slide 5: NSTR Blindness Mitigation Options (1)
Some of the following options may be used to mitigate NSTR blindness
Option 1: align the begin and end of the transmissions on NSTR links
Option 2: let STA2 transmit RTS subject to certain medium conditions
Option 3: AP 2 transmits a trigger frame to STA2
Option 4: AP 2 transmits a short valid PPDU on link 2 to provide sync to STA2
We will explore the pros and cons of each of these options

## Slide 6: NSTR Blindness Mitigation Options (2)
Option 1: align the begin and end of the transmissions on NSTR links
  This option will prevent the NSTR blindness issue from occurring
  Unfortunately, this is not always possible due to WM status on all NSTR links, traffic load
  Mandating NSTR STAs to always use aligned transmissions will limit throughput for NSTR MLDs
Option 2: let STA2 transmit RTS subject to certain medium conditions
  Pro: can provide NSTR devices more medium access after NSTR blindness
  Con: may interrupt ongoing transmission because the NSTR devices are not aware of any basic NAV and intra-BSS NAV

## Slide 7: NSTR Blindness Mitigation Options (3)
Option 3: AP 2 transmits a trigger frame to STA2
  Pro: may provide additional medium access for NSTR STAs after NSTR blindness
  Con: may cause some unfairness to other STAs contention for the medium; in addition, the trigger frame may not take place during the MediumSyncDelay
Option 4: AP 2 transmits a short valid PPDU on link 2 to provide sync to STA2
  The short PPDU is only transmitted when the medium is idle on link 2, or when AP 2 determines that the medium can be considered idle (e.g., subject to regulatory requirements)
    Medium being idle on link 2 will likely cause the longest delay for STAs to recover after NSTR blindness
  Pro: provides a mechanism for NSTR STAs to sync to medium status after NSTR blindness; will not affect the fairness on NSTR links
  Con: AP 2 needs to transmit a small packet during the MediumSyncDelay on link 2 when the medium is idle, similar to a trigger frame

## Slide 8: NSTR Blindness Mitigation Options (4)
Based on the evaluation of the pros and cons of these options, we believe that Option 4 should be considered as an option for mitigating NSTR blindness issues
  Can provide quick medium sync in case the link is idle
  Does not interrupt ongoing transmission on link 2
  Does not impact fairness on link 2

## Slide 9: Conclusions
In this contribution, we discuss a few options to reduce impact from NSTR blindness
We discussed the pros and cons of a number of approaches
Option 4 (AP 2 transmits a short valid PPDU on link 2 to provide sync to STA2) should be considered as an option to mitigate NSTR blindness issues

## Slide 10
References
[1] IEEE 11-20/444r1, MLA: Non-STR STA EDCA Rules After Self-Interference, April 2020
[2] IEEE 11-20/0490r0, Impact of Channel Blindness During ML, March 2020
[3] IEEE 11-20/1009r10, Blindness Issues for Non-STR Operations-Follow Up, July 2020

## Slide 11: Straw poll 1
Do you agree that Option 4 as shown on slide 5 should be considered as an option to mitigate NSTR blindness?
Y/N/Abs: