## Slide 1: Further discussion on BW extension of EHT trigger frame
Date: 2021-02-18
Authors:

## Slide 2: Background
We agree that
  The UL BW Extension field and the UL BW field together indicate the bandwidth of the EHT TB PPDU solicited by the Trigger frame
  The UL BW Extension field is defined as the left table
  The EHT STA is not allowed to transmit HE TB PPDU in Secondary 160 MHz even if the solicited TB PPDU is A-PPDU
  The UL BW Extension now only supports pure EHT TB PPDU transmission since A-PPDU is R2 feature
  However, if the extra entries of UL BW extension field are defined in R2, then R1 STA can not recognize them such that it can not participate A-PPDU transmission with R2 STA
  For example, R1 STA could not participate “HE (Primary 160 MHz) + EHT （Third 80 MHz）” A-PPDU transmission
UL BW (2 bits) | Bandwidth for HE TB PPDU, MHz | UL BW Extension (2 bits) | Bandwidth for EHT TB PPDU, MHz
0 | 20 | 0 | 20
0 | 20 | 1 | reserved
0 | 20 | 2 | reserved
0 | 20 | 3 | reserved
1 | 40 | 0 | 40
1 | 40 | 1 | reserved
1 | 40 | 2 | reserved
1 | 40 | 3 | reserved
2 | 80 | 0 | 80
2 | 80 | 1 | reserved
2 | 80 | 2 | reserved
2 | 80 | 3 | reserved
3 | 160 | 0 | reserved
3 | 160 | 1 | 160
3 | 160 | 2 | 320 -1
3 | 160 | 3 | 320-2

## Slide 3: Discussion
Two cases for A-PPDU transmission
  All the STAs park on primary 20 MHz channel
  Some STAs park on primary 20 MHz channel, and the other STAs park on non-primary 20 MHz channel
  The first case is easily implemented, no extra procedure is needed, like the existing trigger based PPDU transmission
  However, for the second case,
  It not only requires extra procedure to allow some STAs to park on non-primary 20 MHz channel, but also needs to make sure that these STA get sync on with the info provided on primary channel
  Moreover, the transmission rule is also needed if some STAs park on non-primary channel
  A-PPDU （TB） transmission is transparent to the non-AP STA, but requires extra decoding procedure at the AP side. In this case, we could be open that A-PPDU is R2 feature
  To make A-PPDU transmission useful, it is good to allow R1 STA to participate A-PPDU transmission with R2 STA because of no extra complexity

## Slide 4: UL BW extension for A-PPDU
A-PPDU case 1: HE TB ( Primary 160MHz)+EHT TB (Secondary 160 MHz)
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
Non-HT
L-P+RL
SIG-A
Non-HT
Non-HT
Non-HT
trigger
Non-HT
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
L-P+RL
SIG-A
Secondary
160MHz
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Trigger frame
TB PPDU

## Slide 5: UL BW extension for A-PPDU
A-PPDU case 2: HE TB ( Primary 160MHz)+EHT TB (80MHz within Secondary 160 MHz)
  The location of 80 MHz for EHT TB is determined by RU allocation subfield
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
Non-HT
Non-HT
Non-HT
Non-HT
trigger
Non-HT
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Punctured 80MHz channel
Secondary
160MHz
Trigger frame
TB PPDU
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
L-P+RL
SIG-A
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
L-P+RL
SIG-A

## Slide 6: UL BW extension for A-PPDU
A-PPDU case 3: HE TB (80MHz within secondary 160 MHz)+EHT TB (secondary 160 MHz)
Non-HT
Non-HT
Non-HT
Primary
80MHz
Secondary
80MHz
trigger
Non-HT
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Secondary
160MHz
EHT M-BA
L-P+RL
L-P+RL
U-SIG
U-SIG
Non-HT
Non-HT
Non-HT
trigger
Non-HT
L-P+RL
L-P+RL
U-SIG
U-SIG
Trigger frame
TB PPDU
Punctured 80MHz channel
HE M-BA
L-P+RL
L-P+RL
L-P+RL
SIG-A
SIG-A
SIG-A
L-P+RL
SIG-A

## Slide 7: Other cases for UL BW extension
There are some controversial cases for UL BW extension as follows
  HE 80 + EHT 320
  HE 80 + EHT 80 (if these two 80 are in primary 80)
  Both of the above two cases have issue about preamble decoding for 160 capable legacy STAs as mentioned in[1]
  For HE 80 + EHT 80 if HE80 is in primary 160 MHz and EHT80 is in secondary 160 MHz and other two 80 MHz channels are punctured, this case could be TBD
  This case does not have preamble decoding issue. But the question is that only half of 320 MHz is occupied by TB PPDU.

## Slide 8: Summary
In this contribution, we propose to modify the UL BW extension field to support A- PPDU for R1 STA
UL BW (2 bits) | Bandwidth for HE TB PPDU, MHz | UL BW Extension (2 bits) | Bandwidth for EHT TB PPDU, MHz
0 | 20 | 0 | 20
0 | 20 | 1 | reserved
0 | 20 | 2 | reserved
0 | 20 | 3 | reserved
1 | 40 | 0 | 40
1 | 40 | 1 | reserved
1 | 40 | 2 | reserved
1 | 40 | 3 | reserved
2 | 80 | 0 | 80
2 | 80 | 1 | reserved 160
2 | 80 | 2 | reserved
2 | 80 | 3 | reserved
3 | 160 | 0 | reserved 80
3 | 160 | 1 | 160
3 | 160 | 2 | 320 -1
3 | 160 | 3 | 320-2

## Slide 9: References
[1] 11-20-1808-04-00be-backward-compatible-eht-trigger-frame-follow-up

## Slide 10: SP 1
Do you agree that R1 STA can participate trigger based A-PPDU transmission with R2 STA?

## Slide 11: SP 2
Do you agree to modify the UL BW extension field to support A- PPDU transmission for R1 STA
UL BW (2 bits) | Bandwidth for HE TB PPDU, MHz | UL BW Extension (2 bits) | Bandwidth for EHT TB PPDU, MHz
0 | 20 | 0 | 20
0 | 20 | 1 | reserved
0 | 20 | 2 | reserved
0 | 20 | 3 | reserved
1 | 40 | 0 | 40
1 | 40 | 1 | reserved
1 | 40 | 2 | reserved
1 | 40 | 3 | reserved
2 | 80 | 0 | 80
2 | 80 | 1 | reserved 160
2 | 80 | 2 | reserved
2 | 80 | 3 | reserved
3 | 160 | 0 | reserved 80
3 | 160 | 1 | 160
3 | 160 | 2 | 320 -1
3 | 160 | 3 | 320-2