## Slide 1: Release Indication In Capabilities for R2 Devices
Date: 2021-02-23
Authors:
Name | Affiliations | Address | Phone | email
Ruchen Duan | Samsung |  |  | r.duan@Samsung.com
Wook Bong Lee |  |  |  | wookbong.lee@samsung.com
Srinivas Kandala |  |  |  | srini.k1@samsung.com
Ravi Gidvani |  |  |  | ravi.gidvani@samsung.com
Jonghun Han |  |  |  | jong_hun.han@samsung.com
Chulho Chung |  |  |  | ch29.chung@samsung.com

## Slide 2: Background
802.11 be development is divided into release 1 and release 2
Release 2 AP will support both release 1 STA and release 2 STA
  Release 1 STA implements only 802.11 be release 1 features
  Release 2 STA implements both release 1 and 2 features
Potential R2 PHY features including
  APPDU
  SST
  EHT ER PPDU
  …

## Slide 3: Background
In release 1, EHT PPDU contains U-SIG with variations for MU and TB PPDU
Take the EHT MU PPDU U-SIG as an example, it contains Disregard bits from B20-B24 in U-SIG symbol 1, and contains Validate bits in B25 in U-SIG symbol 1 and B2 and B8 in U-SIG symbol 2.

## Slide 4: Background
The functionality of the Disregard bits and Validate bits are:
  Validate:
    If an EHT device encounters a PPDU where any of the Validate bits in the preamble are not set to the default values for those bits specified, or field values of any field in the EHT PHY preamble are set to a Validate state, it shall defer for the duration of the PPDU, pass the information in the version independent fields to MAC, and terminate the reception of the PPDU
  Disregard:
    If an EHT device sees Disregard bits set to any value, or field values of any field in the EHT PHY preamble are set to a Disregard state, it shall ignore these bits/states, and continue receiver processing subject to absence of any of the other Validate bits in the preamble being set to non-default values and any of the other fields in the preamble not being set to a Validate state.

## Slide 5: Possible Issue
In 802.11 release 2, the Validate and Disregard bits can be used for other features or be extended for existing features
With further definition, Validate bits will not be equal to default value
If release 2 STA send PPDU with release 2 U-SIG to release 1 STA
  R1 device may drop this PPDU
  R1 device may not be able to get the information in disregard bits
Communication between release 2 STA and release 1 STA breaks

## Slide 6: Possible Solution
Because this is a stable property of a device, we consider to use the EHT capabilities element to indicate the release version of the device.
Following 11ax design, the EHT Capabilities element can be

## Slide 7: Possible Solution
Introduce 1 bit in EHT Capabilities element to indicate the capability of using U-SIG Validate bits
In the future this bit may be overloaded into other purpose, e.g.
  Group indication of R2 mandatory features
  Support of conditional mandatory features

## Slide 8: SP
Do you agree to introduce 1 bit in EHT Capabilities element to indicate the capability of using U-SIG Validate bits