## Slide 1: Electrical reference points for 11bb
Date: 2021-02-26
Authors:

## Slide 2: Abstract
This presentation considers electrical reference points for the IEEE 802.11bb amendment as alternatives to the optical reference point proposed in IEEE 802.11-20/1962r0.

## Slide 3: Background
Early drafts of the 802.11bb amendment include a definition of ‘antenna port’ used as reference point for receiver minimum input sensitivity and other parameters
For light communications, we use an optical front end (OFE) in place of an electrical antenna and so the definition of antenna port seems inappropriate
Document IEEE 802.11-20/1962r0 proposed the surface of the optical receiver as the natural reference point for light communications
  optical sensitivity defined in terms of irradiance in units of W.m-2
The related discussion revealed it could take time to agree on numbers and get used to units
Alternative approach:
  Consider an electrical reference point for the specification
  Leave definition of irradiance to future consortium or special interest group
Optical port
Advantages:
  Always accessible;
  Takes into account OFE performance;
  Places no requirements on architecture of signal processing chain;
  Allows consistent testing for basic interoperability
  Captures dc level
Disadvantages:
  Inconsistency with other 802.11 PHYs;
    Unfamiliar units (W.m-2);
    No agreement on numbers;
  New test tools required

## Slide 4: Electrical reference points
Point A: Low frequency port
  16-336 MHz interface
  Electrical output of PD and amplification chain
Point A1: High frequency port
  2.4 or 5 GHz interface
  Used by implementations based on existing RF chipsets
Point A2: I&Q baseband port
  Available in chipsets that support multiple antennas
  Could be analogue or digital
General remarks
  Incoming signal is probably dc-blocked
    We cannot measure ambient light level
  Excludes OFE
    Levels at the output of the OFE are very dependent on optical and amplifier chain and mixer performance

## Slide 5: Point A: Low frequency port
The output of the PD and amplifier chain
Pros:
  Always present;
    Part of the basic OFE operation
  Consistent with RF antenna port specs therefore easy to specify;
  Familiar units (dBm);
  Could use existing test techniques
    modified for different frequency range
Cons:
  Not always physically accessible;
    Not implemented by 802.11 chipsets
  TIA conversion gain results in high output levels
    E.g., -18 dBm instead of -65 dBm for 64-QAM 3/4
    Gain is necessary for optimum noise performance
    Need new numbers consistent with output of the TIA
Modulation and rate | OFDM PHY RF min. rx sensitivity | Low frequency port min. rx sensitivity
BPSK 1/2 | -82 | -35
BPSK 3/4 | -81 | -34
QPSK 1/2 | -79 | -32
QPSK 3/4 | -77 | -30
16-QAM 1/2 | -74 | -27
16-QAM 3/4 | -70 | -23
64 QAM 2/3 | -66 | -19
64 QAM 3/4 | -65 | -18

## Slide 6: Point A1: High frequency port
The 2.4 GHz or 5 GHz (or 6 GHz) output of an up-conversion mixer
Pros:
  Available on-chip in up-conversion implementations;
  Consistent with RF antenna port specs;
    Use the same levels already specified in radio specs
  Can use existing test specs and tools
Cons:
  Requires up-conversion architecture;
  Port not present in future direct conversion implementations;
  Levels at output of up-conversion mixer likely to be significantly higher (e.g., -18 dBm) than existing specs require (e.g., -65 dBm for 64-QAM 3/4)
    Higher than receiver maximum input level of -30 dBm specified in 802.11
    Side-effect of levels required for up-conversion mixer
    >40 dB attenuator needed for consistency with input ports of 802.11 chip

## Slide 7: Point A2: I&Q baseband port
The true baseband interface
Pros:
  Always present;
  Available on-chip on some multi-antenna chipsets
Cons:
  Not specified in 802.11 for any PHY;
  Not always accessible;
  Physical implementation may be analogue or digital;
  Uncertain availability of test specs and test tools

## Slide 8: Summary
For this discussion, we exclude the optical and I&Q ports and focus on:
The low frequency port
  The easiest to specify
  But the ‘classic’ receiver sensitivity values don’t match what comes out of the TIA so we need to agree new values
  No chips will implement it in the short term, which implies testing will be difficult.
The high frequency port
  Will be used in the first implementations but has to remain optional
  Also has problems with matching the output levels of the up-conversion mixer so we need to consider new values or (implicitly) require attenuation
  Potentially more (e.g., LO frequencies) also needs to be specified here
Neither port is perfect
A possible specification approach for discussion:
Specify low frequency port as preferred and define appropriate dBm levels
Allow high frequency port as alternative and define additional requirements (LO frequencies, etc.) as necessary

## Slide 9: Thank you!