## Slide 1: Threshold based sensing measurement
Date: 2021-03-09
Authors:
Name | Affiliation | Address | Phone | Email
Yingxiang Sun | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | sunyingxiang@Huawei.com
Chenchen Liu |  |  |  | 
Rui Du |  |  |  | 
Meihong Zhang |  |  |  | 
Danny Kai Pin Tan |  |  |  | 

## Slide 2: Abstract
By following up [1], the potential procedure of threshold based sensing measurement (TBSM) is proposed in this contribution, which has several benefits for sensing.
The potential TBSM procedure is composed of the setup phase, the measurement phase, and the feedback phase.

## Slide 3: Outline
Background of WLAN sensing
Threshold based sensing measurement (TBSM) procedure
  Setup phase
  Measurement phase
  Feedback phase
Summary
References
SP

## Slide 4: Background of WLAN sensing
Sensing based on channel sounding
Explicit feedback
Implicit feedback
Channel changes sometimes play the most import role
Some typical use cases only track changes over time
Regularity
Some use cases like intruder detection might need a regular CSI feedback
Most of the feedbacks over a period may be highly correlated
Intruder detection
Fall detection
Gesture recognition
An example of configuration [1]

## Slide 5: Threshold based sensing measurement (TBSM) procedure
Overview
The TBSM procedure allows a STA to determine the sensing measurement from another STA. By referring to [2]-[4], it could be composed of three phases: the setup phase, the measurement phase, and the feedback phase.
In the setup phase, the sensing initiator (referred to as the ISTA) and the sensing responders (referred to as the RSTAs) that participate the TBSM are determined.
In the measurement phase, CSI measurements are performed.
In the feedback phase, the currently measured CSI is compared with the previously measured CSI, if the CSI variation meets the feedback threshold criterion, the sensing responders will send the feedback to the sensing initiator.
Note: Feedback thresholds configuration could be conducted in the setup phase by ISMR, or in the measurement phase by NDPA.
Need further discussion.

## Slide 6: Setup phase
Initial sensing measurement request (ISMR)
A sensing initiator (referred to as an ISTA) regularly sends the ISMR to a sensing responder (referred to as a RSTA) that associated with it
If the RSTA is available, then it will response and join the TBSM procedure
Otherwise, the RSAT will not response and will not join the TBSM procedure

## Slide 7: Measurement phase
CSI measurement
The ISTA regularly sends NDPAs and NDPs to the associated RSTAs
The RSTAs conduct CSI measurement after receiving the NDPs sent by the ISTA

## Slide 8: Feedback phase (1/3)
Feedback criterion
The feedback criterion could be ΔCSI ≥ ΔCSI_th or ΔCSI ≤ΔCSI_th, depending on the measure that quantitatively evaluate ΔCSI, where the CSI variation ΔCSI is the difference between the current CSI and the previous CSI, ΔCSI_th is the threshold of the CSI variation.
For example, ΔCSI could be evaluated by time-reversal resonating strength (TRRS) [5]. The TRSS is more robust compared to conventional correlation coefficients, since it takes the maximum value of the correlation coefficents.
Note：Two optional thresholds could also be set as feedback requirements:
The threshold of the number of channel changes Nch_th : can adjust how often to feed back when channel changes
The threshold of the number of channel measurement Nmea_th : can avoid the case that no response in a long period of time

## Slide 9: Feedback phase (2/3)
Feedback request
The ISTA regularly sends feedback requests to the RSTAs. The RSTAs will compare ΔCSI with ΔCSI_th and check if the feedback criterion is met, then decide if perform feedback.
The current CSI would be stored in the RSTAs and be used to compare with the result of CSI measurement performed next time.
Some other information also could be stored depending on need, e.g., the final result(referred to the final information that need to know, such as range, velocity, angle, and etc.), the compressed CSI (might be the compressed beamforming feedback matrix or the compressed matrix by other compressing methods), and etc.
The RSTAs would feed back the NDP or the CSI or the compressed CSI or the final result.
Note：The type of feedback shall be decided by the initiator

## Slide 10: Feedback phase (3/3)
The ISTA will perform one of the following operations depending on the feedback sent from the RSTAs
If the feedback is NDP, then the ISTA performs sensing measurement if needed.
If the feedback is the final result of sensing, then no further computing is needed.
If the feedback is the CSI, then the ISTA performs some subsequent computing based on the CSI if needed.
If the feedback is the compressed CSI, then the ISTA reconstructs the CSI and performs some subsequent computing based on the reconstructed CSI if needed.
Note：The type of feedback shall be decided by the initiator

## Slide 11: Threshold based sensing measurement (TBSM) Benefits
Benefits
Reduce the overhead of feedback
Reduce the number of feedbacks from the RSTA to the ISTA, by configuring the threshold of CSI variation ΔCSI_th
Reduce the payload of feedback every time, by sending NDP or compressed CSI
Quantitatively evaluate the CSI variation
Threshold evaluation algorithms, such as time-reversal resonating strength (TRRS)
Adjust how often to feed back when channel changes, if needed
By configuring the threshold of the number of channel changes Nch_th
Avoid the case that no response in a long period of time
By configuring the threshold of the number of channel measurement Nmea_th

## Slide 12: Summary
The threshold based sensing measurement (TBSM) procedure that can benefit the WLAN sensing is proposed and discussed.
The potential three phases of the procedure could be the negotiation phase, the measurement phase, and the feedback phase.

## Slide 13: References
[1] 11-20-1120-01-SENS-follow-ups-on-channel-measurement-procedure-for-wlan-sensing.
[2] 11-21-0147-03-00bf-Definitions-and-scenarios-of-the-WLAN-sensing-follow-ups.
[3] 11-20-1851-01-00bf-Overview-of-Wi-Fi-sensing-protocol.
[4] 11-21-0370-00-00bf-considerations-of-sensing-negotiation.
[5] Z. Wu, Y. Han, Y. Chen and K. J. R. Liu, "A Time-Reversal Paradigm for Indoor Positioning System," in IEEE Transactions on Vehicular Technology, vol. 64, no. 4, pp. 1331-1339, April 2015.
Yingxiang Sun (Huawei)

## Slide 14: Straw Poll 1
Do you agree that 11bf shall consider the proposed threshold based sensing measurement (TBSM)?

## Slide 15: Straw Poll 2
Do you agree that 11bf shall consider the following threshold based feedback?
The current measured CSI would be compared with the previous measured CSI. The difference between them, namely, CSI variation, can be calculated.
A threshold could be configured as the feedback criterion, which could determine if feedback would be performed.
By the comparing the CSI variation with the threshold, the sensing responders would send the feedback to the sensing initiator if the feedback criterion is met.