## Slide 1: Threshold based sensing measurement
Date: 2021-04-02
Authors:
Name | Affiliation | Address | Phone | Email
Yingxiang Sun | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | sunyingxiang@Huawei.com
Chenchen Liu |  |  |  | 
Rui Du |  |  |  | 
Meihong Zhang |  |  |  | 
Danny Kai Pin Tan |  |  |  | 
Mengshi Hu |  |  |  | 

## Slide 2: Abstract
By following up [1], the potential procedure of threshold based sensing measurement (TBSM) is proposed in this contribution, which has several benefits for sensing.
The potential TBSM procedure is composed of the setup phase, the measurement phase, and the feedback phase.

## Slide 3: Outline
Background of WLAN sensing
Threshold based sensing measurement (TBSM) procedure
  Setup phase
  Measurement phase
  Reporting phase
  Termination phase
Summary
References
SP

## Slide 4: Background of WLAN sensing
Sensing based on channel sounding
Explicit feedback
Implicit feedback
Channel changes sometimes play the most important role
Some typical use cases only track changes over time
Regularity
Some use cases like intruder detection might need a regular CSI feedback
Most of the feedbacks over a period may be highly correlated
Intruder detection
Fall detection
Gesture recognition
An example of configuration [1]

## Slide 5: Threshold based sensing measurement (TBSM) procedure
Overview
The TBSM procedure allows a STA to determine the sensing measurement from another STA. By referring to [2]-[4], it could be composed of four phases: the setup phase, the measurement phase, the reporting phase, and the termination phase.
In the setup phase, the sensing initiator (referred to as the ISTA) and the sensing responders (referred to as the RSTAs) that participate the TBSM are determined.
In the measurement phase, CSI measurements are performed.
In the reporting phase, if the CSI variation meets the feedback threshold criterion, the sensing responders will send ACK, then the feedback will be triggered and be sent to the sensing initiator.
In the termination phase, the sensing session is terminated.
Note:
1. Feedback thresholds configuration could be performed in the setup phase by ISMR, or in the measurement phase by NDPA.
2. The comparison between the current measured CSI and the previous measured CSI could be performed in the measurement phase, or in the feedback phase. The same goes for the comparison between the CSI variation and the feedback threshold.

## Slide 6: Setup phase
Initial sensing measurement request (ISMR)
A sensing initiator (referred to as an ISTA) regularly sends the ISMR to the sensing responders (referred to as the RSTAs) associated with it
If a RSTA is available, then it will response and join the TBSM procedure
Otherwise, the RSTA will not response and will not join the TBSM procedure

## Slide 7: Measurement phase
CSI measurement
The ISTA regularly sends NDPAs and NDPs to the associated RSTAs
The RSTAs perform CSI measurements after receiving the NDPs sent by the ISTA

## Slide 8: Reporting phase (1/3)
Feedback criterion
The feedback criterion could be ΔCSI ≥ ΔCSI_th or ΔCSI ≤ΔCSI_th, depending on the measurement that quantitatively evaluate ΔCSI, where the CSI variation ΔCSI is the difference between the current CSI and the previous CSI, ΔCSI_th is the threshold of CSI variation.
For example, ΔCSI could be evaluated by time-reversal resonating strength (TRRS) [5]. The TRSS is more robust compared to conventional correlation coefficients, since it takes the maximum value of the correlation coefficients.
Note：Two optional thresholds could also be set as feedback criterion:
1. The threshold of the number of channel changes Nch_th : we may hope a RSTA sends the measurement results from multiple channel changes at one time, the threshold can adjust how often the feedback happens.
2. The threshold of the number of channel measurement Nmea_th : enables regularly feedback in a period of time regardless of the feedback criterion satisfied, the threshold can help to avoid the case that no response in a long period of time.

## Slide 9: Reporting phase (2/3)
Feedback request and feedback trigger
The ISTA regularly sends feedback requests to the RSTAs. The RSTAs that meet the feedback criterion will send ACK to indicate they will perform feedback. Then the ISTA will trigger the RSTAs those are with feedback intention to perform feedback.
The current measured CSI would be stored to compare with the result of CSI measurement performed next time.
Some other information could be stored depending on need, e.g., the final result(referred to the final information that need to know, such as range, velocity, angle, and etc.), the compressed CSI (might be the compressed beamforming feedback matrix or the compressed matrix by other compressing methods), and etc.
The RSTAs would feed back the NDP or the CSI or the compressed CSI or the final result.
Note：The type of feedback shall be decided by the initiator.

## Slide 10: Reporting phase (3/3)
The ISTA will perform one of the following operations depending on the feedback sent from the RSTAs
If the feedback is NDP, the ISTA performs sensing measurement if needed.
If the feedback is the final result of sensing, no further computing is needed.
If the feedback is the CSI, the ISTA performs some subsequent computing based on the CSI if needed.
If the feedback is the compressed CSI, the ISTA reconstructs the CSI and then performs some subsequent computing based on the reconstructed CSI if needed.
Note：The type of feedback shall be decided by the initiator

## Slide 11: Threshold based sensing measurement (TBSM) Benefits
Benefits
Reduce the overhead of feedback
Reduce the number of feedbacks from the RSTA to the ISTA, by configuring the threshold of CSI variation ΔCSI_th
Reduce the payload of feedback every time, by sending NDP or compressed CSI
Quantitatively evaluate the CSI variation
By some evaluation criterion, such as time-reversal resonating strength (TRRS)
Adjust how often to feed back when channel changes, if needed
By configuring the threshold of the number of channel changes Nch_th
Avoid the case that no response in a long period of time
By configuring the threshold of the number of channel measurement Nmea_th

## Slide 12: Summary
The threshold based sensing measurement (TBSM) procedure that can benefit the WLAN sensing is proposed and discussed.
The potential three phases of the procedure could be the negotiation phase, the measurement phase, and the feedback phase.

## Slide 13: References
[1] 11-20-1120-01-SENS-follow-ups-on-channel-measurement-procedure-for-wlan-sensing.
[2] 11-21-0147-03-00bf-Definitions-and-scenarios-of-the-WLAN-sensing-follow-ups.
[3] 11-20-1851-04-00bf-Overview-of-Wi-Fi-sensing-protocol.
[4] 11-21-0370-00-00bf-considerations-of-sensing-negotiation.
[5] Z. Wu, Y. Han, Y. Chen and K. J. R. Liu, "A Time-Reversal Paradigm for Indoor Positioning System," in IEEE Transactions on Vehicular Technology, vol. 64, no. 4, pp. 1331-1339, April 2015.
Yingxiang Sun (Huawei)

## Slide 14: Straw Poll
Do you agree that 11bf could consider the following threshold based feedback in the proposed threshold based sensing measurement (TBSM)?
The current measured CSI would be compared with the previous measured CSI. The difference between them, namely, CSI variation, can be quantifiable.
A threshold could be configured as one of the feedback criterion, which could determine if feedback would be performed.
By comparing the CSI variation with the threshold, the sensing responders would send the feedback to the sensing initiator if the feedback criteria is met.

## Slide 15: Motion
Move to add the following to 11bf SFD:
The 11bf amendment defines a threshold-based procedure for the reporting phase in which
The current measured CSI would be compared with the previous measured CSI. The difference between them, namely, CSI variation, can be quantifiable.
A threshold could be configured as one of the feedback criterion, which could determine if feedback would be performed.
By comparing the CSI variation with the threshold, the sensing responders would send the feedback to the sensing initiator if the feedback criteria is met.
  Move: Yingxiang Sun Second:
  Result:
  Note： Related document 21/0351r3

## Slide 16: Response(1/3)
Q1: I see that there could be a cost in terms of memory requirements needed. I believe it could be a capability and that this could be an optional feature.
A1: The memory that would be taken by the CSI matrix could be calculated according to the 9.4.1.27 CSI Report field in IEEE P802.11-REVme/D0.0, March 2021.
The Size of CSI matrix for each carrier is (2×Nb×Nc×Nr)
The Coefficient Size indicates the number of bits in the representation of the real and imaginary parts of each element in the matrix. We assume that Nb takes the maximum value as 8. We assume that there are 8 streams for Nc and 8 receivers for Nr.
If no grouping is applied, there is 56 subcarriers for 20MHz, therefore, the size of the CSI matrix could be calculated as Ns×(2×Nb×Nc×Nr) = 56×(2×8×8×8) = 57344bits = 7168Bytes = 7MB.
Nb: is the number of bits determined by the Coefficients Size field of the MIMO Control field
Nc: is the number of columns in a CSI matrix determined by the Nc index field of the MIMO Control field
Nr: is the number of rows in a CSI matrix determined by the Nr Index field of the MIMO Control field

## Slide 17: Response(2/3)
The evaluation results are summarized in Table I.
Ng： is the number of adjacent subcarriers for each group
Ns： is the number of subcarriers sent
Table I
Q2: I see some merits, but I have some question about implementation. Also, it is not clear to me how to distinguish between something not been sent and something being sent but not being received.
A2: Firstly, the regular reporting in this contribution can partially address this issue. Secondly, if the CSI variation meets the feedback threshold criterion, the sensing responders will send ACK, then the feedback will be triggered and be sent to the sensing initiator, the procedure can also help to address this issue.
BW | Ng | Ns | Nb | Nc | Nr | Size(bit) | Size(MB)
20MHz | 1 | 56 | 8 | 8 | 8 | 57344 | 7
20MHz | 2 | 30 | 8 | 8 | 8 | 30720 | 3.75
20MHz | 4 | 16 | 8 | 8 | 8 | 16384 | 2
40MHz | 1 | 114 | 8 | 8 | 8 | 116736 | 14.25
40MHz | 2 | 58 | 8 | 8 | 8 | 59392 | 7.25
40MHz | 4 | 30 | 8 | 8 | 8 | 30720 | 3.75

## Slide 18: Response(3/3)
Q3: On slide 8, when do you plan to submit the report in the timeline? In what order? At the same time?
A3: I believe several options are possible. RSTAs could submit the report either in sequential order or in parallel order.
Q4: If you allocate time slots for feedback, it seems you are still wasting the resources even if no sensing report is sent.
A4: The resources would not be wasted. If the CSI variation meets the feedback threshold criterion, the sensing responders will send ACK, then the feedback will be triggered and be sent to the sensing initiator. It should be noted that, compared to the way that RSTAs send feedback after every single sensing measurement, the resources would have been already significantly preserved.
Q5: Do you suggest to have the actual formulas in the specification? Usually we don’t have these details in the specification.
A5: I would suggest to have the actual formulas in the specification, so that we could evaluate the CSI variation under the same criterion. However, we could have future discussion for the details.