## Slide 1: Threshold Based Sensing Measurement
Date: 2021-04-02
Authors:
Name | Affiliation | Address | Phone | Email
Yingxiang Sun | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | sunyingxiang@Huawei.com
Mengshi Hu |  |  |  | humengshi@Huawei.com
Chenchen Liu |  |  |  | 
Rui Du |  |  |  | 
Meihong Zhang |  |  |  | 
Danny Kai Pin Tan |  |  |  | 

## Slide 2: Abstract
On the basis of [1], the potential procedure of threshold based sensing measurement (TBSM) is proposed in this contribution, which has several benefits for sensing.
No need for a sensing receiver to feed back the CSI all the times.
The CSI can be fed back by a sensing receiver when the CSI variation becomes large.
A threshold can be added to describe whether the CSI variation is large enough.

## Slide 3: Background of WLAN Sensing
Sensing based on channel sounding
Explicit feedback
Implicit feedback
Channel changes sometimes play the most important role
Some typical use cases track channel changes:
Regularity
Some use cases like intruder detection might need a regular CSI feedback.
Most of the feedbacks over a period may be highly correlated.
Note:
Sensing transmitter: a STA that transmits PPDUs used for sensing measurements in a sensing session
Sensing receiver: a STA that receives PPDUs sent by a sensing transmitter and performs sensing measurements in a sensing session
Intruder detection
Fall detection
Gesture recognition
An example of configuration [1]

## Slide 4: Threshold Based Sensing Measurement (TBSM) Procedure
The TBSM procedure allows a STA to determine the sensing measurement from other STAs. Referring to [2]-[4], it could be composed of the following four phases:
Setup phase: the sensing transmitter and the sensing receivers that participate the TBSM are determined.
Measurement phase: CSI measurements are performed.
Reporting phase: if the CSI variation meets the feedback threshold criterion, the sensing receivers will send ACK, then the feedback will be triggered and be sent to the sensing transmitter.
Termination phase: the sensing session is terminated.
Note:
1. Feedback thresholds configuration could be performed in the setup phase, or in the measurement phase.
2. The comparison between the current measured CSI and the previous measured CSI could be performed in the measurement phase, or in the feedback phase. The same goes for the comparison between the CSI variation and the feedback threshold.

## Slide 5: Measurement phase
CSI measurement
The sensing transmitter regularly sends NDPAs and NDPs to the sensing receivers
The sensing receivers perform CSI measurements after receiving the NDPs sent by the sensing transmitter.

## Slide 6: Reporting phase (1/3)
Feedback criterion
The feedback criterion could be ΔCSI ≥ ΔCSI_th or ΔCSI ≤ΔCSI_th, depending on the measurement that quantitatively evaluate ΔCSI, where the CSI variation ΔCSI is the difference between the current CSI and the previous CSI, ΔCSI_th is the threshold of CSI variation.
For example, ΔCSI could be evaluated by time-reversal resonating strength (TRRS) [5]. The TRRS is more robust compared to conventional correlation coefficients, since it takes the maximum value of the correlation coefficients.
Note：Two optional thresholds could also be set as feedback criterion:
1. The threshold of the number of channel changes Nch_th : we may hope a sensing receiver sends the measurement results from multiple channel changes at one time, the threshold can adjust how often the feedback happens.
2. The threshold of the number of channel measurement Nmea_th : enables regularly feedback in a period of time regardless of the feedback criterion satisfied, the threshold can help to avoid the case that no response in a long period of time.

## Slide 7: Reporting phase (2/3)
Feedback request and feedback trigger
The sensing receiver regularly sends feedback requests to the sensing transmitter. The sensing receiver that meets the feedback criterion will send ACK to indicate they will perform feedback. Then the sensing transmitter will trigger the sensing receivers those are with the feedback intention to perform feedback.
The current measured CSI would be stored to compare with the result of CSI measurement performed next time.
Some other information could be stored depending on need, e.g., the final result(referred to the final information that need to know, such as range, velocity, angle, and etc.), the compressed CSI (might be the compressed beamforming feedback matrix or the compressed matrix by other compressing methods), and etc.
The sensing receiver would feed back the NDP or the CSI or the compressed CSI or the final result.

## Slide 8: Reporting phase (3/3)
The sensing transmitter will perform one of the following operations depending on the feedback sent from the sensing receivers:
If the feedback is NDP, the sensing transmitter performs sensing measurement if needed.
If the feedback is the final result of sensing, no further computing is needed.
If the feedback is the CSI, the sensing transmitter performs some subsequent computing based on the CSI if needed.
If the feedback is the compressed CSI, the sensing transmitter reconstructs the CSI and then performs some subsequent computing based on the reconstructed CSI if needed.

## Slide 9: Threshold Based Sensing Measurement (TBSM) Benefits
Benefits
Reduce the overhead of feedback
Reduce the number of feedbacks from the sensing receiver to the sensing transmitter, by configuring the threshold of CSI variation ΔCSI_th
Reduce the payload of feedback every time, by sending NDP or compressed CSI
Quantitatively evaluate the CSI variation
By some evaluation criterion, such as time-reversal resonating strength (TRRS)
Adjust how often to feed back when channel changes, if needed
By configuring the threshold of the number of channel changes Nch_th
Avoid the case that no response in a long period of time
By configuring the threshold of the number of channel measurement Nmea_th

## Slide 10: Summary
To reduce overhead, potential procedures of Threshold Based Sensing Measurement (TBSM) was discussed.
No need for a sensing receiver to feed back the CSI all the times.
The CSI can be fed back by a sensing receiver when the CSI variation becomes large.
A Threshold can be added to describe whether the CSI variation is large enough.

## Slide 11: References
[1] 11-20-1120-01-SENS-follow-ups-on-channel-measurement-procedure-for-wlan-sensing.
[2] 11-21-0147-03-00bf-Definitions-and-scenarios-of-the-WLAN-sensing-follow-ups.
[3] 11-20-1851-04-00bf-Overview-of-Wi-Fi-sensing-protocol.
[4] 11-21-0370-00-00bf-considerations-of-sensing-negotiation.
[5] Z. Wu, Y. Han, Y. Chen and K. J. R. Liu, A Time-Reversal Paradigm for Indoor Positioning System,
in IEEE Transactions on Vehicular Technology, vol. 64, no. 4, pp. 1331-1339, April 2015.
Yingxiang Sun (Huawei)

## Slide 12: Straw Poll
Do you agree that 11bf could consider the following threshold based feedback in the proposed threshold based sensing measurement (TBSM)?
The difference between the current measured CSI and the previous measured CSI is quantified. The difference is referred to as CSI variation.
A threshold value to be used by the sensing receiver in the threshold based procedure is defined.
By comparing the CSI variation with the threshold, the sensing receiver can send a feedback resulting from the large CSI variation to the sensing transmitter
Whether the threshold is predefined, or defined by the sensing receiver, transmitter, initiator or responder is TBD.

## Slide 13: Motion
Move to add the following to 11bf SFD:
The 11bf amendment defines a threshold-based procedure in which
The difference between the current measured CSI and the previous measured CSI is quantified. The difference is referred to as CSI variation.
A threshold value to be used by the sensing receiver in the threshold based procedure is defined.
By comparing the CSI variation with the threshold, the sensing receiver can send a feedback resulting from the large CSI variation to the sensing transmitter.
Whether the threshold is predefined, or defined by the sensing receiver, transmitter, initiator or responder is TBD.
  Move: Second:
  Result:
  Note： Related document 21/0351r4

## Slide 14: Response(1/3)
Q1: I see that there could be a cost in terms of memory requirements needed. I believe it could be a capability and that this could be an optional feature.
A1: The memory that would be taken by the CSI matrix could be calculated according to the 9.4.1.27 CSI Report field in IEEE P802.11-REVme/D0.0, March 2021.
The size of CSI matrix for each carrier is (2×Nb×Nc×Nr) bits
The size of the CSI Report field is Nr8+Ns(3+2NbNcNr) bits
Nb: is the number of bits determined by the Coefficients Size field of the MIMO Control field (Indicates the number of bits in the representation of the real and imaginary parts of each element in the matrix)
Nc: is the number of columns in a CSI matrix determined by the Nc index field of the MIMO Control field
Nr: is the number of rows in a CSI matrix determined by the Nr Index field of the MIMO Control field
Ng： of carriers grouped into one
Ns： is the number of subcarriers sent
BW | Ng | Ns | Nb | Nc | Nr | Size (bit) | Size (KB)
20MHz | 1 | 56 | 8 | 8 | 8 | 57344 | 7.00
20MHz | 2 | 30 | 8 | 8 | 8 | 30720 | 3.75
20MHz | 4 | 16 | 8 | 8 | 8 | 16384 | 2.00
40MHz | 1 | 114 | 8 | 8 | 8 | 116736 | 14.25
40MHz | 2 | 58 | 8 | 8 | 8 | 59392 | 7.25
40MHz | 4 | 30 | 8 | 8 | 8 | 30720 | 3.75
The evaluation results are summarized in the following table:

## Slide 15: Response(2/3)
Q2: I see some merits, but I have some question about implementation. Also, it is not clear to me how to distinguish between something not been sent and something being sent but not being received.
A2: Firstly, the regular reporting in this contribution can partially address this issue. Secondly, if the CSI variation meets the feedback threshold criterion, the sensing receivers will send ACK, then the feedback will be triggered and be sent to the sensing transmitter, the procedure can also help to address this issue.
Q3: When do you plan to submit the report in the timeline? In what order? At the same time?
A3: I believe several options are possible. Receivers could submit the report either in sequential order or in parallel order.

## Slide 16: Response(3/3)
Q4: If you allocate time slots for feedback, it seems you are still wasting the resources even if no sensing report is sent.
A4: The resources would not be wasted. If the CSI variation meets the feedback threshold criterion, the sensing receivers will send ACK, then the feedback will be triggered and be sent to the sensing initiator. It should be noted that, compared to the way that sensing receivers send the feedback after every single sensing measurement, the resources would have been already significantly preserved.
Q5: Do you suggest to have the actual formulas in the specification? Usually we don’t have these details in the specification.
A5: I would suggest to have the actual formulas in the specification, so that we could evaluate the CSI variation under the same criterion. However, we could have future discussion for the details.