## Slide 1: Comparison of FTM and sensing procedure
Date: 2021-03-04
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Claudio da Silva |  |  |  | claudio.da.silva@intel.com
Bahareh Sadeghi |  |  |  | bahareh.sadeghi@intel.com
Carlos Cordeiro |  |  |  | carlos.cordeiro@intel.com
Notes: September 2012

## Slide 2: Abstract
A great overview of FTM procedure was presented in [1].
In this contribution, we provide some preliminary analysis of comparison between FTM and sensing procedure.
  Based on the analysis, we can then initiate discussions on whether we want to reuse FTM protocol in sensing, and if so, what changes need to be done to accommodate the differences.

## Slide 3: Main recap of FTM procedure
The FTM procedure allows a STA to determine its range, relative range and its direction to or from another STA.
  Both sub-7 GHz and 60 GHz are supported.
An FTM session is an instance of an FTM procedure between an ISTA and an RSTA along with the associated scheduling and operational parameters.
An FTM session is composed of a negotiation, measurement exchange and termination.
  Multiple mechanisms are defined, including EDCA based ranging, TB ranging, non-TB ranging etc.
Pre-Association Security Negotiation (PASN) is defined to enable a secured mode that provides Authentication, Key Management, Encryption, and Message Integrity in unassociated state.

## Slide 4: Some low hanging fruit
The overall procedure flow for sensing is similar to FTM, including negotiation, measurement, and termination.
  Negotiation: We can define a similar request/response frame exchange process, with a new Sensing Request/Response frame and new information elements containing the information needed for exchange.
  Measurement: For the sub-7 GHz, reusing the NDP packets to perform sensing measurement is a good choice. For the 60 GHz, we can use the TRN fields.
  Termination: Implicit termination can be defined similarly after the last negotiated burst instance. Explicit termination need separate signaling.
The PASN protocol can be reused to address scenarios where members of a sensing session are not in associated state.

## Slide 5: Tricky parts
Although FTM and sensing procedures share lots of similarities, which makes it attractive to reuse the FTM protocol for sensing, there are several major differences that need to be considered carefully.

## Slide 6: Initiator
In FTM procedure, even though the spec does not explicitly restrict an AP STA to become an initiator, in a typical scenario the ISTA is a non-AP STA, the RSTA is an AP STA.
  RSTA, which is typically an AP STA, therefore provides scheduling, protection, and time synchronization.
However, for sensing, both non-AP STA and AP STA can initiate a sensing session, and both have its typical use cases.
  So it is not necessarily that the RSTA provides scheduling, protection, and time synchronization.

## Slide 7: Responder
In FTM procedure, one sensing session is always between one initiator and one responder.
However, for sensing, there may be multiple responders in one sensing session.
  To achieve collaborative sensing [4][5][6].

## Slide 8: Bidirectional vs. unidirectional measurement
In FTM procedure, in order to get the RTT, both ISTA and RSTA are required to send PPDUs to the other, so there is always bidirectional measurement.
  FTM and Ack for EDCA based ranging measurement exchange.
  I2R NDP and R2I NDP for TB and Non-TB ranging measurement exchange.
However, when performing sensing measurement, we may only need unidirectional PPDUs sent from the transmitters to receivers to perform sensing.
  During the measurement phase, sensing receivers do not need to send sensing PPDUs to transmitters.
  This also helps with reducing the flow overhead.

## Slide 9: Bidirectional measurement in FTM
EDCA based ranging measurement exchange
TB ranging measurement exchange
Non-TB ranging measurement exchange

## Slide 10: Measurement reporting
In FTM, R2I measurement reporting is always there.
  In EDCA based ranging, measurement reporting is included in the FTM frame sent from the RSTA to the ISTA.
  In TB and Non-TB ranging, measurement reporting is included in mandatory R2I LMR and optional I2R LMR.
However, in sensing, measurement reporting may be implicit if the STA who wants sensing measurement result is acting as the sensing receiver.
  In this case, the STA already obtains the sensing measurement result itself, no further need for explicit reporting to other STAs.

## Slide 11: Measurement reporting in FTM
EDCA based ranging measurement exchange
TB ranging measurement exchange
Non-TB ranging measurement exchange

## Slide 12: Conclusions
In this contribution we presented some preliminary analysis of comparison between FTM and sensing procedure.
We think we can reuse relevant aspects from FTM, and meanwhile redesign aspects that is not applicable to sensing.

## Slide 13: References
[1] DCN 032r1, Comparison of the SENS Approaches
[2] IEEE REVmd D5.0
[3] IEEE 11az D3.0
[4] DCN 145r4, Collaborative WLAN Sensing – Follow Ups
[5] DCN 1533r0, Collaborative WLAN Sensing
[6] DCN 1416r0, Wi-Fi sensing: Cooperation and standard support