## Slide 1: PE for 4K QAM
Date: 2021-03-08
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com
Srinath Puducheri | Broadcom |  |  | 

## Slide 2: Discussion
11be supports up to 20uS for 4K QAM over large RU (as part of new 11be rates that are not part of 11ax)
However for small size RU the current PE is limited to 0uS which requires a big gap in the processing of 4K QAM  propose to enable PE for 4K QAM over small RU as well
Proposal:
  Propose to use RU242 nominal packet padding if “EHT PPE Thresholds present = 1”
  Propose to use EHT Common Nominal Packet Padding if “EHT PPE Thresholds present = 0”

## Slide 3: SP #1
Do you support that for 4K QAM over small RU
  Propose to use RU242 nominal packet padding if “EHT PPE Thresholds present = 1”
  Use EHT Common Nominal Packet Padding if “EHT PPE Thresholds present = 0”