## Slide 1: MLO: Broadcast TWT for MLDs
Date: 2021-03-05
Authors:

## Slide 2: Abstract
In this contribution, we propose the facilitation of broadcast TWT operation for multi-link devices.

## Slide 3: Background
Broadcast TWT operation enables an AP to set up a shared TWT session for a group of STAs [1], [2]
  Allows an AP to manage activity in the BSS
  Minimize contention between STAs, minimize STAs’ awake time
For MLDs, individual TWT operation could be set up on a setup link for more than one setup links [Motion 115, #SP60].
In this contribution, we address the broadcast TWT operation for multi-link devices (MLDs)

## Slide 4: Motivation
With broadcast TWT for MLDs, the non-AP MLD can become a member of a particular TWT schedule where the TWT service period (SP) across multiple links are aligned.
  In terms of traffic flow, the AP MLD/non-AP MLD can be benefitted from this SP alignment (more on this on the next slide)
In addition, multiple MLDs can also become members of the same broadcast TWT schedule.

## Slide 5: Motivation
Latency-sensitive traffic can be bursty and periodic
If there is a latency-sensitive TID, the non-AP MLD may want to map the TID to more than one (or all) setup links.
  For the latency-sensitive TID, STAs affiliated with the non-AP MLD may want to wake up at the same time so that the traffic corresponding to the latency-sensitive TID can flow over all the enabled links
  This will increase the channel access opportunity for latency-sensitive flow
  Reduced contention for latency-sensitive flow
In such scenario, the non-AP MLD shall be benefitted if it becomes a member of a TWT schedule which can be aligned across multiple (or all) enabled links.
  Based on the TSF timer values for all links, AP MLD shall align the wake time for that schedule across multiple links.
In the Broadcast TWT announcement, AP MLD may indicate which schedule can be aligned across multiple links
  The non-AP MLD can accordingly choose to become a member of that aligned schedule for frame exchange for latency-sensitive flow.
STA1
MAC-SAP
STA2
STA3
bTWT Schedule A
bTWT Schedule A
bTWT Schedule A
Latency-sensitive Traffic
STA1
MAC-SAP
STA2
STA3
bTWT Schedule B
Latency-tolerant Traffic
Doze
Doze

## Slide 6: Broadcast TWT for MLDs (1/5)
An MLD in a BSS may support broadcast TWT operation
  TWT service period (SP) for any MLD supporting TWT operation can be either trigger-based or non-trigger based
  A non-AP MLD may provide its broadcast TWT operation capabilities during ML setup
When broadcast TWT is supported by both AP MLD and non-AP MLD, an STA affiliated with the non-AP MLD may receive the Beacon frame containing the broadcast TWT element from an AP affiliated with an AP MLD on any link.
  The STA affiliated with the non-AP MLD on the link wakes up to receive the beacon frame and determines the starting time of the broadcast TWT SP.

## Slide 7: Broadcast TWT for MLDs (2/5)
For Broadcast TWT operation for MLDs, there is a TWT schedule, namely Aligned Schedule.
  Aligned Schedule: An Aligned schedule is defined as a Broadcast TWT schedule that shall be aligned across multiple links between the AP MLD and the non-AP MLD.
When the AP MLD announces Broadcast TWT schedules, it shall indicate whether or not a particular Broadcast TWT schedule (corresponding to Broadcast TWT Parameter Set) is an Aligned schedule.
Similarly, when non-AP MLD requests, suggests, or demands Broadcast TWT schedule for any link, it can also indicate whether or not it wants the requested, suggested, or demanded Broadcast TWT schedules to be aligned across multiple setup links.
The Aligned Schedule can be applied to any subset of links between the AP MLD and non-AP MLD.

## Slide 8: Broadcast TWT for MLDs (3/5)
In this illustrative example, three links are set up between the AP MLD and non-AP MLD-A. Also, three links are set up between the AP MLD and non-AP MLD-B. Both AP MLD and non-AP MLDs support broadcast TWT operation. A broadcast TWT negotiation takes place between AP1 of AP MLD and STA1 of non-AP MLD-A. Similarly, another TWT negotiation takes place between AP1 of AP MLD and STA1 of non-AP MLD-B. After successful negotiation, same broadcast TWT agreement is established between AP1 of AP MLD and STA1 of non-AP MLD-A, AP1 of AP MLD and STA1 of non-AP MLD-B.
AP1
AP2
AP3
STA1
STA2
STA3
  Broadcast TWT negotiation
  AP MLD
  non-AP MLD-A
STA1
STA2
STA3
  non-AP MLD-B
AP1
AP2
AP3
STA1
STA2
STA3
  AP MLD
STA1
STA2
STA3
  non-AP MLD-B
  Broadcast TWT
  agreement
  non-AP MLD-A

## Slide 9: Broadcast TWT for MLDs (4/5)
  AP MLD
STA1
STA2
STA3
AP1
AP2
AP3
Beacon
  Non-AP MLD
Broadcast TWT IE
Broadcast TWT Parameter Set
SPs can be aligned for MLO
Doze
Doze
Doze
Broadcast TWT SP A
Link 1
Link 2
Link 3
Beacon
Broadcast TWT SP B
Broadcast TWT SP E
Broadcast TWT SP F
Doze
Doze
Doze
Broadcast TWT IE
Broadcast TWT IE
A
B
A
A
E
F
Broadcast TWT SP A
Broadcast TWT SP A
In this illustrative example, three links are set up between the AP MLD and non-AP MLD. Both AP MLD and non-AP MLD supports Broadcast TWT. The scheduling AP MLD announces the existence of 2 Broadcast TWT Parameter Sets in the Broadcast TWT IE transmitted in the Beacon frame from the AP MLD to the non-AP MLD over Link 1. Moreover, the AP MLD also indicates that the TWT schedule corresponding to TWT Parameter Set A is an Aligned Schedule.
The TWT scheduling AP MLD indicates Accept TWT in the TWT Setup Command field and sets up schedule corresponding to Broadcast TWT Parameter Set A across all three setup links between the AP MLD and non-AP MLD. Also three other Broadcast TWT schedules are set up on three different links.

## Slide 10: Broadcast TWT for MLDs (5/5)
In this illustrative example, three links are set up between the AP MLD and non-AP MLD. Both AP MLD and non-AP MLD supports Broadcast TWT. The non-AP MLD transmits a frame on Link 1 containing a Broadcast TWT element to the AP MLD and suggests a particular Broadcast TWT schedule by setting the TWT Setup Command field to Suggest TWT. Moreover, the non-AP MLD indicates to the AP MLD that it wants the Broadcast TWT schedule to be aligned across setup links, Link 1 and Link 3.
The AP MLD responds to non-AP MLD’s suggestion with acceptance. The AP MLD creates a broadcast TWT schedule with the same Broadcast TWT Parameter Set contained in the Broadcast TWT IE in the TWT initiating frame transmitted by the non-AP MLD. The AP MLD then transmits a TWT IE to the non-AP MLD over Link 1 and Link 3 with that Broadcast TWT Parameter Set and indicates Accept TWT in the respective TWT Setup Command field. The AP MLD also indicates that the corresponding schedule across Link 1 and Link 3 are aligned. The Broadcast TWT Aligned Schedule is set up across Link 1 and Link 3.
  Non-AP MLD
  AP MLD
Broadcast TWT SP
Link 1
Link 2
Link 3
Broadcast TWT SP
Broadcast TWT IE
Broadcast TWT Parameter Set
Frame containing Broadcast TWT IE
STA1
STA2
STA3
AP1
AP2
AP3
AP1
STA1
AP2
STA2
AP3
STA3
Broadcast TWT IE
Broadcast TWT IE
Beacon
Beacon
Beacon

## Slide 11: Summary
In this contribution, we propose the facilitation of broadcast TWT operation for MLDs
  For any MLD, it is optional to support broadcast TWT operation
  A non-AP MLD may provide its broadcast TWT operation capabilities during ML setup
An Aligned Schedule is defined for Broadcast TWT operation for MLDs
  During Broadcast TWT announcement, an AP MLD may indicate whether or not a particular Broadcast TWT schedule is an Aligned Schedule.
  A non-AP MLD shall indicate whether or not it wants any particular Broadcast TWT schedule (Suggest TWT or Demand TWT) to be aligned across multiple links or whether it wants to join any existing Aligned Schedule.
  The Aligned Schedule can be established on any subset of links between the AP MLD and non-AP MLD.

## Slide 12: References
[1] IEEE P802.11ax/D8.0 – 26.8.3 (Broadcast TWT operation)
[2] IEEE P802.11ax/D8.0 – 10.47 (Target Wake Time)

## Slide 13: SP 1
Do you agree that in R1:
  An MLD may support broadcast TWT operation
    Broadcast TWT negotiation can take place on any link between an STA affiliated with a non-AP MLD and an AP affiliated with an AP MLD that support broadcast TWT operation.

## Slide 14: SP 2
Do you agree that in R1:
  For Broadcast TWT operation for MLDs, an Aligned Schedule is defined as a Broadcast TWT schedule that shall be aligned across multiple links between the AP MLD and non-AP MLD.
    During Broadcast TWT announcement, an AP MLD may indicate whether or not a particular Broadcast TWT schedule is an Aligned Schedule.
    A non-AP MLD shall indicate whether or not it wants any particular Broadcast TWT schedule to be aligned across multiple links or whether it wants to join any existing Aligned Schedule.
    The Aligned Schedule can be established on any subset of links between the AP MLD and non-AP MLD.