## Slide 1: TSPEC Request
Date: 2021-04-28
Authors:

## Slide 2: Abstract
In this contribution, we propose the support for traffic information request from a non-AP STA or non-AP MLD to an AP or AP MLD.

## Slide 3: Background
To assist a non-AP STA or non-AP MLD to specify a suggested/demanded set of TWT parameters in TWT Setup (Suggest TWT and Demand TWT in TWT Setup Command), it would be beneficial if the AP or AP MLD can provide information about the expected traffic pattern in the DL for a traffic flow for the non-AP STA or non-AP MLD
It should be possible for the non-AP STA or non-AP MLD send a request to the AP or AP MLD for providing such information

## Slide 4: Motivation
In many cases, STAs may not have the necessary traffic profile information, especially for downlink.
Sometimes the STA may have the inaccurate information.
  For instance, in high contention case, timing information may be disordered, and hence information like burst size and service starting time maybe inaccurate.
Providing this information by the AP/AP MLD would help the non-AP STA/non-AP MLD in better traffic detection

## Slide 5: Motivation
1
2
3
4
5
6
7
8
9
10
11
AP – side DL
timing info
STA – side DL
timing info
1
2
3
4
5
6
7
8
9
TWT SP
doze
doze
doze
Fig. 1 Example to depict the difference between DL timing information available at the AP side and that at the non-AP STA or the non-AP MLD. Only DL packets are shown for simplicity
DL timing information available at the STA is affected by a number of factors
  E.g., TWT settings, high contention, etc.
DL timing information available at the STA side may not be accurate for computation of some of the fields in the TSPEC element
  E.g., Burst size, traffic type, etc.

## Slide 6: Motivation
A single application can support more than one type of traffic
  A number of applications support more than one type of traffic. E.g., Social media apps support video, audio, messaging related features
  A number of applications can be run from within a web browser. E.g., YouTube, news channel websites, etc.
Even with knowledge of the application running, the STA may not have the necessary traffic profile information for DL traffic

## Slide 7: TSPEC Request
We propose to define a new IE called TSPEC request IE
  The TSPEC request IE is sent by the non-AP STA or non-AP MLD to the AP or AP MLD
  It includes a TID bitmap to indicate the information for which TID(s) are being requested
Upon receiving the TSPEC request IE, the AP or AP MLD can send the requested information using the TSPEC element(s) or its variant (e.g. TSPEC-lite) to the non-AP STA or non-AP MLD
  The TSPEC element(s) correspond to the characteristics of the traffic flow in DL for the requested TID(s)

## Slide 8: SP 1
Do you agree to add the following to 11be R1:
  The non-AP STA or non-AP MLD may send a TSPEC request IE to the AP or AP MLD to request for the DL traffic characteristic of a traffic flow
  Upon receiving the TSPEC request IE, the AP or AP MLD can send the requested information using the TSPEC element(s) or its variant (e.g. TSPEC-lite) to the non-AP STA or non-AP MLD