## Slide 1: TSPEC Request
Date: 2021-03-05
Authors:

## Slide 2: Abstract
In this contribution, we propose the support for traffic information request
from a non-AP STA or non-AP MLD to an AP or AP MLD.

## Slide 3: Background
Standard supports a non-AP STA or non-AP MLD to specify a suggested/demanded set of TWT parameters in TWT Setup (Suggest TWT and Demand TWT in TWT Setup Command) [1].
To assist a non-AP STA or non-AP MLD to specify a suggested/demanded set of TWT parameters, it would be beneficial if the AP or AP MLD can provide information about the expected traffic pattern in the DL for a traffic flow for the non-AP STA or non-AP MLD
It should be possible for the non-AP STA or non-AP MLD send a request to the AP or AP MLD for providing such information

## Slide 4: Motivation
In many cases, STAs may not have the necessary traffic profile information, especially for downlink.
  Timing information available at the STA is affected by a number of factors. E.g., TWT settings, high contention, etc.
    For instance, in high contention case, timing information may be disordered, and hence information like burst size and service starting time maybe inaccurate.
  Therefore, DL timing information available at the STA side may not be accurate for computation of some of the fields in the TSPEC element. E.g., Burst size, traffic type, etc.
  Even with knowledge of the application running, the STA may not have the necessary traffic profile information for DL traffic. A single application can support more than one type of traffic
    A number of applications support more than one type of traffic. E.g., Social media apps support video, audio, messaging related features
    A number of applications can be run from within a web browser. E.g., YouTube, news channel websites, etc.
Knowledge of DL timing information (provided by AP) coupled with UL timing information (available at STA) can enable the STA to make a TWT parameter suggestion/demand suitable for both downlink and uplink (jointly) considering its own power saving need and latency sensitivity tolerance

## Slide 5: Motivation
Fig. 1 Illustration to show the improvement in TWT setting considering latency and power savings with the knowledge of DL timing information.
TWT setting 1
TWT setting 2
Wi-Fi Original Traffic
1
2
3
4
5
6
7
8
1
2
3
4
1
2
3
4
5
6
7
8
1
2
3
4
1
2
3
4
5
6
7
8
1
2
3
4
TWT SP
doze
TWT SP
doze
The above figure shows two example TWT settings:
  In TWT setting 1, STA considers UL timing information for TWT parameter specification
  In TWT setting 2, STA considers both DL and UL timing information for TWT parameter specification
Availability of DL timing information can enable the STA to suggest/demand an improved TWT setting for both DL and UL.
Downlink
Uplink

## Slide 6: TSPEC Request
We propose to define a new IE called TSPEC request IE
  The TSPEC request IE is sent by the non-AP STA or non-AP MLD to the AP or AP MLD
  It includes a TID bitmap to indicate the information for which TID(s) are being requested
Upon receiving the TSPEC request IE, the AP or AP MLD can send the requested information using the TSPEC element(s) or its variant to the non-AP STA or non-AP MLD
  The TSPEC element(s) correspond to the characteristics of the traffic flow in DL for the requested TID(s)

## Slide 7: References
[1] IEEE 802.11-2020, “Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specification”

## Slide 8: SP 1
Do you agree to add the following to 11be R1:
  The non-AP STA or non-AP MLD may send a TSPEC request IE to the AP or AP MLD to request for the DL traffic characteristic of a traffic flow
  Upon receiving the TSPEC request IE, the AP or AP MLD can send the requested information using the TSPEC element(s) or its variant to the non-AP STA or non-AP MLD