## Slide 1: Enhanced UORA
Date: 2021-03-12
Authors:
Name | Affiliation | Address | Phone | Email
Yanyi Ding | Panasonic Corporation |  |  | yanyi.ding@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 
Rajat Pushkarna |  |  |  | 

## Slide 2
Background
The efficiency of UORA is low. In the highest-efficiency case, the RU acceptance rate is 37%. [1]
This contribution proposes an enhanced UORA (e-UORA) mechanism to reduce the collision rate and improve the success probability.

## Slide 3
Collision in UORA
In 11ax, UORA allows non-AP HE STAs that wins the contention to randomly select random access RU (RA-RU) assigned by an AP in a trigger frame.
  Non-AP HE STAs can only transmit on the first spatial stream in RA-RUs.
    i.e., UL MU-MIMO is not supported in RA-RUs.
  If more than one non-AP HE STAs select a same RA-RU, collision happens.
(AID 0) RU 1
(AID 0) RU 2
…
(AID 2045) RU 3
RU1 Collision
RU 2 Empty
…
HE TB PPDU from STA 3 (RU 3)
STA1
STA2
STA3
SIFS
SIFS
Multi-STA BlockAck
Trigger frame
(random access)
Frequency
Time
STA 1, STA 2:
associated STAs qualified to contend for RA-RUs.
STA 3:
unassociated STA qualified to contend for RA-RUs.

## Slide 4
Enhanced UORA
In e-UORA, UL MU-MIMO is enabled in RA-RUs. (Whether e-UORA is enabled may be indicated in the trigger frame.)
Non-AP STAs that win the contention may randomly select a single spatial stream in the randomly selected RA-RU to transmit.
  The range of eligible spatial streams may be
    Option 1: limited by the number of HE/EHT-LTF symbols indicated in the trigger frame.
    Option 2: indicated in the trigger frame.
The receiver AP performs decoding on all eligible spatial streams on RA-RUs of TB PPDU.
  To reduce the complexity on AP side, the maximal number of eligible spatial streams shall be limited.
For STAs supporting UL MU-MIMO and UORA, e-UORA is a simple enhancement to realize.

## Slide 5
Enhanced UORA
(AID 0) RU 1
(AID 0) RU 2
…
(AID 2045) RU 3
EHT TB PPDU from STA1 and STA2 (RU 1)
RU 2 Empty
…
EHT TB PPDU from STA 3 (RU 3)
STA1, selects SS1
STA2, selects SS2
STA3, selects SS1
SIFS
SIFS
Multi-STA BlockAck
Trigger frame
(random access)
Frequency
Time
Example of e-UORA
  The number of EHT-LTF symbols indicated in the trigger frame is ‘2’.
    i.e., the range of eligible spatial streams in RA-RU is SS1~SS2.
In this example, the collision that could have happened in RU 1 is avoided.

## Slide 6
Discussion on RU Size Concern
There is restriction on size of MU-MIMO enabled RU.
  In 11ax, the minimal size of MU-MIMO enabled RU is 106-tones.
  In 11be D0.3, the minimal size of MU-MIMO enabled RU is 242-tones.
The restriction on size of MU-MIMO enabled RU was proposed by [2]. Considerations on throughput of DL MU-MIMO within OFDMA was discussed:
  DL MU-MIMO in small-size RU causes large overhead of HE-SIG-B symbols.
    For UORA, there is no HE-SIG-B or only one EHT-SIG symbol in TB PPDU.
The considerations on throughput of MU-MIMO within OFDMA does not exist in e-UORA.

## Slide 7
Simulation Setup
Common setup
  Mechanism: UORA/ e-UORA
  Number of STAs: [ 2, 4, 6, 8, 10, 12, 14, 16 ]
  Number and size of RA-RUs: 8, 26-tone RU
  Range of eligible SS in RA-RUs: [ 2, 4 ] (assume all supported by STAs)
  Each STA has one packet to transmit.
  Iterations: 1000
UORA setup
  EOCWmin = 2
  BSS radius = 15 m
  Active STAs are randomly located in the BSS.

## Slide 8
Simulation Result
Note:
Average number of collided packets is the number of collided packets per iteration.
Nru = 8
At the point of Nru=Nsta, compared with UORA (1.2), the number of collided packets may be reduced by:
  ~40% when 2 SS is applied in e-UORA (0.72).
  ~67% when 4 SS is applied in e-UORA (0.39).
The decrease of collided packets is more obvious with increasing number of active STAs.
1.2
0.72
0.39

## Slide 9
Simulation Result
Under the same SNR, the maximal average number of successful packets can be up to:
  3 in UORA.
  4.2 in e-UORA with Nss = 2.
  6.1 in e-UORA with Nss = 4.
It is still possible for a STA to transmit successfully in UL MU-MIMO within RA-RU, even without scheduling and power control for UL MU-MIMO.
Nru = 8
Note:
D-NLOS Channel with actual timing and basic power control.
‘Successful packets’ means a packet being transmitted successfully and decoded correctly.
Average number of successful packets is the number of successful packets per iteration.
3
4.2
6.1

## Slide 10
Conclusion
In this contribution, we propose the enhanced UORA to reduce the collision rate and improve the efficiency.
  STAs that win contention may randomly select a single spatial stream on the randomly selected RA-RU to transmit.
  The range of eligible spatial streams is
    Option 1: limited by the number of HE/EHT-LTF symbols indicated in the trigger frame.
    Option 2: indicated in the trigger frame.
  Minimal change in non-AP STA side.

## Slide 11
Reference
Draft P802.11ax_D8.0
11-15-0832-00-00ax-performance-evaluation-of-su-mu-mimo-in-ofdma

## Slide 12
SP#1
Do you support that EHT should consider allowing STAs to transmit in SS other than the first SS in RA-RUs?
  This is for information collection.
  Only single SS per STA is allowed.
  This is for R2.
Y/N/A:

## Slide 13
SP#2
Do you support that EHT allows UL MU-MIMO to be enabled in RA-RUs and relaxes the restriction on size of UL MU-MIMO enabled RU for RA-RUs?
  Only applicable to EHT TB PPDU.
  Only single SS per STA is allowed.
  The new minimal size of UL MU-MIMO enabled RA-RU is TBD.
  This is for R2.
Y/N/A:

## Slide 14
SP#3
Do you support that EHT allows non-AP STAs that wins UORA contention to randomly select an eligible spatial stream in the randomly selected RA-RU to transmit?
  The way to indicate the range of eligible spatial streams is TBD.
  This is for R2.
Y/N/A: