## Slide 1: mmWave status in ETSI BRAN
Date: 2019-04-15
Authors:

## Slide 2: Abstract
This document discusses the status of mmWave standard1.

## Slide 3: ETSI BRAN activity in the mmWave band
Band original designated 57-66GHz, now extended to e 57-71GHz.
The group operates under the guidance of ERC Recommandation 70-03 (relating to the use of Short Range Devices)

## Slide 4: ETSI BRAN standard for the band
EN 302 567 – Multiple-Gigabit/2 radio equipment operating in the 60GHz band; Harmonised Standard for access to radio spectrum
EN 303 722 – Wideband Data Transmission System (WDTS) for Fixed Network Radio Equipment in the 57-71 GHz band; Harmonised Standard for access to radio spectrum
EN 303 753 - Wideband Data Transmission System (WDTS) for Fixed and Mobile Network Radio Equipment in the 57-71 GHz band; Harmonised Standard for access to radio spectrum

## Slide 5: EN 302 567 – status
Corresponds to mobile devices, no fixed outdorr.
Appropriate for 11ad devices
In the working for many years.
In the last stages of approval (sent to ENAP)
Coexistence Mechanism: LBT

## Slide 6: EN 303 722
Fixed outdoor access
Appropriate for TDD access in 802.11ay
discussion for about 2 years – about to be set to EC consultant
Channel Sharing Mechanism:
  Automatic Transmit Power Control
  Automatic Link Adaptation
Do we want to act?

## Slide 7: EN 303 753
Fixed and Mobile devices
In the early stages of development
Coexistence Mechanisms: not defined yet
  Narrow Beams
  Aren’t necessary (?)

## Slide 8: References