## Slide 1: UL Replay Protection Summary
Date: 2021-03-11
Authors:

## Slide 2: Abstract
This presentation is a summary of EBCS UL replay protection options.

## Slide 3: Issues on Replay
Duplicate data can be eliminated by application layer.
  It is not an issue.
DDoS attack is main issue.
Server
AP
AP
AP
Replay
STA
Replay
STA
Replay
STA
Replay
STA

## Slide 4: Option 1 (Counter)
Transmitter (non-AP STA)
Transmitter has a counter (32 bits).
UL frame contains the counter value.
The counter is incremented for each UL frame transmission.
If the counter overflows, the counter is reset to 0.
Receiver (AP)
Receiver caches the counter value of each transmitter.
If the counter value in an UL frame is greater than the cached value, the receiver forwards the data, otherwise discard the data.

## Slide 5: Issues on Option 1
The receiver cannot authenticate the first frame from each transmitter.
  The receiver does not have the cached counter value.
The receiver requires to keep the counter value for every transmitter forever.
The receiver cannot discriminate the counter values of different round.
  When a receiver has a cached value 100 for a transmitter and receives an UL frame with the counter value 99, the receiver cannot discriminate whether it is an older frame or a new frame that has a next round counter value.
  The counter value should never be reset.

## Slide 6: Option 2 (Nonce)
Transmitter (non-AP STA)
Transmitter transmit UL frame after receiving nonce.
UL frame contains the received nonce value.
Receiver (AP)
Receiver advertises nonce value.
  (In Beacon, EBCS Info, etc.)
The nonce value is changed periodically.
If the nonce value in an UL frame is identical with the transmitted nonce value, the receiver forwards the data, otherwise discard the data.

## Slide 7: Issues on Option 2
Fake AP
  Replaying nonce advertisement can invoke UL frame transmission.
    The content of the UL frame is to be broadcasted.
    It is not an issue.
Transmitter requires RX function.
Battery consumption
  Which consumes more energy?
    Blind transmission
    Receive before transmission
AP exists
TX
RX

## Slide 8: Option 3 (Time Synchronization)
Transmitter (non-AP STA)
Transmitter has an RTC.
UL frame contains the timestamp from the RTC.
Receiver (AP)
If the difference between the timestamp value in an UL frame and the receiver’s own RTC value is less than the configured value, the receiver forwards the data, otherwise discard the data.
DL uses this option.

## Slide 9: Issues on Option 3
Both transmitter and receiver require accurate RTC.
  It is not practical for sensor use case.