## Slide 1: Information Sharing and Exchange for Multi-AP Coordination
Date: 2021-09-06
Authors:

## Slide 2: Abstract
Various contributions have tried to map out the process/procedure of multi-AP coordinated transmission. However, till now there is no clear consensus upon what information exchange needs to take place before this process.
This contribution tries to identify and discuss the information/data that needs to be exchanged between the different entities involved in the multi-AP coordination process.

## Slide 3: Background
Information exchange between coordinating nodes is imperative for smooth multi-AP operation. Different type of information may need to be shared at different stages of the coordination process as mentioned in various contributions.
Accordingly, we start by looking at the contribution documents [1-8] that mention or discuss some information exchange related multi-AP coordination.

## Slide 4: From the SFD [1]
• EHT APs supporting multi-AP coordination can send a frame (e.g., Beacon or other Management frame) which includes/advertises capabilities of Multi-AP transmission schemes. Any specifics related to this frame are yet to be decided (TBD).
• An AP that intends to use the resources shared by another AP shall be able to indicate its need to the AP that shared the resource.
• Define a mechanism for sharing AP to optionally solicit feedback from one or more APs belonging to the candidate set regarding their resource needs and the intent to participate in the coordinated transmission.

## Slide 5: Transmission Procedure from [2]
A multi-AP transmission procedure assuming the presence of a master-AP (M-AP) and one or more slave-APs (S-APs), which consists of three parts:
Multi-AP sounding – null data packets (NDPs) are transmitted from APs to STA and their feedback is received.
Multi-AP selection – selecting/verifying S-APs that can participate in the coordination.
Multi-AP data transmission – data packet is transmitted using one of the coordination mechanisms.

## Slide 6: Unified Transmission Procedure from [3]
M-AP transmits a slave trigger frame to initiate multi-AP transmission. The function of this trigger frame is to ensure synchronization of all APs and to notify the slave-APs (S-APs) regarding which mode to use and the corresponding time/frequency/spatial/power domain resource allocation.

## Slide 7: Coordination Architecture [4]
The multi-AP coordination could be initiated by the AP or STA. Furthermore, the APs participating in the coordination need to be selected/identified. Since STA has knowledge of the air interface and fronthaul link measurements it can help in the “preparation” stage by suggesting which APs should participate in the coordination. The whole multi-AP coordination process is divided into following stages:
Association – exchange of multi-AP coordination capability information between APs and STAs

## Slide 8: Coordination Architecture [4]… contd
Preparation – AP or STA initiate the multi-AP coordination by deciding which APs should coordinate (STA may suggest potential APs). Recommended APs can be determined by fronthaul link metric collection, load and access control information, etc
Transmission - Chosen APs of the multi-AP network perform DL/UL multi-AP transmission

## Slide 9: Data Sharing b/w APs [5]
[5] considers a M-AP which functions as the coordinator and S-APs which participate in the JT. The M-AP needs to share the (same) data with S-APs in a broadcast, unicast or multicast manner. For multicast, a group indication mechanism (and corresponding announcement frame) needs to be devised.
The announcement frame is broadcast with the body of the frame identifying the S-APs and their RU allocations.
Data frame is only sent to the S-APs.
Block-Ack (BA) frame is sent using assigned RUs indicated in the announcement frame

## Slide 10: Joint Coordination schemes [6]
C-SR is jointly used with C-OFDMA. The “SR coverage” of APs may have many different pattens in terms of number of APs that can transmit at the same time based on Tx power, required MCS level, relative distances among APs, RF radiation pattern etc.
  Shared APs provide the sharing AP with RSSI (or SNR) measurements for each STA-AP pair
  Full scheduling information is sent back to all shared APs
    RU allocation for all STAs
  Each shared AP determines the MCS for its own associated STA using the scheduling table received from sharing AP

## Slide 11: Multi-AP Setup [7]
In a multi-AP coordination scenario, an AP needs to know the channel information of STAs associated to other coordinating APs in additions to its own STAs. Therefore, the AP needs to their identifiers as well. This requires a mechanism that allows APs to share such information. The whole process is divided into the following two phases:.
Discovery - APs can discover each other by receiving Beacon frame or management frames sent by neighboring APs.
Setup – Here the M-AP selects the S-APs and they exchange information to select the coordination set.

## Slide 12: Group Formation and Coordination Scheme Selection [8]
STA requirements – User Priority or Access Category
Link quality metrics – SINR, RSRP, RSSI
Backhaul conditions

## Slide 13: Consolidated List
AP coordination capabilities (can the M-AP keep a database of the S-APs coordination capabilities?)
User related information (application requirements etc.)
Backhaul/fronthaul
Channel state information (CSI)/link quality indication (RSSI, SNR...)
Coordination hypothesis (scheme and muting/power etc.)
Benefit of each hypothesis
Scheduling Information (RU allocation etc.)

## Slide 14: Additional Considerations
What would be the change in information for centralized vs. distributed coordination scenarios?
The benefit metric is usually employed considering a single coordination scheme. Is this what we expect to use? Or do we expect different coordination schemes being used simultaneously (for different users) or different schemes for the same user in different TXOPs?

## Slide 15: Summary
We have highlighted different aspects of information that needs to be shared b/w coordinating nodes.
It would be sensible to categorize this information according to the stages of multi-AP coordinated transmission and then follow up with the mechanism that can support this information exchange

## Slide 16: Straw Poll # 1
Which of these information elements should be shared amongst the coordinating nodes for multi-AP coordination?
AP coordination capabilities
User related information (application requirements etc.)
Backhaul/fronthaul
Channel state information (CSI)/link quality indication (RSSI, SNR…)
Coordination hypothesis (scheme and muting/power etc.)
Benefit of each hypothesis
Scheduling Information (RU allocation etc.)

## Slide 17: Straw Poll # 2
Do you support to add to the SFD that following information needs to be exchanged for a multi-AP coordination process:
AP coordination capabilities, user related information (application requirements etc.), backhaul/fronthaul, channel state information (CSI)/link quality indication (RSSI, SNR, …), coordination hypothesis (scheme and muting/power etc.), benefit of each hypothesis, Scheduling Information (RU allocation etc.) ?
Yes
No
Abstain

## Slide 18: References
Compendium of straw polls and potential changes to the Specification Framework Document - Part 2, IEEE 802.11-20/1935r19.
Multi-AP Transmission Procedure, IEEE 802.11-19/0804r0
A Unified Transmission Procedure for Multi-AP Coordination, IEEE 802.11-19/1102r0
Consideration on Multi-AP Coordination, IEEE 802.11-19/1129r2
Data Sharing for Multi-AP Coordination, IEEE 802.11-19/1554r1
On Joint C-SR and C-OFDMA M-AP Transmission, IEEE 802.11-20/1399r2
Setup for Multi-AP coordination, IEEE 802.11-19/1895r2
Multi-AP Coordination: Recap and Additional Considerations, IEEE 802.11-20/1713r2