## Slide 1: EHT TF Clarifications
Date: 03/17/21
Authors | Email
Xiaogang Chen | Xiaogang.c.chen@intel.com
Po-Kai Huang | 
Alexander Danny | 
Cheng Chen | 
Laurent Cariou | 

## Slide 2: Background
TGbe agreed to define a special user field (with AID = 2007) to carry the extra EHT info for general TF.
This contribution focuses on
  Presence of the special user info field (AID 2007) in different TF types;
  MU-RTS RU allocation indication.

## Slide 3: Presence of the special user info field
Proposal: All types of EHT TF shall always include the special user info field (with AID=2007) right after the common field.
  Guarantee a unified processing on the EHT common info field (including the HE common info field and special user info field) of EHT TF;
  Rx only adjusts depends on B55 instead of depends on both B55 and TF types.
    B55 (presence of the special user field) -> Parse EHT common info if B55 = 0; otherwise Parse HE common info.

## Slide 4: Background of HE MU-RTS
RU allocation in MU-RTS indicate the STA on which 20MHz subchannels the CTS will be transmitted.
RU allocation in HE MU-RTS
  Use the entries (61-68) corresponding to the RU 242/484/996/996*2 in the HE RU allocation table;
  Only allow CTS transmit on P20/P40/P80;
  No puncturing information included in RU allocation.

## Slide 5: Design goal of the RU allocation in EHT MU-RTS
320MHz CTS response support;
  Straight forward.
Including puncture information;
  Straight forward.
EHT MU-RTS trigger CTS from HE and EHT STA.
  Transparent to HE and EHT STA;
  Fully controlled by AP, no need to standardize.

## Slide 6: RU allocation in EHT MU-RTS
Proposal:
  RU allocation in EHT MU-RTS reuse the RU allocation defined for general EHT TF;
  For a non-AP STA, the CTS responses to EHT MU-RTS shall be transmitted on the 20MHz subchannel(s) that are overlapped with the large size RU/MRU indicated by its own RU allocation subfield.

## Slide 7: SP1
Do you agree:
The special user info field (user info field with AID=2007) shall be present in all the EHT TF variants defined in 11be.
  For the special user info field in the EHT variant of MU-RTS, all the bits are reserved except the “BW Extension” subfield.

## Slide 8: SP2
Do you agree that
  The CTS response to MU-RTS supports all the modes in 11ax and 320MHz no-HT duplicate transmission;
  The CTS response to MU-RTS supports punctured transmission for BW >= 80MHz;
  The CTS response to MU-RTS is transmitted on the 20MHz subchannel(s) that are overlapped with the large size RU/MRU indicated by its own RU allocation subfield;
  The CTS response to MU-RTS shall be transmitted including the primary 20MHz channel.
    Whether EHT SST STA can respond to MU-RTS with CTS on the 20 MHz subchannel(s) not including the primary 20 MHz channel is TBD

## Slide 9: Backup

## Slide 10: Valid Large RU indication in MU-RTS
PS160 subfield | B0 of RU Allocation subfield | B7-B1 of RU Allocation subfield | Bandwidth | RU size | RU index | PHY RU index
 |  | 61 | 20, 40, 80, 160, or 320 MHz | 242 | RU1 | 4×N + RU index
 |  | 62 | 40, 80, 160, or 320 MHz |  | RU2 | 
 |  | 63, 64 | 80, 160, or 320 MHz |  | RU3 and RU4, respectively | 
 |  | 65 | 40, 80, 160, or 320 MHz | 484 | RU1 | 2×N + RU index
 |  | 66 | 80, 160, or 320 MHz |  | RU2 | 
 |  | 67 | 80, 160, or 320 MHz | 996 | RU1 | N + RU index
0-1: 160 MHz segment where RU is located | 0 | 68 | Reserved |  |  | Reserved
 | 1 |  | 160, or 320 MHz | 2×996 | RU1 | LU160 + RU index
0 | 0 | 69 | Reserved |  |  | Reserved
0 | 1 |  |  |  |  | 
1 | 0 |  |  |  |  | 
1 | 1 |  | 320 MHz | 4×996 | RU1 | RU1

## Slide 11: Valid Large MRU indication in MU-RTS
PS160 subfield | B0 of RU Allocation subfield | B7-B1 of RU Allocation subfield | Bandwidth | RU size | RU index | PHY RU index
 |  | 90–93 | 80, 160, or 320 MHz | 484+242 | MRU1 to MRU4, respectively | 4×N + RU index
0-1: 160 MHz segment where RU is located | 0 | 94–95 | 160, or 320 MHz | 996+484 | MRU1 to MRU2, respectively | 4×LU160 + RU index
 | 1 |  |  |  | MRU3 to MRU4, respectively | 
0-1: 160 MHz segment where RU is located | 0 | 96-99 | 160, or 320 MHz | 996+484+242 | MRU1 to MRU4, respectively | 8×LU160 + RU index
 | 1 |  |  |  | MRU5 to MRU8, respectively | 
0 | 0 | 100-103 | 320 MHz | 2x996+484 | MRU1 to MRU4, respectively | RU index
0 | 1 |  |  |  | MRU5 to MRU6, respectively | 
1 | 0 |  |  |  | MRU7 to MRU8, respectively | 
1 | 1 |  |  |  | MRU9 to MRU12, respectively | 
0 | 0 | 104 | 320 MHz | 3x996 | MRU1 | RU index
0 | 1 |  |  |  | MRU2 | 
1 | 0 |  |  |  | MRU3 | 
1 | 1 |  |  |  | MRU4 | 
0 | 0 | 105-106 | 320 MHz | 3x996+484 | MRU1 to MRU2, respectively | RU index
0 | 1 |  |  |  | MRU3 to MRU4, respectively | 
1 | 0 |  |  |  | MRU5 to MRU6, respectively | 
1 | 1 |  |  |  | MRU7 to MRU8, respectively |