## Slide 1: Protecting Password Identifiers
Date: 2021-03-30
Authors:

## Slide 2: Abstract
This submission discusses protection of password identifiers in SAE

## Slide 3: What’s The Problem?
Password identifiers are used to look up passwords
  Passwords could be for groups of users– the way they’re used now– or per-user
  In degenerate case, they could become like usernames
Password identifiers are passed in the clear  PII!
  STA is a member of an identified group for shared passwords
  STA is a particular individual when used like usernames
We need to provide privacy to password identifiers
  Give the attacker no information about the underlying identity
  Prevent the attacker from using constructing PII

## Slide 4: Two Possible Solutions
Asymmetric crypto
  AP has a trusted public key, STA does HPKE-like wrapping of password identifier
  Pros: good, modular use of secure building blocks
  Cons: requires distribution of trusted public key, slower, bulkier, possible DOS issues
Symmetric crypto
  AP creates a stateless pseudonym that it can decipher later on
  Pros: faster, lower overhead
  Cons: first connection is with a plaintext identifier
Let’s choose option 2 (trusted public key distribution is hard)

## Slide 5: Solution (broadly speaking)
Have AP maintain a symmetric key
First time the STA associates it does so with an unprotected password identifier
AP encrypts the password identifier (with some salt) and gives it back to the STA during the 4way HS
Subsequent association is with encrypted password identifier, STA gets a new and different pseudonym in the subsequent 4way HS
Each association will have a unique password identifier that can be decrypted by the AP
If STA doesn’t understand protected password identifiers it will just respond in the clear again

## Slide 6: Issue to Consider
Everyone who can receive a pseudonym has to be able to decrypt it
  For ESS, that means all APs share the same symmetric key
  For mesh, that means every mesh point (everyone?) shares the same symmetric key
What’s the Issue?
  STA identities can be protected against other STAs in an ESS– a STA will not know what group another STA is in even if it’s the same group
  Group membership cannot be protected against other mesh points in a mesh (just like APs are not protected against other APs)

## Slide 7: Protected Identifiers and Mesh
Random MACs and different passwords per-mesh point links make encrypted password identifiers difficult to use
  There is no way to know which encrypted password identifier to use when constructing a Commit message
  Mesh point can generate its own protected identifier but that assumes recipients will know it, and if every mesh point knows the password and identifier of every other mesh point, then what’s the point of doing different passwords per-mesh link? Same security as a single password
OK, then what if it’s not random MACs?
  Then what’s the privacy concern? The fixed MAC is the identity bound to the password! No need to use protected password identifiers!
Well, what if there’s a single password for the whole mesh?
  There is no point in using password identifiers then!
Conclusion: password identifiers don’t really work with mesh

## Slide 8: Proposal
All APs in ESS share a symmetric key
Password identifier is padded and encrypted with an 8 octet random nonce which is used as a tweak to generate a stateless, one-time-use, pseudonym
Pseudonym is given out to STA using a KDE in the 4-way handshake
Pseudonym is transferred via IE in next SAE Commit
Peculiarities of mesh
  All mesh points must use the same symmetric key to generate and validate protected password identities
  Each mesh point will generate its own protected password identifier
  There’s little point in doing password identifiers with mesh though

## Slide 9
AES-SIV
key
password identifier:
blahfubar
4000blahfubar
padded:
tweaked:
71a08cf14000blahfubar
protected
password
identifier:
891b52f0725635f3abc8a6b13159df5afbf0a

## Slide 10: Properties of Proposed Scheme
A passive attacker cannot determine a protected identity;
Identifiers are protected against active attack insofar as SAE is resistant to active attack;
A passive attacker cannot connect protected identities across SAE protocol runs
Password identifiers can be arbitrarily padded to foil passive traffic analysis;
Protected identities are secure under a birthday bound of 232 encryptions;
An attacker cannot substitute identifiers to connect distinct runs of SAE;
An AP needs to only manage a single symmetric secret;
APs in an ESS, and all mesh points in a mesh, share a single symmetric secret (in an out of band, out of scope manner);
AP can use the same symmetric secret to protect all groups in the ESS that use password identifiers;
Identities are protected against members of the same group, except in a mesh;
The interface for password identifiers on a STA is unchanged;
The overhead is minimal—25 octets plus padding;
Uses symmetric cryptography for speed and DOS resistance

## Slide 11: References
11-21/0488r0