## Slide 1: Discussion on B55 of Common Info Field in EHT TF
Date: 2021-04-21
Authors:

## Slide 2: Recap
1) 11be has agreed to use B55 of Common Info Field to indicate the presence of Special User Info Field in EHT TF variants
  B55 is set to 1 to indicate that there is no Special User Info field in the Trigger frame.
  B55 is set to 0 to indicate that the Special User Info field is present in the Trigger frame.
2) 11be has agreed that the Special User Info Field shall be present in all EHT TF variants 11be in R1

## Slide 3: Question
Is it necessary for the B55 of the Common Info Field in EHT TF to indicate the presence of the Special User Info Field?

## Slide 4: Discussion
Scenario 1 – non-AP EHT STA associated with EHT AP
  The non-AP EHT STA can tell the Special User Info Field from User Info Fields via AID12=2007 because the Special User Info Field is always there in EHT TF.
Scenario 2 – non-AP EHT STA associated with HE AP
  The non-AP EHT STA will not take the User Info Fields with AID12=2007 as the Special User Info Field even if AID 2007 is assigned because it knows the BSS is not an EHT BSS.
Scenario 3 – non-AP HE STA associated with EHT AP
  The non-AP HE STA will not use the Special User Info Field because no non-AP HE STA will be assigned with AID 2007.

## Slide 5: Discussion
Scenario 4 – The Special User Info field can be omitted while only HE TB PPDUs are solicited by the EHT TF (B54 of the Common Info Field is set to 1) in P160 and there is not S160.
  The non-AP HE STA will not use the Special User Info Field because no non-AP HE STA will be assigned with AID 2007.
  The non-AP EHT STA will not use the Special User Info Field in this case either, for the information in the field is useless for HE TB PPDU.
  Whether there is the Special User Info field in this case should be specified. (i.e., clarification is needed for the 2nd approved SP in the recap slide.)
    If Y, specify there is the Special User Info Field in the EHT TF, which can be bypassed by the non-AP EHT STA.
    If N, specify there is not the Special User Info Field in the EHT TF. The non-AP EHT STA knows there is no Special User Info Field (B54=1 and no S160).

## Slide 6: Conclusion
Whether there is the Special User Info field should be specified for the case that only HE TB PPDU is solicited by EHT TF in P160 and there is no S160.
Based on the above analysis, there is no need to use B55 of the Common Info Field to indicate of presence of the Special User Info Field. The B55 can be reserved with the benefits
  The additional step of processing the B55 can be saved in non-AP EHT STA.
  More bits can be reserved for future use.
  Note - For R2, we can have further discussion in future. Indication of the presence of the Special User Info Field can be added even if there are scenarios and requirements.

## Slide 7: Proposal
Whether there is the Special User Info field is specified for the case that only HE TB PPDU is solicited by EHT TF in P160 and there is no S160.
B55 of the Common Info Field in ETH TF is reserved in R1.
  Note - For R2, we can have further discussion in future on the indication of presence of the Special User Info Field in EHT TF.

## Slide 8: SP1
Do you support that there is the Special User Info Field in the EHT TF to solicit HE TB PPDU only in P160 and there is no S160.
  Option1: Yes and there is the Special User Info Field.
  Option2: Yes and there is not the Special User Info Field.

## Slide 9: SP2
Do you support to reserve B55 of the Common Info Field in ETH TF in R1?
  Note - For R2, we can have further discussion on the indication of presence of the Special User Info Field in EHT TF.

## Slide 10: Reference
[1] https://mentor.ieee.org/802.11/dcn/20/11-20-1935-26-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2.docx