## Slide 1: Trellis Coded Quantization for CSI Feedback Part 2: Quantization for the Magnitude of CSI
Date: 2021-05-10
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Yan Xin |  |  |  | 
Osama AboulMagd |  |  |  | 
Edward Au |  |  |  | 

## Slide 2: Background
This PPT slides continue to describe the application of TCQ to the CSI Feedback
In the Part 1, we described on how to apply the TCQ for the phase of the measured CSI
We propose how to convert the Rayleigh distributed samples into a uniform distributed samples and apply the TCQ for the quantization of the CSI Magnitude in this Part 2
CSI matrix should be considered as a sensing measurement result type for sub-7 GHz applications [1]
  CSI matrix
    Real and imaginary parts of each element of the matrix (that is, sub-carrier for each antenna/antenna pair).
    Report would be the estimated CFR – no loss of information as in the compressed beamforming feedback matrix.

## Slide 3: Statistics of Rayleigh Distribution
When the measured CSI (CFR) are represented in the magnitudes and phases, the magnitudes are approximately Rayleigh-distributed
PDF of Rayleigh-Distributed Random Variable (x) is
  =, where x is greater than or equal to 0 and is a scaling factor
  Mean of x is,
The generation of Rayleigh-Distributed samples is given from the following equation, , where U is Uniformly-Distributed between 0 and 1.
Hence, we can have the following relation, to convert the Rayleigh samples into the Uniform samples with the range between 0 and 1

## Slide 4: Histogram per OFDM Symbol of Measured CFR (Magnitude) : 4 PPDUs are plotted below, but similar trend for all the tested PPDUs with IEEE Chan D

## Slide 5: Quantization for the Magnitudes of CSI
First of all, we take the average over an OFDM symbol for the magnitude samples from each measured CSI per sub-carrier
Second, we can obtain the scaling factor () from the following equation, where is the average obtained at the First step
  If the scaling factor is greater than 16, the channel normalization should be taking place before converting the CFR into the magnitude and phase
Third, we convert the magnitude samples of an OFDM symbol to the uniformly-distributed samples ranged between 0 and 1 according to the following equation, where x is the magnitude samples, is the scaling factor obtained at the Second step and U is the converted samples
Once we obtain the uniformly-distributed samples U , we can now apply the TCQ to the U ranged between 0 and 1. We feedback the TCQ outputs and to the Initiator
The Initiator, first of all, recovers the U samples from the fed-back TCQ outputs and convert them to the magnitude samples x with the following equation,

## Slide 6: TCQ for uniform-distributed samples U ranged between 0 and 1
We use the 802.11 BCC Trellis Scheme
We use the same Codeword generation method as in Part 1, but just the lower and upper bounds of the source data are changed to 0 and 1
Forward State Transition Function:

## Slide 7: Codeword Generation
For an n-bit TCQ quantizer, the codebook is divided into four sub-codebooks, each with N/2 codewords, where N = 2n.
When the i-th (0<= i <= 3) sub-codebook is denoted as , where is the l-th codeword in Ci .
These sub-codebooks are generated in the following way.
  Let Lb and Ub be the lower and upper bounds of source data.
  Let and , then =.
Depending on the trellis scheme, Ci can be arranged to make the distance between Ci s maximally equal, when mapped to the trellis output bits.

## Slide 8
For an example with 8 bit TCQ, N=28=256 and the source data samples to be quantized being uniformly distributed between 0
There are 4 sub-codebooks and 128 codewords in each sub-codebook, thus, C0 to C3 are obtained as follows according to the method in slide 6
, .993164063}
}
}
}
The Lb and Ub in the previous slide corresponds to , respectively

## Slide 9
The subscript i in Ci represents the output bits in a state transition, and the 00 is paired with 11 and 01 is paired with 10 in the outgoing branches from a state as we see from the figure beside
In order to make the distances among sub-codebooks maximally equal, correspond to the output bit 00, correspond to 01, correspond to 11, and correspond to 10
Therefore, each outgoing branch from a state has a corresponding output and thus has a corresponding sub-codebook
1
0
3
4
5
2
………………………..………..
6
7
62
63
1
0
3
4
5
2
…….
6
7
8
9
10
11
12
13
14
15
62
63
60
61
0/00
1/11
0/01
1/10
0/11
1/00
0/10
1/01
0/00
1/11
0/01
1/10
0/11
1/00
0/10
1/01
0/11
1/00
0/10
1/01

## Slide 10: Quantization of scaling factor ( )
The range of scaling factor can be any number beyond 0, usually ranged between 1 and 16
This scaling factor is quantized once per sensing frame, and without being fed-back per each sub-carrier
The scaling factor can be any real number greater than 0, so we propose to quantize the Decimal number and the fractional value below decimal point separately.
  We assign M bits for the decimal number, and assign K bits for the value below the decimal points
  E.g. M is 4 bits, and K is 12 bits. Then, M bits represent the decimal points from 1 to 16, and K bits provide 212 , 4096 quantization steps between 0 and 1
  For the scaling factor 4.7125762 as an e.g., the decimal number is 0100, and the fractional value below decimal point is quantized by choosing an 12 digit index closest to .7125762

## Slide 11: Simulation
We used the same convolutional scheme as in 802.11 (Slide 5)
We generated the Chan D to measure the CSI information
  Magnitude information is computed per each subcarrier  Rayleigh Distribution  Convert it into Uniform Distribution
8 bit TCQ  n = 8 and N=28=256,
9 bit TCQ  n = 9 and N=29=512
Source to Quantization Noise Ratio (SQNR) : 10log(E(x2)/E(q2)) (dB), where x is the source data and q is the quantization noise
TCQ shows 1 dB gain compared to the Scalar Quantization (SQ)
 | MSE (E(q2)) | SQNR (dB)
TCQ (8bit) | 2.236e-4 | 53.5077
SQ (8bit Scalar Quantization) | 2.894e-4 | 52.3948
TCQ (9bit) | 5.587e-5 | 59.529
SQ (9bit Scalar Quantization) | 7.775e-5 | 58.1106

## Slide 12: Summary
We proposed to use the TCQ scheme to quantize the magnitudes of the measured CSI
  It is provided how to convert the Rayleigh-distributed samples into the Uniformly-distributed samples
This result shows 1 dB better SQNR gain than using the Scalar Quantization

## Slide 13: SP1
Do you support to convert the CSI (CFR) in complex number to the CSI (CFR) in phase & magnitude for the Quantization of CSI ?

## Slide 14: SP2
Do you support to convert the Rayleigh Samples of CSI Magnitudes to the Uniform Distributed Samples before applying a Quantization as described in slide 5?

## Slide 15: SP3
Do you support the TCQ for the Quantization of CSI ?
  Codeword generation of Sub-Codebooks is described in Slide 6 of 21/770r0
  FB informations of the TCQ are Beginning State, input bits, and Codewords index of the corresponding Sub-codebook

## Slide 16: SP4
Do you support the Quantization of Scaling Factor as described in slide 10?

## Slide 17: Reference
[1] C. da Silva, et. al., “Discussion of Sensing Measurement Result Types”, 802.11-21/0357r1, Mar. 2021
[2] J. Zhang, et. al., “Trellis-Coded Quantization of Phases in MISO Wireless Systems”, TELKOMNIKA, Vol.10, No.7, November 2012, pp. 1808~1814
[3] M. Marcellin, et. al., “Trellis Coded Quantization of Memoryless and Gauss-Markov Sources”, IEEE TRANSACTIONS ON COMMUNICATIONS, VOL. 38, NO. 1, JANUARY 1990