## Slide 1
Considerations on Soft AP Power Saving
Date: 2021-11-20
Authors:

## Slide 2: Introduction
For battery powered AP (Soft AP), power saving can be beneficial as discussed in [1]
When multi-link is concerned, power saving is more important for battery powered APs
When there is no STAs associated with a Soft AP, the Soft AP may be able to power down all links until STAs request to associate
There are several possible Soft AP power saving procedures
  Implicit listening interval
  TWT based power saving
  Master link

## Slide 3: ML Soft AP Power Saving (Implicit Listening Interval)
In order for STAs to associate with APs of Soft AP MLD, APs stays awake for some time duration (implicit listening interval) after transmitting a Beacon frame
If there is a transmission from unassociated STAs, an AP of Soft AP MLD shall keep normal mode for a certain time duration

## Slide 4: ML Soft AP Power Saving (Timer Based)
In order for STAs to associate with APs of Soft AP MLD, APs stay awake for some time duration (Timer Based) after transmitting a Beacon frame.
In order for AP to save more power, AP may indicate the waiting time allocation which is after a certain Beacon transmission,

## Slide 5: ML Soft AP Power Saving (TWT based)
In order for STAs to associate with APs of Soft AP MLD, APs stays awake for some time duration (TWT based) after transmitting a Beacon frame.

## Slide 6: ML Soft AP Power Saving (Master Link)
Soft AP can activate one link (Master link) and power off the other links or put them in power save mode
  In Soft AP power save mode, soft AP may transmit Beacon frames for STAs

## Slide 7: Conclusion
Battery powered power saving is important for Soft AP
  Soft AP with multi-link may need efficient power saving methods
In this presentation, various Soft AP power saving procedures were discussed
  Implicit listening interval
  TWT based power saving
  Timer based power saving
  Master link based power saving
Soft AP power saving may be considered in R2

## Slide 8: Reference
[1] 11-20/1115r6 Multi-link for Battery Powered AP MLD