## Slide 1: EBCS Traffic streams
Antonio de la Oliva (Interdigital, UC3M)
Xiaofei Wang (Interdigital)
Joseph Levy (Interdigital)

## Slide 2: Controlling EBCS streaming
Server
Source of EBCS traffic stream
EBCS AP
EBCS STA
EBCS Traffic Category 1
Traffic is streamed without request from STA
(No negotiation)
EBCS traffic stream being tx
Without need of anyone starting it
(e.g., time schedule of buses)
EBCS traffic stream tx by AP without anyone requesting it

## Slide 3: Control loops
For EBCS traffic category 2, 3 and 4, there are two separate EBCS control loops
  1st control loop: starting streaming EBCS traffic from server to EBCS Aps (in blue in the following)
  2nd control loop: starting over the air transmission of the EBCS traffic from a particular EBCS AP

## Slide 4: Controlling EBCS streaming
Server
Source of EBCS traffic stream
EBCS AP
EBCS STA
EBCS Traffic Category 2
Traffic is streamed based on request from STA
(associated or unassociated), consumed by everyone
Option 1.- EBCS traffic stream being tx by server without need of anyone starting it
(e.g., time schedule of buses)
EBCS traffic stream tx if STA request for it, consumed by everyone in the area, regardless of association state
Option 2.- Starting EBCS traffic stream from server
To AP by higher layer request by STA
EBCS traffic stream tx by AP based on request from STA

## Slide 5: Controlling EBCS streaming
Server
Source of EBCS traffic stream
EBCS AP
EBCS STA
EBCS Traffic Category 3
Traffic is streamed based on request from
associated STA, consumed by everyone
Option 1.- EBCS traffic stream being tx by server without need of anyone starting it
(e.g., time schedule of buses)
EBCS traffic stream tx if STA request for it, consumed by everyone
Option 2.- EBCS traffic stream is started
by higher layer request by STA
EBCS traffic stream tx by AP based on request from associated STA

## Slide 6: Controlling EBCS streaming
Server
Source of EBCS traffic stream
EBCS AP
EBCS STA
EBCS Traffic Category 4
Traffic is streamed based on request from
associated STA, consumed by authorised STAs at higher layer
Option 1.- EBCS traffic stream being tx by server without need of anyone starting it
(e.g., time schedule of buses)
EBCS traffic stream tx if STA request for it, consumed by authorized STAs whose have the higher layer key to consume the service
Option 2.- EBCS traffic stream is started
by higher layer request by STA
EBCS traffic stream tx by AP based on request from associated STA