## Slide 1: ANQP Elements Augmentation Proposal
Date: 2021-06-14
Authors:
May 2021

## Slide 2: Abstract
This submission proposes new elements for ANQP

## Slide 3: Background – ANQP in Federations
In large federations (where multiple venues may allow for multiple sources of identities), the multi-to-multi relationship makes it more difficult for the STA profile to understand the expectations of the venue, and how these map to the identity profile that the STA is configured to use
This ambiguity can cause unnecessary overhead, or may cause the STA to send elements that may not be required by the infrastructure (and that can in turn, affect the user privacy or result in a lower user experience)
This submission proposes additional ANQP elements that can clarify the infrastructure expectations

## Slide 4: Advertising Credential Types
In a multi-to-multi environment (e.g., a venue member of a federation), the venue may advertise a RCOI (Roaming Consortium) that includes multiple sources of identity, each with different credential type requirements (e.g. ,simple email, proof of residence, identity validation or other). Each consortium member may also accept multiple types of credentials. However, the venue may also be constrained in the type of credentials it can accept (e.g., ‘only accept credentials where the user identity can be verified’)
It may be useful to define the credentials types that the venue can accept, as this may be a subset of the credentials accepted by all RCOI members (e.g., type of credentials accepted, with type of verification accepted, credential lifetime)
The venue may also mandate that the user connects with verifiable outer identity. In other cases, the venue requirements are satisfied with an anonymous outer identity, provided that an authentication source validates the user credentials. It may be useful to specify if the venue requires a ‘real’ outer identity, to remove the need for clients to expose the user identity where it is not needed.

## Slide 5: Credential Types ANQP-Element
Suggest insert after 9.4.5.29
Credential Types ANQP-Element
The Credential Types ANQP-element provides STA with the information about the types of credentials accepted via that AP. One or more types of credentials are listed.
The credential types subfield includes for each type of accepted credential, the credential type (table 1), the required validation type (table 2), the minimum lifetime required for the credentials, and a privacy indicator.
Info ID
Length
Credential Types
category
validation
B0
lifetime
2
2
variable
octets:
Bits:
B5
B8
B6
B9
B13
Privacy Indicator
B15
B14

## Slide 6: Credential Types ANQP-Element
Insert after 9.4.5.29
Credential Types ANQP-Element (Cont.)
The credential category subfield includes a category of credentials accepted through the AP.
Credential Category | Value
Any | 0
Service Provider | 1
Cloud or Social Media Provider | 2
Enterprise | 3
Government | 4
Automotive | 5
Credential Category | Value
Hospitality | 6
Aviation | 7
Education or Research | 8
Cable Industry | 9
Loyalty or Merchant | 10
Reserved | 11-64

## Slide 7: Credential Types ANQP-Element
Insert after 9.4.5.29
Credential Types ANQP-Element (Cont.)
The validation method subfield lists the type of credential validation that must occur for the credentials to be deemed valid.
The values are inclusive (e.g., 4 indicates that 4 and 5 are accepted).
Validation method | Value | Notes
No verification | 0 | Credentials do not need to be verified
Any method allowed | 1 | Any method, from 1 to 5, is accepted
Email verification | 2 | 
SMS verification | 3 | 
Government ID | 4 | e.g., account obtained by showing a Government ID
Government issued credentials | 5 | e.g., a certificate emitted by a Government
Reserved | 6-7 | 

## Slide 8: Credential Types ANQP-Element
Suggest insert after 9.4.5.29
Credential Types ANQP-Element (Cont.)
The Lifetime subfield indicates the minimum age required for the credentials to be accepted, in units of quarters (e.g., a value of 8 represents that the matching credentials are accepted if the account is more than 8 quarter, or 2 years, old).
When set, the Privacy indicator indicates that this network requires the user to expose a real contactable identity to the network (usually for legal purposes). Default value is 0, indicating that this network will accept anonymous roaming.

## Slide 9: SLA ANQP-Element
Insert after 9.4.5.29
SLA ANQP-Element
The SLA ANQP-element provides STA with the information about the types of credentials accepted via that AP. One or more types of credentials are listed.
Info ID
Length
SLA Indicator
B0
2
2
variable
octets:
Settlement Indicator
Bits:
B1
B8
B2
B3
B7
SLA Details
SLA Indicator
Settlement Indicator
SLA Indicator
Settlement Indicator
1
SLA Indicator
Settlement Indicator
SLA Details
B4
B5
B6
(nx8)

## Slide 10: SLA ANQP-Element
Insert after 9.4.5.29
SLA ANQP-Element (Cont.)
The Settlement Indicator subfield indicates if the network will accept all roaming, offers paid services or free services. The SLA Indicator subfield indicates the SLA that the network offers for the associated settlement. When the SLA is the same for all Settlements values, the Settlement and SLA values are indicated in the first half of the element (e.g., 0011 0000 indicating Gold SLA for all).
The SLA details field is optional, and indicates the details of the SLA. The content of this subfield is outside the scope of this specification.
Settlement Indicator Value | Settlement
0 | All
1 | Free services
2 | Paid services
3 | Reserved
SLA Indicator Value | SLA Level
0 | No SLA
1 | Bronze
2 | Silver
3 | Gold

## Slide 11: Straw Poll
Do you support the addition of the additional ANQP elements presented in this submission?
Yes
No
Abstain