## Slide 1: FT-Friendly PASN
Date: 2021-06-12
Authors:

## Slide 2: Abstract
PASN allows a pre-association encrypted exchange with an AP. There are multiple cases where such exchange has to be repeated with multiple APs in sequence.
  e.g., FTM, 802.11bc EBCS and ANQP exchanges, 802.11aq PAD queries, 802.11be NSEP priority access requests, 802.11 ANQP queries, 11k link measurements and more.
PASN (Draft P802.11az D3.0 12.12.6) allows for an “FT mode”, but supposes that FT key hierarchy has already been established
This submission proposes a PASN-FT scheme to allow for an efficient and protected exchange burst with multiple APs, without the need for initial association.

## Slide 3: High Level Solution Description
The model for PASN-FT is as follows:
  STA establishes a PASN session with a first AP
    PASN mode is PASN, FT support is expressed
    FT Key Hierarchy is derived
  STA uses FT-style Over-the-DS to establish keying with the next AP(s)
  STA can then jump to any other target AP and (almost) immediately proceed to encrypted exchanges
Note that this method is RCM-compatible

## Slide 4: Initial PASN-FT AP Discovery
As expected, the AP advertises support for PASN and FT (+SAE) AKMs in beacons and probe responses
  RSNE includes PASN and FT AKMs and the MDE, with Domain ID and FT capability and Policy field (Over-the-DS FT)
STA / supplicant
AP/ Authenticator
Beacon(RSNE(PASN, FT, AKM),{RSNXE],MDE)

## Slide 5: Initial PASN-FT AP Connection
RSNA Authentication Desired
STA selects the following, based on AP beacons/probe responses:
  PASN as well as FT (+SAE) AKMs
  A Pairwise Cipher Suite for the future PTKSA
  A Finite cyclic group
RSNA Authentication not sought
STA selects the following, based on AP beacons/probe responses:
  A Pairwise Cipher Suite for the future PTKSA
  A Finite cyclic group (at least of security strength provided by advertised MPMK and Cipher suites)
  PASN parameters indicate that FT hierarchy is to be derived (No Base AKM for authentication)
The initial AP connection is identical to PASN.
FT Key hierarchy is derived

## Slide 6: Initial PASN with FT AP Connection (2)
(With finite cyclic group selected), STA generates an ephemeral private key, uses the group’s scalar operation with the private key to generate ephemeral public key
STA builds an RSNE with selected AKM, Pairwise cipher suite, MFPC and MFPR bits (in RSN capabilities field) set to 1 [PMF mandated], Extended key ID for individually addressed frames (bit 13) set to 0 [as cipher suite is not CCMP/CGMP], Group Data Cipher Suite and Group Management Cipher suite set to 00-0F-AC:7 [group addressed traffic not allowed], PMKID count and PMKID list set depending on PMKSA identifiers (if present)
SAE protocol may be tunnelled for initial FT-SAE authentication

## Slide 7: Initial PASN with FT AP Connection – frame 1
Process uses PASN
ISTA sends first PASN frame – uses PASN structure
  Includes RSNE with Base AKM Parameters (list of PMKIDs [0 or more]), STA ephemeral public key, PASN Parameters, (optionally) Base AKM Data, (optionally) Time Interval Element, (optionally) RSNXE
STA / supplicant
AP/ Authenticator
802.11 Authentication(1, PASN, RSNE(Base AKM, PMKID[0…n]), [RSNXE], S-Ephemeral Pub, PASN Parameters, Base AKM Data-1

## Slide 8: Initial PASN with FT AP Connection – AP side
Process uses PASN
AP validates the first frame, builds the second PASN frame
  RSNE contains pairwise cipher, MFPC and MFPR in RSN capabilities field set to 1, No pairwise bit set to 0, PMKID count of 1 and PMKID list corresponding to the PMKID from the PMKSA if applicable, Group Data Cipher Suite and Group Management Cipher suite are set to 00-0F-AC:7 (no group traffic allowed), Extended Key ID for individually addressed frames (bit 13) set to 0
  PASN Parameters Element has the wrapped data format, chosen finite cyclic group ID, and the AP ephemeral public key
  Optionally Wrapped Data Element,
  A MIC Element computed as per 12.12.8.1

## Slide 9: Initial PASN with FT AP Connection – frame 2
Process uses PASN
AP validates the first frame, and responds with second PASN frame
  Includes RSNE with MPMK Parameters and pairwise cipher, AP ephemeral public key, PASN Parameters, (optionally) Base AKM Data, (optionally) Time Interval Element, (optionally) RSNXE
STA / supplicant
AP/ Authenticator
802.11 Authentication(2, PASN, RSNE(Base AKM, PMKID[0…n]), [RSNXE], A-Ephemeral Pub, PASN Parameters, Base AKM Data-2, MIC

## Slide 10: Initial PASN-FT AP Connection – frame 3
Process uses PASN
STA validates the second frame, and responds with third PASN frame
  Status success, includes PASN Parameters Element, optionally Wrapped Data Element, MIC Element
STA / supplicant
AP/ Authenticator
802.11 Authentication(3, PASN, Base AKM Data-3, MIC)

## Slide 11: OTA PASN-FT
FT includes OTA and over the DS modes
  There is no need for an OTA mode with PASN-FT, as STA can establish the PASN connection with the target AP with the same count of frames as the FT-pre-establishment would consume
  There could be a mode for OTA PASN-FT to verify that the target AP is connected over the backend to the current AP, but this is also accomplished by Over-the-DS mode, and thus OTA mode has no clear additional benefit
PASN-FT includes an Over-the-DS mode
  S1KH-ID is STA MAC address – STA can decide of the MAC as it makes the request, i.e., the MAC does not need to be the same for all APs
  If the STA has associated to the first AP with an FT mode, the FT mode is used to carry the Over-the-DS action frame
  If the STA has not associated to the first AP, the current PASN key structure is used to carry over the DS exchange as shown in the following slides

## Slide 12: Over-the DS PASN-FT - 1
STA sends first PASN-FT frame to target AP
  The frame type is action (not authentication as in slide 7), so the frame can be protected (robust)
  In addition to parameters from slide 7, includes MDE, FTE with S1KH-ID
  TBD define Base AKM Data to contain FT information – MDE, FTE(S1KH-ID) etc.
Protected Action [PASN FT(1, PASN, RSNE(Base AKM, PMKID[0…n]), [RSNXE], S-Ephemeral Pub, PASN Parameters, Base AKM Data-1, MDE, FTE (S1KH-ID)]
STA / supplicant
Target AP
AP/ Authenticator

## Slide 13: Over-the-DS PASN-FT - 2
Target AP responds to STA with second PASN-FT frame
  The frame type is action (not authentication as in slide 9), so the frame can be protected (robust)
  In addition to parameters from slide 9, includes the MDE, the Target AP MAC address, the target STA MAC and S1KH-ID, FTIE with timeout value
STA / supplicant
Target AP
Protected Action[PASN FT(1, PASN, RSNE(Base AKM, PMKID[0…n]), [RSNXE], S-Ephemeral Pub, PASN Parameters, Base AKM Data-1, MDE]
AP/ Authenticator

## Slide 14: Over-the DS PASN-FT - 3
STA validates the second frame, and responds with third PASN-FT frame
  The frame type is action (not authentication as in slide 10), so the frame can be protected (robust)
  Status success, includes PASN Parameters Element, optionally FILS Wrapped Data Element, MIC Element, FTE with S1KH-ID and Target AP MAC
STA / supplicant
Target AP
AP/ Authenticator
Protected Action[PASN FT(3, PASN, FT, Base AKM Data-3, MIC, FTE)]

## Slide 15: Open Issues
Protected FTM frames are protected, including pre-association. What other frames are protected pre-association?
Should the pre-association protection mechanism be extended to other frames (e.g., those listed on slide 2)? It seems logical to extend to protected dual of public action frames.
OTA PASN FT would be simpler, but would expose the S1KH-ID. Should we envision a hybrid mode, e.g., where the S1KH-ID is sent over-the-DS, then the exchange is done OTA?

## Slide 16: Straw Poll
Do you support the adoption of a PASN FT mechanism to protect pre-association exchanges over multiple APs?
Yes
No
PASN-who?

## Slide 17: Appendix