## Slide 1: TGbi - Enhancing Privacy – Following a user use case
Date: 2021-05-01
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
Joseph LEVY | InterDigital, Inc. | 111 W 33rd Street New York, NY 10120 | +1.631.622.139 | jslevy@ieee.org

## Slide 2: Abstract
This document describes use cases where following a MAC address across a region leads to potential privacy risks

## Slide 3: Use case description
Hotels or public spaces with WiFi infrastructure allow an attacker to remotely track the presence of a device in the hotel premises.
  Presence or absence of presence within the hotel
  Potentially, room number, or even continuous tracking of location
This may lead to potential privacy risks such as:
  Extra charges for consumption in the hotel while abroad
  Use of credit cards when sleeping or while traveling by plane
  Kidnapping

## Slide 4: Example
Alice checks in a hotel, while doing the registration, she will connect its mobile device to the Hotel’s WiFi.
Bob, a very bad guy nearby, is monitoring the registration desk and capturing MAC addresses used to connect to the Hotel’s WiFi.
Since Alice’s mobile device will use the same MAC address within the hotel, Bob can know when Alice is in the hotel.
Bob follows Alice to her room, to know which room she is in.
Bob can wait in a nearby cafe, until Alice leaves the hotel, and then rob her room.

## Slide 5: Problem 1: statement
Current MAC Address randomization capabilities do not address the issues in this case
  The STA will use the same MAC address while connected to the hotel’s network
  Generating a new randomized MAC address to (re)associate to the hotel’s network does not allow the hotel network identify the user to provide services
  Hotel chains rely on MAC address to provide to provide identification for (re)association.
Mechanisms are needed to provide enhanced privacy.
  Enabling devices to keep connected and be know to the network, but not identifiable/trackable by unauthorized/undesired observers.