## Slide 1: Discussion on the handling of sequential blindness periods for NSTR MLD
Date: 2021-06-30
Authors:
Liuming Lu (OPPO)
Name | Affiliation | Address | Phone | Email
Liuming Lu | OPPO |  |  | luliuming@oppo.com
Lei Huang |  |  |  | 
Chaoming Luo |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
802.11be has specified “35.3.14.7 Medium access recovery procedure” to handle blindness issues due to the NSTR-based interference for NSTR MLD, but the handling of sequential blindness periods has not been considered in 11be Draft 1.0.
This contribution provides the potential issues lying in the sequential blindness periods caused by the NSTR-based interference from the continuous transmissions, and proposes the method to handle the sequential blindness periods.

## Slide 3: Issues
11be Draft 1.0 specifies the mechanism of medium access recovery upon the lost medium synchronization due to the transmission of one PPDU, shown in the following, but doesn’t mention the handling of sequential blindness periods caused by the transmission of multiple PPDUs.
“ STA affiliated with a non-AP MLD that belongs to a NSTR link pair is considered to have lost medium synchronization (due to UL interference) when the other STA, which is affiliated with the same MLD and belongs to that link pair, transmits a PPDU, except under the following condition:
—Both STAs ended a transmission at the same time.
A STA that has lost medium synchronization due to transmission by another STA affiliated with the same MLD shall start a MediumSyncDelay timer at the end of that transmission event if that transmission event is longer than aMediumSyncThreshold. The STA may not start the MediumSyncDelay timer if the transmission event is shorter than or equal to aMediumSyncThreshold. ”

## Slide 4: Issues
When the sequential blindness periods caused by the transmission of multiple PPDUs happen, some issues need to be considered to be handled in order to implement medium access recovery.
Whether the MediumSyncDelay timer expire or reset to zero when the MediumSyncDelay timer has started due to the transmission of PPDU1 and the transmission of PPDU2 begins?
Whether the MediumSyncDelay timer is restarted when the transmission of PPDU2 ends?

## Slide 5: Issues
When the sequential blindness periods caused by the transmission of multiple PPDUs happen, some issues need to be considered to be handled in order to implement medium access recovery.
when the MediumSyncDelay timer has started due to the transmission of PPDU1 and the transmission of PPDU2 begins, the MediumSyncDelay timer doesn’t expire
When the transmission of PPDU2 ends the MediumSyncDelay timer is NOT restarted even if the transmission event of PPDU2 is longer than aMediumSyncThreshold.
This would lead to the inadequate protection provided for the channel in Link2

## Slide 6: Proposals
When the MediumSyncDelay timer has started due to the transmission of PPDU1 and the transmission of PPDU2 begins, the MediumSyncDelay timer expires or resets to zero if the transmission event of PPDU2 is longer than aMediumSyncThreshold.
When the transmission of PPDU2 ends the MediumSyncDelay timer is restarted

## Slide 7: Proposals
If the MediumSyncDelay timer has started due to the transmission of PPDU1, the MediumSyncDelay timer doesn’t expire when the transmission of PPDU2 begins or ends if the transmission event of PPDU2 is not longer than aMediumSyncThreshold.
When the transmission of PPDU2 ends the MediumSyncDelay timer is NOT restarted.

## Slide 8: Summary
This contribution provides the potential issues lying in the sequential blindness periods caused by the NSTR-based interference from the continuous transmissions, and proposes the method to handle the sequential blindness periods, which can be considered to improve the specification of “35.3.14.7 Medium access recovery procedure” .

## Slide 9: Reference
[1] IEEE 802.11be Draft 1.0
Liuming Lu (OPPO)