## Slide 1: A framework for E/DMG monostatic radar PPDU
Date: 2021-06-10
Authors:

## Slide 2: Abstract
The following document discusses a framework for a PPDU format that can be used for monostatic radar the mmWave bands (E/DMG)

## Slide 3: What we have today
The whole PPDU may be used for radar
  using preamble fields and TRN subfields for radar is preferred because the waveforms have better correlation properties
The maximum length of a DMG TRN field is 34usec. The maximum length of an EDMG TRN field is 4.2ms, however, the PPDU length is limited to 2ms.

## Slide 4: What happens when an (uninvolved) STA receives a PPDU with TRN fields
If the PPDU is a (DMG) TRN-R or EDMG-TRN-R PPDU
  It may perform measurements on the TRN field
  However, since the PPDU was not addressed to it, it will not use the measurement
If the PPDU is a (DMG) TRN-T or EDMG-TRN-T/R-T PPDU
  It may perform measurements on the TRN subfields
  Since the frame was not addressed to it, The MAC will discard the results.
Simply put – PHY may perform measurements, MAC ignores.

## Slide 5: What can an uninvolved STA expect from a TRN field
The PPDU is a TRN-R PPDU, the TRN field is transmitted using the same antenna pattern as the preamble.
If the PPDU is a TRN-T or R-T PPDU, the TRN field may be transmitted using totally different antenna pattern,
  The signal power may change drastically from one TRN-T subfield to the other. It may disappear or become much stronger.
  There can be no assumption on the level of the signal received during the TRN field

## Slide 6: What will happen if a radar transmits non-standard waveform during the TRN field in uninvolved STAs
Nothing!
The uninvolved STAs will receive the signal as if standard compliant signal was transmitted, its MAC will ignore it.
There is no need for interoperability in the transmitted waveform, since only the transmitter needs to receive it
Hence:
Any waveform can be transmitted by a monostatic E/DMG device as part of a of the TRN field of a valid TRN-T PPDU as long as it complies with :
  Length,
  Power,
  Power spectral density,
  Occupied bandwidth,
Of a valid TRN field

## Slide 7: Conclusion
There is no need to define a waveform for a E/DMG monostatic radar/sensing
A monostatic radar may use the time of the TRN field of a TRN-T or R-T E/DMG PPDU for transmitting any type of waveform if it complies with the TRN field:
  Power
  Occupied bandwidth
  Length
  Power Density
The monostatic radar shall still comply with all DMG access rules
Data field must contain a valid MAC frame
Note:
  Waveforms may need to be specified for multi-static radars/sensing

## Slide 8: References