## Slide 1: 802.11bc Architecture Discussion
Date: 2021-06-21
Authors:

## Slide 2: Abstract
This document discusses the 802.11bc architecture and proposes a way forward that is compatible with the existing 802.11 architecture while supporting the new capabilities provided by 802.11bc.
r0: Initial draft for discussion

## Slide 3: Enhanced Broadcast Services (EBCS) Supported by 802.11bc
DL EBCS:
  AP is configured by the network administrator to transmit group addressed frames containing specific content from a content server(s) (e.g., station information (gate, destination, boarding time, departure time))
  AP advertises broadcast services that it can provide (configured by network administrator), STAs request services, AP transmits group addressed frames containing the requested content provided by a content server.
UL EBCS:
  An un-associated STA transmits a frame intended for a Server, an AP that receives the transmission forwards the frame to the Server.
802.11bc provides the ability to support these services by adding 802.11 functionality, it does not provide specifications or requirements for any behaviour necessary to support these services beyond the scope of 802.11

## Slide 4: Big Picture for 802.11bc
DL Data Flow for EBCS
UL Data Flow for EBCS
Note: EBCS Proxy Server is shown inside the DS, it may also be outside the DS

## Slide 5: 802.11bc Basic Assumptions
All DL data streams to be broadcast are sourced by an entity outside the purview of 802.11, a content server.
A network administrator will configure the APs and the DS to:
  Transmit broadcast streams that will always be broadcasted (e.g., train timetables)
  Advertise which broadcast streams are available to be broadcasted
  To “receive” the broadcast streams from the content server(s)
  Enabled/disable forwarding of UL broadcast data frames
The AP will be capable of “filtering” (choosing) which DL broadcast streams are transmitted, based on its configuration and requests made by STAs
When the AP receives an UL broadcast, it will forward the UL broadcast to the appropriate Proxy Server, if the service is enabled on the AP
802.11bc should minimize 802.11 and network architecture “changes” so that implementation of 802.11bc does not have a high implementation threshold

## Slide 6: Hence it is Preferred to
Not add a SAP to current 802.11 Architecture
Make no changes to the DS or how the DS connects to the AP or Portal
Minimize any architecture change to provide the required functionality
Therefore, the preferred way forward is to:
Add a “filter” which will control which DL broadcast streams are transmitted
Enable the AP to process STAs’ request for DL broadcast streams
Add all control/configuration capabilities to allow a network administrator to configure the AP to provide 802.11bc services.
Add a “proxy” which will forward UL broadcast streams to the appropriate server

## Slide 7: Current 802.11 Data Plane Architecture
Non-AP STA
AP
Note: DA address filtering may be implemented “lower in the stack”
Note: In an AP there is no connection from the Role specific behavior box to the upper layers. The control port only connects to the DSAF.
These diagrams are Figures 5-1, 5-3, and 5-4 from IEEE Std. 802.11-2020

## Slide 8: EBCS AP Data Plane
For .11bc DL broadcast:
EBCS Filtering is added to the transmission flow, providing the AP the ability to control which EBCS MPDUs received are transmitted. The filter parameters are configured by the network administrator and requests received from STAs.
For .11bc UL broadcast:
The address 1 address filtering is enhanced to filter/tag UL HLP frames so they will be process by the EBCS Addressing Proxy. The EBCS Addressing Proxy is configured by the network administrator to enable the DS to route the received HLP MSDUs to the EBCS Proxy Sever. The EBCS Proxy Server will process the HLP frame and forward it to the target server with all necessary information fields.

## Slide 9: UL EBCS Flows – Proxy Server Location?
Two EBCS Proxy Server location are show:
If the proxy server is in the DS, the DS will know the MAC address of the server which is shared with the APs in the DS, all HLP frames addressed are routed by the DS to the proxy server.
If the server is beyond the portal, the portal provides a MAC address to the DS for the proxy sever and all HLP frames are routed through DS to the portal to the proxy server.
Both locations are possible and should be supported.
Either way the network administrator must configure the network so that APs address the UL HLP frames to the EBCS Proxy Server.

## Slide 10: References
Draft P802.11bcD1.03
11-21/0900r4 EBCS Architecture Hitoshi Morioka (SRC Software)
11-21/0791r5 Clause 11 Discussion Hitoshi Morioka (SRC Software)