## Slide 1: DS and Portal concepts and models
Date: 2021-07-15
Authors:

## Slide 2: Abstract
This presentation considers architecture concepts for DS, Portal and attached APs, and attempts to relate the concepts to implementation options.
The contents here are meant to be tutorial in nature.

## Slide 3: DS, Portal and attached AP concepts
The DS and Portal are architectural concepts only. Care needs to be taken to not try to map these concepts directly to actual implementation(s).
This presentation gives the logical view of these concepts, followed by some examples and discussion of how they *might* appear in an implementation.

## Slide 4: DS, Portal and attached AP concepts
The Distribution System (DS) and Portal are architectural concepts only. Care needs to be taken to not try to map these concepts directly to actual implementation(s).
This presentation gives the logical view of these concepts, followed by some examples and discussion of how they *might* appear in an implementation.
Neither the DS nor Portal are fully specified by IEEE Std 802.11. Rather, 802.11 provides a description of the service provided by these components, and some requirements on externally visible behavior, and leaves the details of how these are accomplished as implementation choice.

## Slide 5: Reminder of 802.11 as a MAC service
IEEE Std 802.11 provides a “black box” MAC sublayer service to various user devices. The user devices are the Portal, and non-AP STAs (for infrastructure BSSs), and source and destination mesh STAs (for MBSSs).
All interactions within this “black box” are transparent to the LLC sublayers within the user devices. The entire architectural model of 802.11 should be viewed as a monolithic solution that delivers MSDUs from one LLC sublayer to a peer LLC sublayer, possibly including interconnection to other IEEE 802 family standards also providing MAC sublayer services. (Cf: IEEE Std 802.1AC-2016, Figure 9-1)

## Slide 6: Definitions (from REVme D0.1)
distribution system (DS): A system used to interconnect a set of basic service sets (BSSs) and integrated local area networks (LANs) to create an extended service set (ESS).
portal: The logical point at which the integration service is provided.
NOTE—For the purposes of this Standard, there is at most one portal in a given extended service set’s (ESS’s) infrastructure. In an implementation, a single logical portal function may be provided by multiple devices that provide integration services for the ESS. How such multiple devices coordinate to appear as a single logical portal is implementation dependent.

## Slide 7: DS service
The definition of the service expected from the DS is provided in clause 7 of IEEE Std 802.11. In summary, there are two services:
Delivery of MAC service tuples between APs, mesh gates, and the portal
Maintenance of a mapping of STA MAC addresses to the set of attached APs and mesh gates.
The DSAF (distribution system access function) provides the connection from APs and mesh gates to the DS.
It is important to note that the DS _provides_ a service to the DSAFs. That is, the DSAF is a service user of the DS SAP.
How the DS provides the service is unspecified, and may (likely) include use of other 802 Standards and/or other communications standards. While the DS is itself part of providing the 802.11 MAC service, the DS implementation may include higher-layer service(s) that are invisible to the MAC service users.

## Slide 8: Portal
The Portal is modeled as the _only_ point that interconnects a DS to non-802.11 LAN.
The Portal connects to the DS via the integration service, which provides any necessary mappings or transformations of the DS service to the MAC service of the external LAN.
While the Portal is modeled as a single point, in an implementation it could be a distributed function, occurring across multiple physical devices.

## Slide 9: Conceptual model
Modified from Figure 7-1, REVme D0.1
Also note other concept diagrams such as Figures: 4-2, 4-6, and 4-9

## Slide 10: Simplified model
Use this model as a reference, on remaining slides

## Slide 11: “802.11 sourced” MSDU process
Consider an MSDU generated at the leftmost MAC sublayer service user:
The MSDU is delivered into the 802.11 scope, via the MAC SAP to the non-AP 802.11 stack on the left. This includes the SA, DA, user data, and other details per the MA-UNITDATA.request primitive.
The MSDU is delivered through the AP, to the DS (at the DS SAP), as part of a MAC Service tuple.

## Slide 12: “802.11 sourced” MSDU process
(Continued):
The DS considers the DA:
  If the DA is the broadcast address:
    The DS delivers the MSDU to all DS SAPs, including back to the same DS SAP that provided it originally. <Done>
  If the DA is a multicast address:
    The DS could be “simple”, and deliver the MSDU as if it were broadcast (per just above) <Done>; OR
    The DS could use any (standardized or proprietary) method to “prune the tree”, and deliver the MSDU only to those DS SAPs that map to (one or more) destination MAC SAPs that should receive the MSDU. <Done>

## Slide 13: “802.11 sourced” MSDU process
(Continued):
The DS considers the DA:
  If a directed address, consult the mapping database:
    If an entry exists, it will _by definition_ result in a single exit point DS SAP. Deliver the MSDU there. <Done>
    If there is no entry in the database for this DA, deliver it to the Portal, at the Portal’s DS SAP.
    NOTE: The (3)(c)(ii) delivery is why the Portal is modeled as a _single_ point in the ESS. Any complexity resulting from an implementation having more than one Portal is implementation-specific, and out of scope.

## Slide 14: “802.11 sourced” MSDU process
(Continued):
The Portal uses the integration function to map the MAC service tuple appropriately for the non-802.11 MAC, and delivers the MSDU (using an MA-UNITDATA.request) to the non-802.11 MAC service.
The non-802.11 MAC delivers to the destination. <Done>

## Slide 15: “External sourced” MSDU process
There is really very little difference for MSDUs which originate on a MAC service user not connected to the 802.11 domain.
The “802.11 sourced” flow is reproduced below, with differences shown in italics.

## Slide 16: “External sourced” MSDU process
Consider an MSDU generated at the rightmost MAC sublayer service user:
The MSDU is delivered into the 802.11 scope, via an indication at the (non-802.11) MAC SAP attached to the Portal. This includes the SA, DA, user data, and other details per the MA-UNITDATA.request primitive.
The Portal uses the integration function to map the indication into a MAC service tuple appropriate for the DS SAP and delivers the MSDU to the DS (at the DS SAP), as part of a MAC Service tuple.

## Slide 17: “External sourced” MSDU process
(Continued):
The DS considers the DA:
  If the DA is the broadcast address:
    The DS delivers the MSDU to all DS SAPs, except is not reflected back to the Portal. <Done>
  If the DA is a multicast address:
    The DS could be “simple”, and deliver the MSDU as if it were broadcast (per just above) <Done>; OR
    The DS could use any (standardized or proprietary) method to “prune the tree”, and deliver the MSDU only to those DS SAPs that map to (one or more) destination MAC SAPs that should receive the MSDU. <Done>

## Slide 18: “External sourced” MSDU process
(Continued):
The DS considers the DA:
  If a directed address, consult the mapping database:
    If an entry exists, it will _by definition_ result in a single exit point DS SAP. Deliver the MSDU there. <Done>
    If there is no entry in the database for this DA, (potentially something went wrong in the non-802.11 network and this shouldn’t happen? This detail is out of scope), ignore the MSDU. <Done>

## Slide 19: Real-world practicalities
Implementation mental-model 1:
One possible actual implementation, which is often a useful mental model:
Assume a controller-based AP structure
Proprietary links to the APs, that support exactly the DS SAP:
  Transfer MSDUs, via MAC Service tuples, to/from the AP and controller
  APs send “update” commands to maintain the mapping database
No direct connection to AP for management, etc.
  APs don’t even have MAC addresses
The APs are relatively “dumb”:
  Packets in on the WM get Address 1 and Address 3 filtering (per 10.2.8)
  Otherwise, all MSDUs are forwarded to the controller, without further processing/checks

## Slide 20: Implementation “model” 1

## Slide 21: Real-world practicalities
Implementation mental-model 2:
More realistic, but less useful mental model:
“Standalone” APs, with direct connection to 802.3
APs probably discover each other on the 802.3 network via proprietary protocol.
DS function is “distributed”
  Each AP encapsulates MAC Service tuples, and forwards to other APs, as appropriate (proprietary method)
Portal function is “distributed”
  Each AP can put MSDUs directly to/from the 802.3 network in ‘native form’ for connection outside 802.11 scope
APs have management interface and MAC Address, but that is a separate plane, and must not be confused with the logical AP/DS/Portal data plane, even though they share the 802.3 interconnection.

## Slide 22: Implementation “model” 2