## Slide 1: Device Fingerprinting Leading to PCI Capture
Date: 2021-08-12
Authors:

## Slide 2: Abstract
Personally Correlated Information may be captured and utilized to obtain Personally Identifiable Information from unencrypted frames (Probe Request, Authentication, Association).

## Slide 3: Background
Capturing many different 802.11 packet flows and performing analysis on them has led to some conclusions with regards to information which may be gathered from devices.
Per previous presentations around ‘device fingerprinting’ I’ve done some analysis on data captures and will offer some use cases where this data may be used to:
  Correlate Information on devices
  Provide PCI from devices
  Possibly provide PII from devices

## Slide 4: Directed Probes
Clients which actively probe by placing an SSID in the SSID Parameter TLV become trivial to track.
  Tag: SSID parameter set: ARRIS-IOT-5G
  Tag Number: SSID parameter set (0)
  Tag length: 12
  SSID: ARRIS-IOT-5G
Multiple Directed Probes from the same device makes the device even easier to track
  Apple_b1:a9:f0 Broadcast 802.11 217 Probe Request, SN=847, FN=0, Flags=........C, SSID=TMobileWingman
  Apple_b1:a9:f0 Broadcast 802.11 183 Probe Request, SN=788, FN=0, Flags=........C, SSID=ARRIS-IOT-5G

## Slide 5: Directed Probes
Users who utilize personally identifiable information in their network’s SSID open themselves to further information gathering including PII.
  Tag: SSID parameter set: JohnDoe24 (name changed to protect the innocent)
  Tag Number: SSID parameter set (0)
  Tag length: 12
  SSID: JohnDoe24 (name changed to protect the innocent

## Slide 6: Directed Probes
A system capturing Probe Requests for analysis may obtain PCI and sometimes PII from devices which perform directed Probe Requests.
This will be difficult to address without a loss of some speed in (re)association times when (re)joining a network.
  Possible Solutions
    Only use directed probes when in proximity to the ‘known’ network
      Drawback is time to perform passive scans prior to directed Probes
    Advise STA devices to NOT perform directed probes, only Wildcard SSID Probes.
      May break current functionality or increase association times.

## Slide 7: Capabilities Reporting
  IEEE 802.11 Wireless Management
  Tagged parameters (153 bytes)
  Tag: HT Capabilities (802.11n D1.10)
  Tag: Extended Capabilities (8 octets)
  Tag: Interworking
  Tag: VHT Capabilities
  IEEE 802.11 Wireless Management
  Tagged parameters (63 bytes)
  Tag: SSID parameter set: home_ssid
  Tag: Supported Rates 6, 9, 12, 18, 24, 36, 48, 54, [Mbit/sec]
  Tag: HT Capabilities (802.11n D1.10)
  Tag: VHT Capabilities
IEEE 802.11 Wireless Management
Tagged parameters (137 bytes)
Tag: Supported Rates 1(B), 2(B), 5.5(B), 11(B), [Mbit/sec]
Tag: Extended Supported Rates 6, 9, 12, 18, 24, 36, 48, 54, [Mbit/sec]
Tag: DS Parameter set: Current Channel: 6
Tag: HT Capabilities (802.11n D1.10)
Tag: Extended Capabilities (8 octets)
Ext Tag: HE Capabilities (IEEE Std 802.11ax/D3.0)
Most STAs when Probing include a great amount of information regarding Device Capabilities. Examples are given below:

## Slide 8: Capabilities Gathering
Generally, there is enough unique information within the capability elements broadcast by a STA to be able to fingerprint a device (or device manufacturer).
Capabilities which are gathered can be analyzed by back-end systems capturing Probes to gain PCI information which could lead to PII information outside of the Network
  Example, a device probes within an Apple Store. APs and backend systems determine there is device which is VHT capable and is a Samsung device. A text is sent to an associate to look for a person with a Samsung device or a device that could be upgraded to an HE capable device.

## Slide 9: Vendor Specific Information
IEEE 802.11 Wireless Management
Tag: Vendor Specific: Apple, Inc.
Tag: Vendor Specific: Microsoft Corp.:
Tag: Vendor Specific: Broadcom
IEEE 802.11 Wireless Management
Tag: Vendor Specific: Microsoft Corp.: WPS
Tag: Vendor Specific: Wi-Fi Alliance: P2P
Tag: Vendor Specific: Microsoft Corp.:
Tag: Vendor Specific: Broadcom
IEEE 802.11 Wireless Management
Tag: Vendor Specific: Broadcom
Tag: Vendor Specific: Epigram, Inc.: HT Capabilities (802.11n D1.10)
IEEE 802.11 Wireless Management
Tag: Vendor Specific: Wi-Fi Alliance: Multi Band Operation - Optimized Connectivity Experience
IEEE 802.11 Wireless Management
Tag: Vendor Specific: Microsoft Corp.: WPS
Many devices place Vendor Specific Extensions in Probes. This Vendor Specific Information may allow back end systems to further fingerprint devices.

## Slide 10: Directed Probes
Straw Poll 1)
Is the use of directed Probes from a STA a use case this working group wishes to address?

## Slide 11: Capabilities Advertisements
Straw Poll 2)
Is the advertisement of device capabilities which may be gathered and utilized to gather PCI which may lead to PII information gathering something this working group wishes to address?

## Slide 12: Vendor Specific Information
Straw Poll 3
Is the advertisement of Vendor Specific Information which may lead to device fingerprinting and/or PCI information gathering something this working group wishes to address?

## Slide 13: References
Document references
Why MAC Address Randomization is not Enough: An Analysis of Wi-Fi Network Discovery Mechanisms
11-21-0839r0, 11-19-0489r0, 11-20-940r0, 11-20-746r1