## Slide 1: Redundant Transmission for Enhanced Reliability and Reduced Latency
Date: 2021-07-21
Authors:

## Slide 2: Background
One of 11be needs: with the high throughput and stringent real-time delay requirements of these applications, users expect enhanced throughput, enhanced reliability, reduced latency and jitter, and improved power efficiency in supporting their applications over WLAN. [1]
3GPP New Radio introduces PDCP PDU duplication transmission over multiple cells for URLLC (Ultra Reliable Low Latency Communications).
  Copies of a PDCP PDU are concurrently delivered to be transmitted over multiple cells and stopped as soon as there is a copy transmitted successfully.
  The latency of the PDCP PDU is the latency of the copy first successfully transmitted.
  It is straight forward to achieve Ultra Reliability.
Multi-link is introduced in 11be.
  Similar mechanism can be taken into consideration.

## Slide 3: Discussion
Which data to be applied with redundant transmission?
  The data of TIDs that need enhanced reliability and reduced latency, or
  The data of TSIDs that need enhanced reliability and reduced latency, or
  Other ways to identify the data?
Over which links the redundant transmission is applied?
  Data’s TID mapped links, or
  Any other considerations?
When to stop redundant transmission of a MSDU?
  Until the MSDU is transmitted successfully, or
  As soon as the MSDU is transmitted with a copy over each permitted link, or
  Any other conditions?

## Slide 4: Discussion
Redundant Transmission can be up to implementation. However some specification is needed to
  register redundant transmission service on the AP side
  prohibit abuse of redundant transmission should be prohibited
  introduce optimizations
  etc.

## Slide 5: Proposal
To achieve enhanced reliability and reduced latency, redundant transmission of MSDU or MPDU over a subset of multiple links between 2 MLDs is introduced in 11be R2.

## Slide 6: SP1
Do you support to introduce redundant transmission of MSDU or MPDU over a subset of multiple links between 2 MLDs in 11be R2 ?
  Option 1, Yes
  Option 2, No
  Option 3, Abstain

## Slide 7: Reference
[1] https://www.ieee802.org/11/PARs/P802_11be_PAR_Detail.pdf