## Slide 1: Changing STA MAC addresses per association
Date: 2021-09
Authors:

## Slide 2: Abstract
Problems: Client identifiers sent in clear OTA should change frequently, however:
  Regarding STA MAC address used OTA as TA/RA in 802.11 baseline
    TA/RA allowed to change for each association. However, not done due to impact on DS.
    TA/RA currently must persist for association, since AP processes received packets based on STA MAC address.
  Regarding STA MAC address used as SA/DA in the DS
    Legacy devices send & receive other devices SA/DA OTA. SA/DA available to all devices on DS. Potential Privacy issue.
    If SA/DA can change, should still persist for each association, to avoid impacting higher layer protocols.
  DS needs a client identifier persisting across multiple associations for managing connections.
Notes:     For example, a client might be associated with the AP in a vehicle for an extended period. If the client’s over-the-air (OTA) MAC address does not change, then the movement of the user can be determined.
    Similarly, if a client is associated with a stationary AP for an extended period, then presence of the OTA MAC address can be used to infer that the user has remained in radio range of the station AP.

## Slide 3: For Reference: Address fields
TA = MAC address of the AP/STA transmitting the frame
RA = MAC address of the AP/STA receiving the frame
SA = MAC address of the source device (wired or wireless) of the frame
  Can be the same as TA
DA = MAC address of the destination device (wired or wireless) receiving the frame
  Can be the same as RA

## Slide 4: Issues with Changing the OTA MAC address between Associations
802.11 baseline supports a client changing MAC address for each association.
Changing MAC address for each association causes issues in the DS
  Theses issues caused by DS management relying on a persistent MAC address to identify client.
  Consequently, clients do not change MAC address for each association
A persistent client identifier is needed which the DS can use to correlate multiple associations from the same client.
  This seems related to TGbh work is identifying and addressing issues related to changing the MAC address between associations.

## Slide 5: Potential Solution: 3 Tiers of Client Identifier using MLO Architecture
Identifier | Usage | Potential Solution | 
 |  | Identifier Persistence | Visibility over the air
Affiliated STA MAC addresses | Identifying Client using TA or RA in over the-air frames | Change randomly for each association. Optionally change within long-term associations. | Unencrypted (in the clear)
Non-AP MLD MAC Address | Identifying Client using SA or DA in DS frames | Can change randomly for each association1 | Unencrypted (in the clear) or Encrypted2 (hidden) TBD
 |  | Can persist across associations1 | Encrypted2 (hidden)
Persistent Identifiers | E.g. Identifying Client across multiple associations with same trusted network. | Maybe in scope of TGbh | Encrypted (hidden)
    If higher layer protocols sessions continue to new association, then keep existing MAC address If higher layer protocols sessions do not continue to new association, then change MAC address
    In 802.11be, non-AP MLD MAC address is current exchanged in the clear (un-encrypted). This would need to change.

## Slide 6: Slide to add to 11-21-0641-r2 “Proposed Issues” (Use cases)

## Slide 7: X) STA MAC address persistence
Problem/Issue
Current STA MAC address usage presents challenges to providing privacy.
  MAC address used for TA/RA does not change
  MAC address used for DA/SA does not change
Additional challenges
  DS requires an identifier for correlating associations from a single STA
    Currently using the MAC Address, and we want to change MAC address to improve privacy
  MAC address for DA/SA is used in upper layers. Changing these within association impacts upper layers
  MAC address for TA/RA is used for received packet filtering at the AP.
Status
  [Text indicating when use case was presented and any agreements on the use case.]
Reference
(This contribution)

## Slide 8: SP1
Do you agree to include this “STA MAC address persistence” issue in document “21/641 Proposed Issues”?