## Slide 1: Further consideration on sensing measurement flow for non-AP initiator
Date: 2021-08-08
Authors:

## Slide 2: Motivation and Abstract
  The collaborative WLAN Sensing were discussed in 11bf:
  It takes more benefits than overhead on collaborative WLAN Sensing which multitude of Wi-Fi devices with group-based WLAN sensing are collaborated. [20/1533r, 21/0145r5]
  Sensing measurement flows involves non-AP initiator, an AP responder and other non-AP STA responders.[21/0990r2]
  In this contribution, we further consideration on Sensing measurement flow for non-AP initiator, involves AP as coordinator and other non-AP responders case.
  Since the AP knows all the parameters and schedules, and the non-AP initiator may not knows/ fully knows the abilities of other surrounding non-AP STAs. Therefore, at least one AP should participate in the sensing session initiated by the non-AP STA, and this AP can collaborate with other non-AP STA involved and coordinate the sensing session.

## Slide 3: Assumptions
  It is assumed the other non-AP STA responders are associated to the AP responder.
  Considering NDP based sensing measurement, it will be either non-AP STAs transmits sensing PPDUs to the AP, or the AP transmits sensing PPDUs to non-AP STAs.
  AP requests other non–AP responder involved and negotiate their role the same as non-AP STA initiator for sensing measurement.
  Adopt generic Trigger-based flow for measurement phase. The AP as scheduler to exchange and assign all sensing parameters and dynamic communicate with each non-AP STA responder participating in the sensing measurement.

## Slide 4: Flow: initiator is non-AP STA
  Initiator is transmitter
  AP negotiate with other non-AP responder
  The information of participated non-AP responder(s) could be informed to Initiator
AP
STA1
(Sensing Initiator)
(Sensing Transmitter)
STA2
STA3
(Sensing Responder)
(Sensing Receiver)
(Sensing Responder)
(Sensing transmitter)
Sensing Negotiation
Sensing Measurement
Report
(Sensing Responder)
(Sensing transmitter)
Sensing Negotiation
Sensing Measurement
Sensing Negotiation
Sensing Measurement

## Slide 5: Flow: initiator is non-AP STA
  Initiator is receiver
  AP negotiate with other non-AP responder
  The information of participated non-AP responder(s) could be informed to Initiator
AP
STA1
(Sensing Initiator)
(Sensing Receiver)
STA3
STA2
(Sensing Responder)
(Sensing Transmitter)
Sensing Negotiation
(Sensing Responder)
(Sensing Receiver)
(Sensing Responder)
(Sensing Receiver)
Sensing Measurement
Sensing Measurement
Sensing Negotiation
Sensing Measurement
Sensing Negotiation
Feedback
Report
Feedback

## Slide 6: Straw Poll #1
Do you agree with the following?
  If the sensing initiator is a non-AP, AP could negotiate with other non-AP responder, and coordinate non-AP initiator and other non–AP responder for sensing measurement.
  Y/N/A

## Slide 7: Straw Poll #2
Do you agree with the following?
  If the sensing initiator is a non-AP, AP can response initiator with other non-AP responder(s)’s profile.
  The details of profile is TBD.
  Y/N/A

## Slide 8: References
[1] IEEE 802.11-21/0145r5
[2] IEEE 802.11-21/0990r2
[3] IEEE 802.11-20/1533r0