## Slide 1: Threshold Based Sensing Procedure
Date: 2021-08-05
Authors:
Name | Affiliation | Address | Phone | Email
Mengshi Hu | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | humengshi@huawei.com
Rui Du |  |  |  | 
Chenchen Liu |  |  |  | 
Yi Lv |  |  |  | 
Danny Kai Pin Tan |  |  |  | 

## Slide 2: Introduction (1/3)
In [1][2], a threshold based sensing procedure was proposed to help find the receivers with large CSI variations.
The CSI variation measured at the receiver is used to indicate the motions of objects.
Only the receiver detecting a large CSI variation compared with a threshold will be triggered to have a further feedback in Procedure B.
The overhead reduction results from the reduced number of receivers triggered in Procedure B. If the CSI variations of all devices are relatively small, only Procedure A is needed in the threshold based sensing procedure.
Procedure A
Overhead A (small)
Procedure B
Overhead B (large)

## Slide 3: Introduction (2/3)
A motion related to the above threshold based procedure has passed [3]:
A threshold is used for the comparison with the CSI variation, but it is not clear how to signal this threshold in the threshold based sensing.
In this contribution we give an example on the whole procedure related to the threshold used for the threshold based sensing.
The 11bf amendment defines an optional threshold based measurement and reporting procedure in which
The difference between the current measured CSI and the previous measured CSI is quantified. The difference is referred to as CSI variation.
A threshold value to be used by the sensing receiver in the threshold based procedure is defined.
By comparing the CSI variation with the threshold, the sensing receiver can send a feedback resulting from the large CSI variation to the sensing transmitter.
Whether the threshold is predefined, or defined by the sensing receiver, transmitter, initiator or responder is TBD.
The threshold based procedure is not always required (Procedure A in 21/0351r5 is not always required).

## Slide 4: Introduction (3/3)
To make the discussion clear, we first introduce the procedure of the Sensing.
Before the sensing session, there exists a phase for discovery.
Four phases exist in the sensing session (Setup/Measurement/Reporting/Termination).
In the following slides, the procedure related to the threshold for the threshold based sensing is discussed on the basis of the following procedure.
Discovery
Capabilities exchange
Example: In association
Sensing Session
Contains one or more of the following phases
Setup phase
Setup of the sensing session
Measurement phase
The phase doing measurement
Reporting phase
Feed back measurement results
Termination phase
Termination (Explicit or Implicit)

## Slide 5: Info Exchange in Discovery Phase
The following information (an example) can be exchanged in the Discovery phase:
Information | Note
Initiator/Responder/Transmitter/Receiver | Indicating supported roles
Threshold Based Sensing Support | 0: Not support & 1: Support
Changeable Threshold Support (in a sensing session) | 0: Not support & 1: Support
Delay Support (in threshold based sensing) | 0: Not support & 1: Support
… | …
Discovery
Sensing Session
Setup phase
Measurement phase
Reporting phase
Termination phase

## Slide 6: Tell Threshold in Setup Phase
An example: The initiator can send a Sensing Request frame in the Setup phase to establish one or more sensing sessions.
The threshold can be either in Common field or in Per User field.
Note: This is only an example showing that the threshold can be determined by the initiator. People can have different designs for the setup establishment.
Discovery
Sensing Session
Setup phase
Measurement phase
Reporting phase
Termination phase
Common | Per User | Per User | Per User | …
Measurement Setup ID | Receiver Feedback Type | Transmitter Feedback Type
Changeable | Delay | Common Threshold value | …
Info in Common
Role Dependent User Info | …
Info per user
AID | Responder Role (Transmitter/Receiver) | Threshold value

## Slide 7: Change Threshold in Measurement/Reporting Phase
Discovery
Sensing Session
Setup phase
Measurement phase
Reporting phase
Termination phase
The initiator can change the threshold in the Measurement/Reporting phase, if the threshold is allowed to change in a sensing session:
Example 1: If the initiator is a transmitter, the threshold can be changed by NDPA in Measurement phase and Feedback Request in Reporting phase.
Example 2: If the initiator is a receiver, it can tell the transmitter the threshold in Feedback Response, and the transmitter can sent it to the responders next time through NDPA.
Example 3: If the initiator is neither a transmitter nor a receiver, we assume there exists a response sent by the initiator for the feedback in this case, and the threshold can be changed in the Response frame.
Note: For simplicity, changing threshold can be supported only in the case that the initiator is a transmitter. Another choice is that the threshold is unchangeable in a Sensing Session.

## Slide 8: Conclusion
Provided examples for the threshold signaling on the basis of the current sensing procedure.
Info exchange in Discovery phase
Tell the threshold in Setup phase
Change the threshold in Measurement/Report phase (This can be disallowed)
As shown in the given examples, it is natural for the initiator to determine the threshold.

## Slide 9: References
[1] 11-21-0351-05-00bf-threshold-based-sensing-measurement
[2] 11-21-1069-05-00bf-threshold-based-sensing-measurement-follow-up
[3] 11-20-1874-13-00bf-tgbf-motions-list

## Slide 10: Straw Poll 1
Do you agree that in the threshold based sensing measurement and reporting procedure, the threshold compared with the CSI variation value is determined by the initiator?
Y
N
A