## Slide 1: Privacy Protection Gaps
Date: 2021-08-24
Authors:
Name | Affiliations | Address | Phone | Email
Thomas Derham | Broadcom |  |  | thomas.derham@broadcom.com
Nehru Bhandaru |  |  |  | 

## Slide 2: Abstract
This contribution aims to highlight examples of PII and PCI in 802.11 stack, use cases in which they impact user privacy, and potential solution space

## Slide 3: Introduction
11aq amendment defines MAC address randomization by non-AP STA
  STA might use a different randomized MAC address when sending pre-association frames and each time it visits a network (associates with an ESS)
  Helps avoid long-term tracking of devices by third-party passive observers
However, various other information can be derived from 802.11 transmissions that can also impact user privacy; two broad categories [1]
  Personally Identifiable Information (PII)
  Personally Correlated Information (PCI)
User privacy concerns can exist whenever the user has not explicitly “opted-in” to (explicitly or implicitly) sharing of PII or PCI
  The user cannot control sharing of PII and PCI if it is unprotected (or unprotectable)
    For MAC layer and above, this means PII/PCI sent in the clear, or decryptable by an unauthenticated peer
This contribution highlights examples of such PII and PCI, use cases in which they impact user privacy, and potential solution space

## Slide 4: User privacy concerns
Reveal explicit personal information
  real name, account name, etc
User / device tracking
  using explicit identifiers of user or user’s device – e.g. device identifier, (non-personal) account identifier, etc
  using implicit / correlated data (fingerprinting) – e.g. distinguishable / unusual characteristics of the device’s transmissions (MAC, PHY and RF)
Reveal user’s activities
  (types of) applications/services being discovered and used
  physical user interactions with device (e.g. keyboard entry)
Note: Use of PCI for user/device identification is not only theoretical and (with some irony!) is being proposed as a network management solution to mitigate MAC randomization e,g. [2]

## Slide 5: Examples of PII and PCI in 802.11 stack
MAC and above
  data plane payload (if unprotected, e.g. non-RSN, EAPoL): (older) TLS exchanges, DNS queries, service discovery messages, IP headers, IP data without higher layer protection, etc
  specific explicit or implicit identifiers of user, device or (small) device group: SAE password identifier, PMKID, SSID, MAC/BSSID, etc
  identifiable MAC signaling behavior of device: (unusual) capability indication in elements/fields, PM indication behavior patterns, etc (e.g. [3], [10], [15], [16])
  identifiable MAC channel access behavior of device: (SoftAP) beacon frame timing, IFS timing, probing behavior, data stream aggregation characteristics (e.g. [4], [5], [12], [13], [14], [17])
  identifiable response to non-standard or malformed frames (e.g. [11])
  identifiable traffic characteristics of application/service types: TID/UP, data frame burst timing etc
PHY
  identifiable PHY behavior of device: scrambler seed correlation, etc (e.g. 3.1 of [4])
  channel perturbation information that might reveal physical user activity (e.g. keystrokes [6], human movement): CSI in sounding feedback, etc
RF
  identifiable RF characteristics of device: CFO, sync and subcarrier phase correlation, etc (e.g. [7])

## Slide 6: Gaps to be addressed
Some items on previous slide do not need new standards work, e.g.
  RSN provides authenticated encryption of payloads of data frames, robust unicast mgmt frames
    sufficient protection against divulgence to third parties, assuming authentication credentials are secret
      separate discussion might be needed for control of PII/PCI sharing with the (authenticated) AP/network
  minimization of distinguishable RF/PHY/MAC behaviors can be handled in device implementation, without interoperability concerns
    e.g. scheduling behavior (e.g. RUs), scrambler seed, frame tx timing, response to non-standard frames
Many of the remaining items could be addressed by PII/PCI encryption/masking, or avoidance of PII/PCI transmission, in:
  pre-association (and other non-robust or broadcast) management frame payloads [also see [18])
  control frame payloads
  data frames prior to PTKSA establishment (e.g. EAPoL)
  PHY/MAC headers of all frames
Define an extensible framework for progressive privacy enhancements
  Identify and prioritize the most feasible attack vectors; noting that in reality not every theoretical vector can be effectively addressed
    Note: In the degenerate case of a single user living in an isolated location, monitoring the presence of *any* energy in any communications band is a strong indicator of the presence of that user!

## Slide 7: Progressive protection/avoidance of PII/PCI
Step 1: Encrypt/mask frames sent prior to PTK establishment
  Capabilities, methods and configurations (Assoc, Auth and GAS frames, also probes)
    Fingerprinting device or device type (e.g. Cap field values, presence/values of elements, etc)
  SAE password identifier (Authentication frames)
    Static identifier of user/device, might also contain explicit personal info (e.g. real name)
  PMKID (Association frames, also 4-way etc)
    Medium-term identifier of a device (possibly static across BSS transitions)
  SSID (Association frames, also SoftAP Beacons/Probes) [also correlated to Address fields via Beacons/Probes]
    Static identifier of (small) group of devices (STAs), or a single device (SoftAP)
Step 2: Encrypt/mask MAC header identifiers, and frames sent after PTK establishment
  Address fields (e.g. more frequent MAC and BSSID randomization, SA/DA masking)
    Short-term (with MAC randomization) identifier of device
  OMN, quiet, timing measurement, etc (non-robust mgmt frames)
    Fingerprint device or device type
  Sequence numbers (BlockAck control frames, etc)
    Correlated values as identifier of device
Step 3: Encrypt/mask frames implicating PHY layer, other relevant PHY/MAC headers
  Beamforming report action frames
    (High SNR) CSI that reveals keystrokes or other user activity (without need for attacker to directly measure perturbed channel)
  Control fields (e.g. power save)
    Fingerprinting device or device type, identifying application/services by traffic ID/tags
  Preamble (e.g. protected LTFs)

## Slide 8: Potential solutions
Encryption/masking of pre-association management frame contents
  Scalable encryption mechanisms for unicast frames (e.g. public key based [8] [9], use of PASN keys when available)
    Note: May be difficult to fully mitigate active privacy attacks (MiTM, evil-twin, downgrade) prior to establishment of initial trust with AP/network
  Use of protected identifiers or pseudonyms (for frames that do not have other payload that needs protection)
  Also, omit non-essential information in broadcast frames (e.g. probe requests)
    Interop with legacy devices needs to be considered
    Special consideration may be needed for SoftAP (e.g. SSID masking, protected out-of-band discovery)
Encryption/masking of non-robust management frame contents
  Define robust variants (possibly limited to new PHY/MAC, e.g. 11be)
Encryption/masking of control frame contents
  Define protected control frames (or protected mgmt frame variants of control frames)
PII/PCI avoidance in PHY/MAC headers
  Difficult to address by encryption/masking in general case. Partly address by avoiding transmitting PII/PCI by enabling more dynamic address field randomization, masking etc

## Slide 9: Summary
Framework is proposed to support progressive privacy protection enhancements in 802.11 standard
  note: the proposed steps do not need to be strictly serialized
Work is justified by strong industry interest in client privacy
  significant activities in security research community (e.g. see references)
  recent introduction of privacy features in many Wi-Fi products
As a next step, prepare slides to add to 11-21-0641 with corresponding use case descriptions

## Slide 10: References
[1] 11-20-0940-00-0rcm-introduction-to-p802e
[2] https://levl.tech/products/
[3] https://www.ieee802.org/1/files/public/docs2017/802E-henry-private-threat-analysis-0115-v01.pdf
[4] https://www.hindawi.com/journals/scn/2017/6235484/
[5] https://www.blackhat.com/presentations/bh-usa-08/Bratus/BH_US_08_Bratus_Peebles_Cornelius_Hansen_Active_802.11_fingerprinting.pdf
[6] https://dl.acm.org/doi/10.1145/2976749.2978397
[7] https://arxiv.org/pdf/2011.12644.pdf
[8] 11-19-0489-00-000m-client-privacy-discussion-cid-2689
[9] 11-20-0746-00-000m-identifier-privacy-mechanism
[10] https://papers.mathyvanhoef.com/asiaccs2016.pdf
[11] https://www.cs.dartmouth.edu/~dfk/research/bratus-fingerprint/bratus-fingerprint.pdf
[12] https://www2.seas.gwu.edu/~cheng/6547/Readings/p46-desmond.pdf
[13] https://cs.gmu.edu/~mccoy/papers/wireless-fingerprinting.pdf
[14] https://ieeexplore.ieee.org/document/5544294
[15] https://www.researchgate.net/publication/317159974_Noncooperative_80211_MAC_Layer_Fingerprinting_and_Tracking_of_Mobile_Devices
[16] https://tel.archives-ouvertes.fr/tel-01921596/document
[17] http://www.uninformed.org/?v=5&a=1
[18] 11-21-1060-01-00bi-element-fingerprint-issue