## Slide 1: A framework for (E)DMG multi/bistatic radar
Date: 2021-06-10
Authors:

## Slide 2: Abstract
The following document discusses a framework for the PHY and lower MAC of a bistatic/multi-static radar/sensing in DMG and EDMG. It assumes a single Tx/Rx chain per STA.
Waveforms are not discussed in this document

## Slide 3: What is the difference between (E)DMG sensing and <7GHz sensing
DMG sensing is directional
  To achieve a range larger than a ~1m, under limitation of regulation, power, technology and price, an antenna array should be used in the transmitter and receiver.
    Many E/DMG devices use array to solve similar problems in communications.
    Control over the direction of transmission/reception is done using analog control (number of Rx/Tx chains is much lower than number of antennas)
  Many Use cases/applications benefit from the ability to separate targets at different places

## Slide 4: What are the results of using directional transmission in (E)DMG radar/sensing
When a transmission is directed towards a target, the LOS path towards the receiving STA may be highly attenuated by the transmit antenna pattern

## Slide 5: What are the advantages/disadvantages of directional Tx/Rx
Advantages
  Ability to achieve desired range/SNR.
  Ability to spatially separate targets
Disadvantages –
  to cover a larger area, both Rx and Tx need to scan (transmit in many directions) – transmit time increases.
  A transmission that is directed towards a target, may be highly attenuated at the receiving STA, due to transmit antenna pattern attenuating the path to the RX
    In order for the receiver to have the same time base as the transmitter, synchronization sequences need to be sent to the receiver.

## Slide 6: What do we need for DMG bi/multi-static radar/sensing
For an initiating transmitter:
  The ability to transmit a waveform in many direction
  The ability to transmit a waveform in the direction of the receiver that will be used for synchronization – synchronization accuracy should be in the order of 1ns – every 1ns error generates ~15cm error in range.
For the receiver –
  to synchronize to the TX time-base
  measure reflection in many directions
  Provide feedback
    CSI
    Target List

## Slide 7: What do we need from DMG bi/multi-static radar/sensing (cont.)
For an initiating receiver
  The ability to request transmission of a waveform in many directions
  The ability to receive transmissions and synchronization sequences
For the responding transmitter
  The ability to send waveforms in the many directions and synchronization waveforms in the direction of the receiver

## Slide 8: What we have today – initiating transmitter
In EDMG we have a BRP frame with TRN-R-T field
  The transmitter may transmit the TRN subfields in many directions and the receiver may receive in many directions
  The preamble and data fields, and periodically repeating fields within the TRN field are transmitted in the direction of the RX STA
CSI is optionally included in the BRP response.

## Slide 9: What we have today – initiating receiver
In (E)DMG, there is no option to request the other STA to perform transmit training.
  It is very easy to add the option to request either TX training or TX-RX training to the existing BRP frame
The TX STA may switch TX direction while transmitting the TRN field and the RX STA may switch RX directions while receiving the TRN field
  synchronization fields provided by periodic TNR subfields using the same antenna pattern as the one used for the preamble and data fields.

## Slide 10: What else is needed
The initiating and responding STAs need to exchange capabilities/parameters
  number of directions in Tx and Rx
  Feedback capabilities
    CSI
    Target List (Range/Az/El/Dopper, power per Target)
  information about Tx/Rx antenna patterns used (optional)
The initiating STA (TX or RX) needs to know the directions the responding STA is using in each TRN field.

## Slide 11: Multi-static radar/sensing in DMG
Multi-Static improves performance by increasing accuracy of directions estimates
Multiple devices needs to be synchronized to a single time base
Multi-static sensing is different from by bistatic because we cannot assume that the preamble/data part of a PPDU sent to one STA is received by another STA.

## Slide 12: Multi-Static Sensing – Transmitting initiator
Measurement setups are needed to prepare the RX STAs to the measurement assign the sync fields, and to schedule the sync and TRN field
The sensing PPDU preamble header and data field are received only by some of the RX STAs.
The sync#n fields are STAs specific, they set the time base of the TRN fields
  The sync#n are different per STA
Feedback may be polled as in EDMG MU MIMO procedure.

## Slide 13: Multi-Static sensing – Receiving Initiator
Measurement setup are needed to prepare the TX STAs to the measurement and to assign and schedule the sync fields
Each sync field triggers a different STAs
  Different sync fields used for different STAs
No need for feedback.

## Slide 14: Rx Initiator vs Tx Initiator
For an example of 16 Antenna patterns at both the initiator and responder
  The TRN field (TRN-P=2 TRN-M=16) is 125.6usec long
  The feedback, (channel measurement element, 64 taps, 16bits per tap, EDMG-MCS-12) – ~85usec
Since Rx Initiator does not require feedback, and the length of the TRN field is the same in both cases, in BI-static sensing RX initiator is more efficient.
In Multi-static sensing, the TRN-Field is repeated per STA and the feedback is repeated per STA
  since the TRN field is longer, Tx initiator is more efficient
Are both still needed – Yes
  There are devices which have different size Rx and Tx arrays.

## Slide 15: multi BI-static vs Multi-Static
For Rx initiator multi BI-static is comparable to multi-static (as long as one STA transmit at a time).
For Tx initiator the advantage is that the TRN field is transmitted only once – multi-static is much shorter, even given the overhead.

## Slide 16: Summary
We showed that EDMG bi-static radar/sensing can be achieved by reusing EDMG PPDU structures and frames with minor changes.
Multi-static sensing requires more changes and may be more efficient in some cases.

## Slide 17: References