## Slide 1: Requirements for Sensing Transmitters
Date: 2021-11-01
Authors:

## Slide 2: Abstract
Requirements for sensing transmitters in CSI-based WLAN sensing are discussed.

## Slide 3: Introduction
It is agreed that CSI (that is, the channel measured during the training symbols of a received PPDU) is a type of sensing measurement result for sub-7 GHz WLAN sensing.
For a wide range of WLAN sensing applications, measuring and monitoring CSI variation over time are essential.
A time series of CSI measurements captures how wireless signals travel through surrounding objects and humans in the time, frequency, and spatial domains.
  For example, CSI amplitude variations in the time domain have different patterns for different humans, activities, gestures, etc., which can be used for human presence detection, motion detection, activity recognition, gesture recognition, and human identification/authentication.

## Slide 4: Introduction (cont’d)
To measure a single snapshot of CSI, a sensing transmitter needs to transmit a sounding PPDU (e.g., an NDP) to a sensing receiver.
To obtain a time series of CSI measurements, the sensing transmitter is required to transmit multiple sounding PPDUs to the sensing receiver at various time instants.
CSI-based WLAN sensing can be impacted by dynamic changes in sensing transmitter configurations (e.g. transmit power and transmit beamforming).
  It can become challenging to distinguish between CSI variations caused by the activities of a sensing target and caused by changes to transmitter configurations.
In contribution 11-20-1851-03-00bf-Overview-of-Wi-Fi-sensing-protocol, it was suggested: “PHY configuration freeze/hold – PPDUs used for measurement shall be transmitted with same set of transmit parameters”.

## Slide 5: Transmit Beamforming
WLAN transmitters may use beamforming which changes the amplitude and phase of CSI measurements.
This completely changes CSI patterns and makes CSI-based sensing significantly more challenging since the beamforming matrix may not be available at the sensing receiver.
In the r0 version of this document, we suggested the following:
  If transmit beamforming is used by the sensing transmitter, then its steering matrix shall be kept unchanged during the process of transmitting consecutive sounding PPDUs to the sensing receiver.
Based on online comments and offline discussion, we now propose that, for a sounding NDP, no beamforming steering matrix is applied to the waveform.
  This is similar to the 11az requirement for ranging NDPs.

## Slide 6: Transmit Power
It is desirable to avoid CSI fluctuation caused by changes to transmit power at a sensing transmitter.
11az specifies a transmit power control mechanism to deal with the near-far problem in UL MU transmission of ranging NDP.
  The mechanism makes it difficult to keep transmit power constant.
In this document, we intend to identify the sensing measurement scenarios which do not suffer from the near-far problem. We propose that for these scenarios, the transmit power of the sensing transmitter shall be constant over time.

## Slide 7: Non-Trigger based Sensing Measurement
Document 11-21-1433-01-00bf-Non-TB-sensing-measurement discusses the non-TB sensing measurement instance with a non-AP STA as the initiator.
  For this instance, the transmit power of the sensing transmitter shall be fixed.
This document discusses the non-TB sensing measurement instance with an AP as the initiator.
  The AP-centric use of non-TB protocol works well for (single) home AP with (mostly) associated clients, since the AP knows when the STAs will be available.
  It gives the AP all the control on scheduling, which removes the need to negotiate/communicate that part with the STAs, and can be done quite dynamically (e.g., as soon as any CSI change is detected, the AP can perform measurements with all STAs in short order). This is a big advantage over the TB protocol.
  This can well support the STA based proxy approach (presented in Document 11-21-1692).
  It can be naturally combined with TWT for periodic schedule and power saving.

## Slide 8: Non-TB Sensing Measurement Instance for UL Sounding
This instance can be highly efficient when combined with TWT (shown in the figure below).
It is the most power-saving measurement instance for a non-AP STA!
  Minimized wake time
  Minimum processing required
Highly attractive feature for battery-powered WLAN sensing devices
doze
TWT Response
TWT
Request
TWT wake interval
NDP
NDP
AP
STA
doze
TWT SP
TWT SP

## Slide 9: Non-TB Sensing Measurement Instance for DL Sounding
In general, the AP knows the availability of its associated STAs.
Once the AP obtains a TXOP, it initiates a non-TB sensing measurement instance by transmitting an NDPA frame to the non-AP STA followed by an Initiator-to-Responder (I2R) NDP SIFS after.
I2R
NDP
AP
STA
measurement feedback
SIFS
Sensing NDPA
SIFS

## Slide 10: Non-TB Sensing Measurement Instance for Bidirectional Sounding
Once the AP obtains a TXOP, it shall initiate a non-TB sensing measurement instance by transmitting an NDPA frame to the non-AP STA followed by an Initiator-to-Responder (I2R) NDP SIFS after. SIFS after the I2R NDP, the non-AP STA shall transmit a Responder-to-Initiator (R2I) NDP to the AP.
This instance may serve as the basis for a unified flow to cover the aforementioned two scenarios:
  If the AP is only the sensing transmitter, then the R2I NDP is a “dummy” DNP and should be transmitted with minimum possible length with one LTF symbol.
  If the AP is only the sensing receiver, then the I2R NDP is a “dummy” DNP and should be transmitted with minimum possible length with one LTF symbol.
I2R
NDP
AP
STA
R2I
NDP
SIFS
Sensing NDPA
SIFS
measurement feedback
SIFS

## Slide 11: Trigger-based Sensing Measurement Instance
In TB sensing measurement, if only one AP and one non-AP STA participate, then there is no MU near-far problem and hence the transmit power of the sensing transmitter can be fixed.
A use case:
An AP and multiple non-AP STAs participate in a sensing session where infrequent sensing measurements is adequate. The AP can schedule TB sensing measurements with the STAs sequentially so that only one STA is involved in each measurement instance, which allows constant transmit power for each sensing transmitter.

## Slide 12: Summary
CSI fluctuation caused by changes to transmitter configurations can degrade WLAN sensing performance.
To avoid this performance degradation, requirements for transmit beamforming and transmit power at a sensing transmitter are discussed.
  No beamforming is applied to sensing NDPs.
  For non-TB sensing measurement (either with an AP as the initiator or with a non-AP STA as the initiator), the transmit power of the sensing transmitter shall be fixed.
  For TB sensing measurement with only one AP and one non-AP STA involved, the transmit power of the sensing transmitter shall be fixed.
The transmit power issue for the more general MU TB sensing measurement will be addressed in a future contribution.

## Slide 13: SP1
Do you agree with the following?
  The NDP in 11bf shall have the following property: no beamforming steering matrix is applied to the waveform.

## Slide 14: SP2
Do you agree with the following?
  11bf shall define the following non-trigger based (non-TB) sensing measurement instances with one AP being the sensing initiator and one non-AP STA being the sensing responder:
    The AP is only the sensing receiver;
    The AP is only the sensing transmitter;
    The AP is both the sensing transmitter and the sensing receiver.
  Whether the three instances are defined individually or in a unified flow is TBD.

## Slide 15: SP3
Do you agree with the following?
  For non-TB sensing measurement (either with an AP as the initiator or with a non-AP STA as the initiator), the MAC sublayer of the sensing transmitter shall not change the TXPWR_LEVEL_INDEX parameter of the TXVECTOR when transmitting multiple sounding NDPs to the sensing receiver during a sensing session.

## Slide 16: SP4
Do you agree with the following?
  If only one-AP and one non-AP STA participate in TB sensing measurement, then the MAC sublayer of the sensing transmitter shall not change the TXPWR_LEVEL_INDEX parameter of the TXVECTOR when transmitting multiple sounding NDPs to the sensing receiver during a sensing session.